## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Qualitative Use-Case Evaluation]
Date Submitted: [11. Sept, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document presents the first version of the qualitative use-case evaluation]
Purpose: [Prensentation in IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Qualitative Use-Case Evaluation
Joerg Robert (FAU Erlangen-Nuernberg)

## Slide 3: General Evaluation Procedure
Suitability
  Analysis the general suitability of a candidate technology
Qualitative Evaluation
  Analysis pros and cons, and dependency on other technologies
Quantitative Evaluation
  Exact performance (only for selected technologies)
This document

## Slide 4: Motivation
Analyze the remaining use-cases
  Derive a set of combined technology options that are able to cover the requirements according to the suitability evaluation documents in an optimal way
  Figure out whether existing IEEE standards offer the combined technology options
Analyze the communalities between the reaming uncovered use-cases

## Slide 5: Remaining Use-Cases with Potential for a new LPWAN Standard
Domain | Use-Case
Agriculture and Environmental | 
Consumer/Medical | Pet Tracking
Industrial | Industrial Plant Condition Monitoring
Infrastructure | Pipeline Monitoring – Terrestrial, Smart Grid - Fault Monitoring, Smart Grid - Load Control, Smart Metering, Structural Health Monitoring
Logistics | Global Tracking, Fast Asset Tracking
Smart Building | 
Smart City | Public Lighting, Smart Parking, Vending Machines – general, Vending Machines - Point of Sale, Waste Management

## Slide 6: Industrial Plant Condition Monitoring
Monitoring of large industrial plants (e.g. oil refinery/platform) using distributed sensor-nodes, use of licensed frequency bands

## Slide 7: Industrial Plant Condition Monitoring
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | None
Active Interfering Users | Medium
Communication Mode | Uplink/Broadcast Downlink
Data Period | Occasionally 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <10s
LP-WAN Localization Precision | <10m
Typical Power Supply | Energy Harvesting
Frequency Regulation | NA
Cell Radius | <50km
Data Security | Layer-3

## Slide 8: Industrial Plant Condition Monitoring
Modulation:
  Precise localization requires broadband signals
  No interference (licensed spectrum) and low number of users
   Spreading modulation
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  Convolutional code
MAC:
  Low number of users
  Latency < 10s
   Fully synchronized network / extended star / multi-hop

## Slide 9: Industrial Plant Condition Monitoring
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Medium number of active users
  Latency < 10s
  Fully synchronized network / extended star / multi-hop
The optimum parameter configuration exactly matches the existing IEEE 802.15.4 standard. Therefore, a new LPWAN standard would not offer significant benefits.

## Slide 10: Pipeline Monitoring – Terrestrial
Channel Model | Parameter
Channel Model | Outdoor Rural
Interference Model | None
Active Interfering Users | Low
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | Energy Harvesting
Frequency Regulation | NA
Cell Radius | <50km
Data Security | Layer-2

## Slide 11: Pipeline Monitoring – Terrestrial
Modulation:
  Precise localization requires broadband signal
  No interference (licensed spectrum) and low number of users
   spreading modulation
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Low number of users
  Latency < 10s
   Fully synchronized network

## Slide 12: Pipeline Monitoring – Terrestrial
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Low number of active users
  Latency < 1min
  Extended star or mesh
The optimum parameter configuration exactly matches the existing IEEE 802.15.4 standard. Therefore, a new LPWAN standard does not offer significant benefits.

## Slide 13: Fault Monitoring in the Medium Voltage Distribution Network
Use-case description: Detection and indication of faults in the medium voltage distribution network.
Assumptions
  No suitable 110/220V power supply to power the sensor node  powered by battery
  Devices only transmit in case of error or one alive message per day  low traffic
  Only uplink data, no downlink required
  But, in case of a major network failure many devices may report an error at the same time  dense traffic
  System may be operated in populated areas  strong interference
  The distance between different sensor nodes may be multiple km

## Slide 14: Fault Monitoring in the Medium Voltage Distribution Network
The large spacing between different measurement nodes requires low payload bit-rates
Measurement locations may be separated by multiple km

## Slide 15: Fault Monitoring in the Medium Voltage Distribution Network
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <50km
Data Security | Layer-2

## Slide 16: Fault Monitoring in the Medium Voltage Distribution Network
Modulation: The
  Localization precision <100m
  Strong interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  Convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work due to pure uplink mode

## Slide 17: Fault Monitoring in the Medium Voltage Distribution Network
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  High number of active users with interference
  Latency < 1min
  Extended star (e.g. with mesh backhaul)
Potential use-case for new LPWAN standard

## Slide 18: Smart Grid - Load Control
Control of the load of the smart grid with focus on private homes. May also be combined with smart electricity meters.
Assumptions:
  External power supply available
  High interference and density as used in highly populated areas
  Significant amount of payload data also on the downlink, also software updates

## Slide 19: Smart Grid - Load Control
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | None
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1s
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | NA
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 20: Smart Grid - Load Control
Existing systems are already on the market (e.g. based on IEEE 802.15.4g)
These systems employ mesh structures with antennas that are typically not highly exposed even dense cell traffic can be handled efficiently
The mesh structure also allow for significant downlink bit-rates that would not be possible in
However, LPWAN may be used to connect remote houses (last mile) that may currently not be well covered by mesh structures

## Slide 21: Smart Grid - Load Control with LPWAN Extension
Mesh Network (e.g. 802.15.4g)
for normal users
Remote User
Long-Range LPWAN Link

## Slide 22: Smart Grid - Load Control: LPWAN Extension Part
Modulation:
  Long-range transmission with potential interference
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  Convolutional code
MAC:
  Low number of users
  Uplink and downlink
  Latency < 1s
   Fully synchronized network

## Slide 23: Smart Grid - Load Control with LPWAN Extension
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Low number of active users
  Latency < 1min
  Point to point for last mile
Potential LPWAN use-case to extend mesh network to remote users

## Slide 24: Smart Metering (Water / Gas)
Gas and water meters are equipped with LPWAN
No power supply available, data transmission required only once per day, backhaul network can also be mesh
Mesh
LPWAN

## Slide 25: Smart Metering (Water / Gas)
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Broadcast Downlink
Data Period | Periodically 1/day
Data Length (Uplink) | <=16bytes
Availability | Medium
Latency | <1day
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | End-to-end

## Slide 26: Smart Metering (Water / Gas)
Modulation:
  Localization not required an high interference
  High interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  Convolutional code
MAC:
  Very high number of users, strong interference
  Uplink and broadcast downlink
  Latency < 1day
   ALOHA network

## Slide 27: Smart Metering (Water / Gas)
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1day
  Star or extended star (e.g. based on mesh network)
Potential for new LPWAN standard also for increasing the range of mesh networks

## Slide 28: Structural Health Monitoring
Monitoring of the structural health of bridges, etc.
Stations may be separated by multiple km
5km
5km
LPWAN

## Slide 29: Structural Health Monitoring
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2

## Slide 30: Structural Health Monitoring
Modulation:
  Localization not required an high interference
  High interference and many users
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Very high number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 31: Structural Health Monitoring
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1min
  Pure mesh not useful due to low traffic per sensor node
  Star or extended star
Potential for new LPWAN standard

## Slide 32: Logistics: Global Tracking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Periodically 1/hour
Data Length (Uplink) | <=16bytes
Availability | Best effort
Latency | <10min
LP-WAN Localization Precision | <100m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-3

## Slide 33: Logistics: Global Tracking
Modulation:
  High interference and many users
  Localization < 100m
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  Very high number of users, strong interference
  Uplink only
  Latency < 10min
   Only ALOHA may work

## Slide 34: Logistics: Global Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 10min
  Extended star (e.g. with mesh backhaul)
The optimum parameter configuration exactly matches the existing IEEE 802.15.4 standard. Therefore, a new LPWAN standard does not offer significant benefits.

## Slide 35: Logistics: Fast Asset Tracking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | High
Communication Mode | Uplink
Data Period | more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1 min
LP-WAN Localization Precision | <10m
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2

## Slide 36: Logistics: Fast Asset Tracking
Modulation:
  High interference and many users
  Localization < 10m
   Spreading modulation, but only if many base stations are used
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 37: Logistics: Fast Asset Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Precise localization
  Latency < 1min
  Extended star (e.g. with mesh backhaul)
The optimum parameter configuration exactly matches the existing IEEE 802.15.4 standard. Therefore, a new LPWAN standard does not offer significant benefits.

## Slide 38: Smart City: Public Lighting
Switch on and off of public street lights
Short distance between street lights
Significant downlink communication

## Slide 39: Smart City: Public Lighting
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally 1/hour
Data Length (Uplink) | <=16bytes
Availability | Medium
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 40: Smart City: Public Lighting
The system requirements are perfectly met by existing standards (e.g. IEEE 802.15.4g) that are already in commercial use
A new LPWAN standard would not provide benefits and may not work due to the required downlink traffic

## Slide 41: Smart City: Smart Parking
Parking spaces along the street that are spread over large areas

## Slide 42: Smart City: Smart Parking
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | <=16bytes
Availability | High
Latency | <1min
LP-WAN Localization Precision | Not required
Typical Power Supply | 2xAA
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-2

## Slide 43: Smart City: Smart Parking
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  Convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1min
   Only ALOHA may work

## Slide 44: Smart City: Smart Parking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Different sensor nodes may be highly separated
  Latency < 1min
  Star or extended star (e.g with mesh as backhaul)
Potential for new LPWAN standard

## Slide 45: Smart City: Vending Machines – general
Vending machines indicate whether the are running out of products
Distance between vending machines may be several km

## Slide 46: Smart City: Vending Machines – general
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=64bytes
Availability | Medium
Latency | <60min
LP-WAN Localization Precision | Not required
Typical Power Supply | Energy Harvesting
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-3

## Slide 47: Smart City: Vending Machines – general
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 64 bytes
  Convolutional code or Turbo or Polar codes
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1h
   Only ALOHA may work

## Slide 48: Smart City: Vending Machines – general
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Machines may be placed in high distance
  Latency < 60min
  Star or extended star (e.g. with mesh backhaul)
Potential for new LPWAN standard

## Slide 49: Smart City: Vending Machines - Point of Sale
Secure authorization (e.g. credit card) for vending machines

## Slide 50: Smart City: Vending Machines - Point of Sale
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Occasionally, more than 1/hour
Data Length (Uplink) | >256bytes
Availability | High
Latency | <10s
LP-WAN Localization Precision | Not required
Typical Power Supply | External
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Secure Authentication

## Slide 51: Smart City: Vending Machines - Point of Sale
A significant amount of downlink traffic is required (e.g. certificates, etc.), which cannot be delivered by LPWAN systems in the license exempt frequency bands
 No use-case for LPWAN

## Slide 52: Smart City: Waste Management
Trash cans transmit their whether they have to be emptied
Use case very similar to water/gas metering

## Slide 53: Smart City: Waste Management
Channel Model | Parameter
Channel Model | Outdoor Urban
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink
Data Period | Occasionally 1/day
Data Length (Uplink) | <=16bytes
Availability | Best effort
Latency | <60min
LP-WAN Localization Precision | Not required
Typical Power Supply | Energy Harvesting
Frequency Regulation | ETSI/FCC
Cell Radius | <10km
Data Security | Layer-2

## Slide 54: Smart City: Waste Management
Modulation:
  High interference and many users
  Localization not required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 16 bytes
  convolutional code
MAC:
  High number of users, strong interference
  Uplink only
  Latency < 1h
   Only ALOHA may work

## Slide 55: Smart City: Waste Management
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Low amount of packets not the first option for mesh
  Latency < 60min
  Star or extended star (e.g. with mesh backhaul)
Potential for new LPWAN standard

## Slide 56: Consumer/Medial: Pet Tracking
Localization of cat in the neighborhood

## Slide 57: Consumer/Medial: Pet Tracking
Channel Model | Parameter
Interference Model | Dense
Active Interfering Users | Very high
Communication Mode | Uplink/Downlink
Data Period | Periodically, more than 1/hour
Data Length (Uplink) | <=64bytes
Availability | Best effort
Latency | <1min
LP-WAN Localization Precision | <100m
Typical Power Supply | CR2025
Frequency Regulation | ETSI/FCC
Cell Radius | <5km
Data Security | Layer-2
Node Velocity | 3km/h

## Slide 58: Consumer/Medial: Pet Tracking
Modulation:
  High interference and many users
  Localization <100m required
   FHSS
Coding:
  Long distance requires good coding
  Data length <= 64 bytes
  Convolutional code or Turbo or Polar code
MAC:
  High number of users, strong interference
  Uplink only/downlink
  Latency < 1min
   Fully synchronized

## Slide 59: Consumer/Medial: Pet Tracking
Connectivity
  Use of IPv6 with header compression or transparent
Network topology
  Very high number of active users and dense interference
  Latency < 1min
  LPWAN localization would require multiple distributed base-stations  not useful for personal use  GPS tracking
  Star topology
Potential use-case for LPWAN if GPS localization is used

## Slide 60: Potentially Relevant Use-Cases
Domain | Use-Cases
Agriculture and Environmental | 
Consumer/Medical | Pet Tracking
Industrial | 
Infrastructure | Smart Grid - Fault Monitoring, Smart Grid - Load Control with LPWAN Extension, Smart Metering, Structural Health Monitoring
Logistics | 
Smart Building | 
Smart City | Smart Parking, Vending Machines – general, Waste Management

## Slide 61: Communalities of Uncovered Use-Cases
Communalities:
  Mainly focusing on uplink communication with highly limited downlink traffic
  Require large cells
  Are operated outdoors
  Have to support many users
  Suffer from interference
  Typically require LPWAN localization < 100m
  Require data length <= 16 bytes
  Have a latency requirement <1min
LPWAN is highly interesting to offer connectivity to remote users

## Slide 62: Thank You for Your Interest!