## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [L2R error on non-storing mode]
Date Submitted: [11 September 2017]
Source: [Noriyuki Sato, Kiyoshi Fukui] Company [Oki Electric Industry Co., Ltd.]
Address [2-6-8, Bingo-machi, Chuo-ku, Osaka, Japan]
Voice:[+81-6-6260-0700], E-Mail:[sato652@oki.com]
Re: [L2R error on non-storing mode]
Abstract: [Explaining the omission on L2R non-storing mode process and giving a solution to fix]
Purpose: [To explain an issue]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Non-storing mode in IEEE802.15.10 has an error from the inconsistency.
  Primitives are designed for the NHL to manage downward routing record
  E2E Acknowledgement from the mesh root needs attach source routing address list, which is assumed to be attached by L2R layer automatically.
  In P2P routing using combination of up/down route, the mesh root needs to attach source routing list. It is assumed that L2R layer attach the list automatically.
  In on-demand P2P routing with non-storing mode has similar issue on E2E Ack and Path storing to send a unicast.
Two options to solve
  Add an address record for the source routing (Much easier)
  To let the NHL operate E2E ack and P2P routing, add new scheme and primitives (Complex)

## Slide 3: An issue on P2P (Up + Down)
MAC
S
D
A
B
R
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.ind doesn’t issue a data frame
From S to D
DATA.req from R cannot send a frame as if S is source. It just a send a frame from R to D.
S
..hops..
R
D
NHL
Solution A: Let L2R has a record of path. Put a note saying that the record is attached when a data is sent.
Solution B: Add a new primitive to indicate the event (up to down) and add a new primitive to send a frame so that it keeps its source address as the originator not mesh root.
..hops..

## Slide 4: An issue on E2E Ack
MAC
S
D
A
B
R
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.req from R cannot send a L2R Ack frame
S
..hops..
R
S
NHL
Solution A: Let L2R has a record of path. Put a note saying that the record is attached when a data is sent.
Solution B: Add a new parameter to indicate L2R ack request to the DATA.indication primitive to and add a new primitive to send a frame so that it keeps its source address as the originator not mesh root.
..hops..
Sending Acknowledgment should be done within that layer (e.g. handling timeout)