## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [L2R error on non-storing mode]
Date Submitted: [15 January 2018]
Source: [Noriyuki Sato, Kiyoshi Fukui] Company [Oki Electric Industry Co., Ltd.], [Charlie Perkins] Company [Futurewei]
Address [2-6-8, Bingo-machi, Chuo-ku, Osaka, Japan] [2330 Central Expy, Santa Clara Ca, USA]
Voice:[+81-6-6260-0700], E-Mail:[sato652@oki.com] [charlie.perkins@huawei.com]
Re: [L2R error on non-storing mode]
Abstract: [Explaining the omission on L2R non-storing mode process and giving a solution to fix it]
Purpose: [To explain an issue and suggest a preferable solution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
Non-storing mode in IEEE802.15.10 has a serious omission.
  In non-storing mode, primitives are designed for the NHL at the mesh root to manage downward routing records
  (A) E2E Acknowledgement from the mesh root has to attach an address list for source routing, which is assumed to be done automatically by the L2R layer.
  (B) In P2P routing using up/down routes, the mesh root has to attach source routing list, which is assumed to be done automatically by the L2R layer.
Two options to solve problems A and B:
  Address lists in the MT to enable source routing (simple)
  Let the NHL operate E2E ACK and P2P routing; add a new scheme and primitives (complex)

## Slide 3: Problem: non-storing P2P (Up  Down)
MAC
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.ind can’t issue a data frame
From S to D
DATA.req from R cannot send a frame as if S is source. It just a sends a frame from R to D.
S
..hops..
R(root)
D
NHL
Solution I: Let L2R have a record of the paths. Insert text specifying that the record is attached when a data is sent.
Solution II: Add a new primitive to indicate the event (up  down) and add a new primitive to send a frame so that it keeps its source address as the originator not mesh root.
S
D
A
B
R
..hops..

## Slide 4: Problem: non-storing E2E Ack
MAC
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.req from R cannot send a L2R Ack frame
D
..hops..
R
S
NHL
Solution I: Let L2R have a record of the paths. Insert text specifying that the record is attached when a data is sent.
Solution II: Add a new parameter to the DATA.indication primitive, to indicate L2R ack request. Add another to send a frame as if its source address were the originator, not themesh root.
S
D
A
B
R
..hops..
Sending Acknowledgment should be done by L2R layer (e.g. handling timeout)

## Slide 5: Solution I details to fix issues A and B
Add an entry to the mesh table 5-1 (MT)
  Path List
    Consists of ‘Destination Address’ and ‘Address List’ pair
    Enabled only when non-storing mode
Add new specification after the following text in 5.2.4.2
  When the mesh root receives the RA IE or the SRA IE, it delivers the path and the source address therein to the next higher layer with the L2LME-INTERMEDIATE-ADDR-LIST.indication primitive, and stores them as the pair of the address list and the destination address into the ‘Path List’ in the MT.
Add to IntermediateAddrList description of L2RDATA.request (7.2.1.1):
  Addresses to be inserted in the Intermediate Address List of the L2R Routing IE. When IntermediateAddrList is ‘NULL’, the ‘Address List’ in the ‘Path List’ in the MT is used, where the destination address matches to the one in this primitive. Omitted if source routing is not used.
No format change. No change of protocol between devices S, D, R.

## Slide 6: Other editorial corrections
While discussing the solutions to the aforementioned problems, the need for some other editorial improvements has been noticed.
Should we go ahead and fix them also?