## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [L2R operation]
Date Submitted: [11 September 2017]
Source: [Noriyuki Sato, Kiyoshi Fukui] Company [Oki Electric Industry Co., Ltd.]
Address [2-6-8, Bingo-machi, Chuo-ku, Osaka, Japan]
Voice:[+81-6-6260-0700], E-Mail:[sato652@oki.com]
Re: [L2R operation]
Abstract: [Explaining L2R operations with ULI management box]
Purpose: [To discuss]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: L2R Operations
Configuration
  Device types
    PAN Coordinator, Mesh root, L2R router, End device
  Operation mode
    PAN Coordinator decides PAN type – SSPAN, Regular PAN,TMCTP
    Mesh root decides operation options
      Address mode, Non-store/Store/Adhoc-P2P/etc…
    Joining device to be configured – allowed options
      Ex. I can join to the mesh operates in either non-storing mode or storing.
  L2R PIBs
Operations
  Bootstrap procedure
    Process the procedure as configured – (Management box does?)
  Security setting
    Need a detailed procedure of KMP to set key parameters to L2R PIBs
  Interaction with higher layer (see following pages)

## Slide 3: Short address assignment
Device
L2R Router
Mesh root

## Slide 4: Short address assignment
Device
L2R Router
Mesh root
Only PAN Coordinator has short address assignment function.
If the mesh root is also PAN coordinator, it has a function to assign a short address.
If the mesh root is not PAN coordinator, mesh root play a role of proxy using PAN coordinator direct connection (PANCDC)
PANCDC
PANCDC also manages the inter mesh flooding
A mesh root forwards flooding data using PANCDC to PAN Coordinator and PAN Coordinator forwards all the mesh roots.

## Slide 5: Short address request on a joining device
PDE
MMI
L2R
15.4
Device requesting a short address
L2R
Protocols sublayer
MMI-DATA.request
IEEE802.15.4
MCPS-DATA.request
MMI
sublayer
AA-RQ IE
MMI-DATA.confirm
MCPS-DATA.confirm
AA-RQ IE
AA-RP IE
AA-RP IE
MMI-DATA.indication
MCPS-DATA.indication
L2R invokes MMI-DATA.request to invoke MCPS-DATA.request.

## Slide 6: Short address assignment on a mesh root (Option 1 – APL does)
PDE
MMI
L2R
15.4
AA
Mesh root on PAN coordinator
PDE
MMI
L2R
15.4
Alternate AA
Mesh root with PANC DC
PAN coordinator
PANC DC

## Slide 7: Short address assignment on a mesh root (Option 1)
MMI-DATA.indication
L2R
Protocols sublayer
MMI
sublayer
IEEE802.15.4
MCPS-DATA.indication
L2RLME-AA-RQ.indication
AA MGT App.
PDE-MGMT.indication
PDE
sublayer
MMI-DATA.request
MCPS-DATA.request
L2RLME-AA-RP.request
PDE-MGMT.request
AA-RQ IE
AA-RP IE
PANC DC
PDE-MGMT.confirm
L2RLME-AA-RP.confirm
MMI-DATA.confirm
MCPS-DATA.confirm

## Slide 8: Short address assignment on a mesh root (Option 2 – Management box does)
PDE
MMI
L2R
MGMT
15.4
AA
Mesh root on PAN coordinator
PDE
MMI
L2R
MGMT
15.4
PANC comm.
Mesh root with PANC DC
PAN coordinator
PANC DC
Alt. AA

## Slide 9: L2R short address assignment (Option 2)
MMI-DATA.
indication
L2R
Protocols sublayer
MMI
sublayer
IEEE802.15.4
MCPS-DATA.
indication
L2RLME-AA-RQ.indication
NHL
MMI-DATA.
request
MCPS-DATA.
request
L2RLME-AA-RP.request
MGMT-MGMT.
response
Management
Protocols sublayer
PDE
sublayer
AA-RQ IE
PDE-MGMT.
response
MGMT-MGMET.
indication
PDE-MGMT.
indication
AA-RP IE
PANC DC
NHL
PDE-MGMT.
confirm
Management
Protocols sublayer
PDE
sublayer
MGMT-MGMT.
confirm
MGMT-MGMET.
request
PDE-MGMT.
request
PANC DC
MCPS-DATA.
confirm
MMI-DATA.
confirm
L2RLME-AA-RP.confirm

## Slide 10: Short address assignment on a mesh root (Option 3 APL does & MGMT pass the messages)
PDE
MMI
L2R
MGMT
L2R
15.4
AA
Mesh root on PAN coordinator
PDE
MMI
L2R
15.4
Alternate AA
Mesh root with PANC DC
PAN coordinator
PANC DC
L2R
MGMT

## Slide 11: Short address assignment on a mesh root (Option 3)
MMI-DATA.indication
L2R
Protocols sublayer
MMI
sublayer
IEEE802.15.4
MCPS-DATA.indication
L2RLME-AA-RQ.indication
AA MGT App.
PDE-MGMT.indication
PDE
sublayer
MMI-DATA.request
MCPS-DATA.request
L2RLME-AA-RP.request
PDE-MGMT.request
AA-RQ IE
AA-RP IE
PANC DC
PDE-MGMT.confirm
L2RLME-AA-RP.confirm
MMI-DATA.confirm
MCPS-DATA.confirm
Management
Protocols sublayer
MGMTMGMT.
indication
MGMT-MGMT.
request
MGMT-MGMT.
confirm

## Slide 12: Source routing
It depends on how to fix inconsistency on source routing error in IEEE802.15.10.
  NHL manages source routing
  L2R layer manages source routing

## Slide 13: Source routing
L2R mesh root
L2R Router
DST node
APL
APL
APL
Source route
APL manages source routing. APL needs to manages the mode in which L2R operates and need to invoke L2R-DATA.request with appropriate parameters.

## Slide 14: Source routing
L2R mesh root
L2R Router
DST node
APL
APL
APL
Source route
Management Box manages source routing.
It manages mode in which L2R operates and it also manages data transmission.

## Slide 15: Source routing
L2R mesh root
L2R Router
DST node
APL
APL
APL
Source route
If the source routing is managed in L2R. APL just send a data using Data-SAP

## Slide 16: Source routing P2P communication on no-Storing mode
SRC node
L2R mesh root
DST node
APL
APL
APL
Source route
Hop by Hop routing
Source routing
APL handles source routing – Call L2R primitives directly?
Or PDE handles indication and notify to APL?
It can be that MGMT handles first and then invokes appropriate primitives

## Slide 17: Source routing P2P communication on no-Storing mode
SRC node
L2R mesh root
DST node
APL
APL
APL
Source route

## Slide 18: Source routing P2P communication on no-Storing mode
SRC node
L2R mesh root
DST node
APL
APL
APL
Source route
L2R Layer manages source routing. Nothing to do with management box or APL.