## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: DSSS SIK Modulation for Facility IoT Connected V2X CAMCOM Link
Date Submitted: November 2017
Source: Jaesang Cha (SNUST), Mariappan Vinayagam (SNUST), Minsoo Kim (SRENG Co., Ltd.), Younkwan Kim (The Catholic University of Korea), Jaekwon Shin, Jintae Kim (Fivetek Co., Ltd.)
Address: Contact Information: +82-2-970-6431, FAX: +82-2-970-6123, E-Mail: chajs@seoultech.ac.kr
Re:
Abstract: This documents introduce the DSSS SIK modulation method for VAT V2X CAMCOM Link. The proposed DSSS SIK modulation method for VAT to operate on the application services like ITS, ADAS, etc on road condition, Bio-Plant / Manufacturing Industry Safety AIDS using Lighting / Display based infrastructure. Also this can be used for IoT/IoL, LEDIT, Digital Signage with Advertisement Information etc..
Purpose: To Provided Concept models of Vehicle CamCom for VAT Interest Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Contents
V2X CAMCOM Link System
V2X CAMCOM Link Needs
DSSS SIK
Conclusion

## Slide 3: V2X CAMCOM Link System
Image Sensor based V2X Communication
  Tx - LED ; Rx - CMOS Image Sensor
  Data Rate : 10 Mb/s
  Day-Night Communication Mode
Vehicle-to-Vehicle (V2V)
CAMCOM Technology
Vehicle-to-Infrastructure (V2I)
CAMCOM Technology

## Slide 4: V2X CAMCOM Link Needs (1)
Issues Needs to be address in design
  Minimizing the effect of external noise
    Artificial or Natural
  Ambient lights effect
  Interference minimization
  Robust Modulation
Need Robust Modulation Techniques
  CamCom Link in ITS is largely affected by natural and artificial lights (noise and interference) such as Sunlight, ambient lights, road/street lights etc.
  Different Modulation used including Optical MIMO
  Adaptive Modulation Techniques for different applications
  Equalization Techniques have advantages in design

## Slide 5: V2X CAMCOM Link Needs (2)
Efficient Modulation Methods Considered
  OOK
  Multilevel PPM
  Inverted PPM
  Sub Carrier PPM
  DSSS SIK

## Slide 6: DSSS SIK (1)
Direct Sequence Spread Spectrum (DSS) Sequence Inverse-Keying (SIK)
  Spectrum spreading is accomplished before transmission through the use of a spreading code that is independent of the data sequence
  The same spreading code is used in the receiver (operating in synchronism with the transmitter) to de-spread the received signal so that the original data may be recovered.

## Slide 7: DSSS SIK (2)
"VIDAS D4.1: Modulation Schemes for outdoor visible-light communication systems" by Navin Kumar, 2010

## Slide 8: DSSS SIK (3)
DSSS uses bipolar spreading sequences that cannot be used as such in the all-positive (unipolar) optical medium
Because in optical medium there is no negative going pulses and when there is no light pulse, the signal has to be represented by zero level
Therefore, a technique called unipolar-bipolar sequencing, allows the same spreading codes of radio systems to be used in optical systems, is employed instead

## Slide 9: DSSS SIK (4)
Unipolar-bipolar sequencing, involves transmission of a unipolar spreading sequence and correlation with a bipolar version of the same spreading sequence, preserves the correlation properties of bipolar-bipolar sequencing although with the introduction of a fixed dc offset.
At the transmitter, a unipolar spreading sequence is modulated by binary data such that the sequence is transmitted for a binary „1‟ while the inverse (complement) sequence is transmitted for a binary „0‟.
This type of modulation is called as SIK. The resulting spread spectrum signal uses a rectangular NRZ chip waveform to modulate the intensity of the visible light source (LEDs).

## Slide 10: DSSS SIK (5)
Minimize the effect of interference according to the processing gain advantage
  While the additional bandwidth requirement of a spread-spectrum modulation scheme reduces the system bandwidth efficiency
the processing gain of the spread spectrum technique helps to
  Combat artificial light interference effects
  Multipath dispersion (if any) without the need for extra circuitry such as equalizers.

## Slide 11: Conclusion
Introduced the Effective Modulation method called “DSSS SIK” for V2X CAMCOM Link
V2X CAMCOM Link guarantees data communication from infrastructure-to-vehicle and vehicle-to vehicle, broadcasting many safety related information, hence suitable for road safety applications.