## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ETRI’s Proposals for Pulsed Modulation PHY
Date Submitted: 03 March 2018
Source: Sang-Kyu Lim, Il Soon Jang, Jung-Sik Sung, Tae-Gyu Kang [ETRI]
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 34129, Korea
Voice:[+82-42-860-1573], FAX: [+82-42-860-5218], E-Mail:[sklim@etri.re.kr]
Re:
Abstract: Proposals for Pulsed Modulation PHY
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
ETRI’s Proposals
for Pulsed Modulation PHY
Sang-Kyu Lim, Il Soon Jang, Jung-Sik Sung, Tae-Gyu Kang [ETRI]

## Slide 3
PPDU Format
Preamble
PHY
header
HCS
PSDU
124 to 16,444 bits
32 bits
16 bits
variable

## Slide 4
Preamble (1)
FLP (101010…..)
TDP
~ TDP
TDP
~ TDP
64 to 16,384 bits
60 bits
P1
Peer-to-Peer
P2
Star
P3
Broadcast
P4
Coordinated
P5
Relay functionality
P6
Heterogeneous RF-OWC functionality
(TDP assignments for various topologies)
* FLP : Fast Locking Pattern
* TDP : Topology Dependent Pattern

## Slide 5
Preamble (2)
We propose 15-bit Gold code as a TDP pattern because Gold codes are used in CDMA and satellite systems.
If we use Gold codes, we can get 6 sequences with good auto correlation and cross correlation properties to distinguish different topologies.
The Gold codes have DC balancing but since they are odd, they are off by one (e.g. 8 zeros and 7 ones for 15-bit Cold code).
If exact DC balance is needed, the code can be inverted and repeated.
In another aspect we need to discuss about whether TDP patterns to distinguish different topologies are necessary or not.

## Slide 6
Preamble (3)
We propose that the preamble is transmitted using OOK modulation (2-level PAM).
The preamble shall be sent at a clock rate chosen by the TX and supported by the RX.
The preamble is a time domain sequence and does not have any channel coding or line coding.
The FLP is fixed to start as a “1010…” pattern i.e., it ends with a ‘0’.

## Slide 7
Preamble (4)
The different TDP patterns are to minimize interference between different topologies and having wrong devices connect to network.
If there is no TDP pattern, all devices would connect to network and then MAC will reject it - this can cause significant contention between intended topology and non-intended topology.
If we use TDP pattern, devices with wrong TDP will not be able to attach to network.

## Slide 8
PHY Header (1)
Burst mode
MCS ID
(Modulation and Coding Scheme)
PSDU length
Reserved
8 bits
16 bits
PHY header fields
Bit-width
Burst mode
1
MCS ID
8
PSDU length
16
Reserved fields
7
1 bit
7 bits
Explanation on usage
Reduce preamble and IFS
Provide information about PHY type and data rate
Length up to aMaxPHYFrameSize
Future use

## Slide 9
PHY Header (2)
We propose that the PHY header uses OOK modulation (2-level PAM) for simplicity.
The clock rate does not change throughout the frame between the preamble, header, and payload.

## Slide 10
HCS
HCS (Header Check Sequence)
16 bits
The PHY header shall be protected with 2 octet CRC-16 HCS.
A schematic of the CRC processing used for HCS calculation is shown in Annex C.
The HCS bits shall be processed in the transmitter order.
The registers shall be initialized to all ones.

## Slide 11
PSDU
The PSDU field has a variable length and carries the data of the PHY frame.
The FCS is appended if the PSDU has non-zero byte payload.
MHR
MAC Payload
FCS
Up to aMaxPHYFrameSize

## Slide 12
Data Rates (1)
Modulation | Level | FEC RS(n,k) | Line Code | HCM | Optical Clock Rates (MHz) | Data Rates (Mbps)
PAM | 2 | (255,248) | 8B10B | (1,1) | 50 (200/22) | 38.9
 |  |  |  |  | 25 (200/23) | 19.45
 |  | (36,24) |  |  | 12.5 (200/24) | 6.67
 |  |  |  |  | 6.25 (200/25) | 3.33
 |  |  |  |  | 3.125 (200/26) | 1.67

## Slide 13
Data Rates (2)
We withdraw the modes using Manchester line code because if the different line codes are used for the PHY header and Payload, respectively, the system complexity is increased.
Especially if the Manchester line code is used only for the Payload, and so the time domain dimming is supported only for the Payload, the system complexity is increased and the system is not effective.
The optical clock rates and data rates we propose can be changed depending on the optical clock support approach.

## Slide 14
Scrambler and Interleaver
Adding a scrambler is always good to randomize the data and it avoids repetitions of data and long strings of 0’s and 1’s.
However, it’s redundant because PM PHY use 8B10B line code as a DC balanced code.
So, we propose that PM PHY does not use the scrambling.
If there is a block code based channel coding e.g. convolutional codes or turbo codes, an interleaver is useful.
However, TG13 have mainly discussed RS codes for FEC of PM PHY.
So, we propose that PM PHY does not use an interleaver.