## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PAR and CSD document discussion]
Date Submitted: [15 January, 2018]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [Document proposed draft text for SG LPWA PAR and CSD document]
Purpose: [Discussion in SG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed Scope and Need for LPWAN PAR
Joerg Robert (FAU Erlangen-Nuernberg)

## Slide 3: Motivation
Primary focus of the SG LPWA is the definition of the PAR (Project Authorization Request) and the CSD (Criteria for Standards Development) documents
Aim of this presentation is to achieve general agreement on the content of both documents

## Slide 4: Goal of New Amendment
Improvement of IEEE 802.15.4 performance in use-cases with very low payload bit-rates (e.g. typically <30kBit/s) in license-exempt frequency bands with potentially high levels of interference
No introduction of new modulation schemes, base on existing IEEE 802.15.4k FSK PHY
All modifications should be supported by existing IEEE 802.15.4 chipsets with updated software

## Slide 5: Required Amendments for Powerful LPWA Functionality
Amend current 802.15-4 revision wrt.
  FCC compliant ultra-low bit-rate modes based on 802.15.4k FSK PHY
  Fragmented transmission of FEC code-words
  Fragmentation mechanisms and channel hopping patterns
  Convolutional codes with lower rates in addition to the K=7 R=1/2 code? (would offer potentially improved gains)

## Slide 6: PAR Document
SG LPWA has to agree on “Scope” and “Need” defined in the PAR document
All other items are mainly editorial
Final PAR document will be drafted after we have agreed “Scope” and “Need”

## Slide 7: Proposed “Scope”
Focus on low bit-rates (e.g. payload bit-rate typically <30kBit/s)
Definition of mechanism for fragmented transmission of FEC code-words
Definition of time / frequency patterns for the transmission of the fragments
Minor adjustments of the MAC required for the efficient transmission of the fragments
No definition of new modulation schemes wrt. the 802.15.4k FSK PHY, addition of lower bit-rates and frequencies
Definition of additional convolutional codes based on the K=7 R=1/2 convolutional code?

## Slide 8: Proposed Text for “Need” ( I / II )
There is significant commercial interest in Low Power Wide Area Networks (LPWAN). According to recent studies, it is getting a very important solution in different areas to achieve cost-effective connectivity to billions of devices spread over large areas.
A main functional requirement for LPWAN is a high link margin. However, the use of sub-GHz license exempt frequency bands – that are typically used by LWPAN – has increased over the recent years. Additionally, the upcoming large roll-out of IEEE 802.11ah will further increase the use of this spectrum. This significantly affects the reliability of transmissions relying on a high link margin due to two main reasons: First, the high link margin allows for very low reception levels. Hence, CSMA based channel access schemes may not be able to properly detect LPWAN transmissions. Second, the low bit-rates required for a high link margin result in long on-air times, further increasing the probability to get hit by interferer. Additionally, the required on-air times of the required very low bit-rates may exceed regulatory limits defined by the FCC.

## Slide 9: Proposed Text for “Need” ( II / II )
Current standards have not been designed for a very high link margin in license-exempt frequency bands with strong interference. Thus, they cannot guarantee the required transmission reliability in such scenarios. Hence, an amendment to the existing IEEE 802.15.4 standard is needed to close this gap.

## Slide 10: CSD Document
SG LPWA has to agree on “Distinct Identity” and “Broad Market Potential”
All other items are mainly editorial
Final CSD document will be drafted after agreement on both items

## Slide 11: Distinct Identity
Each proposed IEEE 802 LMSC standard shall provide evidence of a distinct identity. Identify standards and standards projects with similar scopes and for each one describe why the proposed project is substantially different.

## Slide 12: Proposed Text for “Distinct Identity”
The LPWAN market is rapidly growing. Suitable standards have to support very high link margins in license-exempt frequency bands with high interference.
Analyses have shown that only IEEE 802.15.4 in addition to very low bit-rates is able to achieve the required link margins.
However, further analyses indicate that the performance in case of highly occupied license-exempt frequency bands is significantly reduced, as the existing IEEE 802.15.4 standard has not been designed for such channels.
Consequently, the transmission reliability in license-exempt frequency bands can be highly improved by means of an amendment to IEEE 802.15.4 that is focusing on the very challenging LPWAN environment.

## Slide 13: Broad Market Potential
Each proposed IEEE 802 LMSC standard shall have broad market potential. At a minimum, address the following areas:
  Broad sets of applicability
  Multiple vendors and numerous users

## Slide 14: Proposed Text for “Broad sets of applicability”
An immense number of potential use-cases is currently discussed for LPWAN. Many of these use-cases can only be effectively covered by technology based on LPWAN. Furthermore, recent studies predict billions of low-cost IoT devices based on LPWAN technology in the upcoming years. Hence, the proposed amendment to IEEE 802.15.4 will be able to efficiently cover a broad set of applications with billions of potential devices.

## Slide 15: Proposed Text for “Multiple vendors and numerous users”
The LPWAN market is rapidly growing. An immense number of potential use-cases is currently discussed by network providers, chip manufacturers, start-ups, potential users, and in the scientific community. Recent studies predict billions of IoT devices based on LPWAN connectivity in the upcoming years. An important requirement to achieve this goal is the availability of an open standard, that will be defined within the scope of the group.

## Slide 16: Thank You!
Any Discussions?