## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SG SECN Call for Proposals]
Date Submitted: [5 March, 2018]
Source: [Don Sturek] Company [Itron]
Address [230 W. Tasman Drive, San Jose, CA 95134]
Voice:[+1 669 770 4790], FAX: [+1 866 776 0015], E-Mail:[don.sturek@itron.com]
Re: [IEEE 802.15 4y SECN]
Abstract: [4y SECN Itron proposal for enhanced security]
Purpose: [4y SECN Itron proposal for enhanced security]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15 4y SECN Itron Proposal for Enhanced Security
Don Sturek Itron

## Slide 3: IEEE 802.15.4 Auxiliary Security Header
General MAC Frame Format
No change proposed.

## Slide 4: IEEE 802.15.4 Auxiliary Security Header
Frame Control
  Security Enabled True for Enhanced Security Frames
  No changes proposed to existing fields

## Slide 5: IEEE 802.15.4 Auxiliary Security Header
Auxiliary Security Header
No changes proposed to the Security Control, Frame Counter or Key Identifier fields

## Slide 6: IEEE 802.15.4 Auxiliary Security Header
Security Control Field
No changes to Security Level, Key Identifier Mode, Frame Counter Suppression, ASN in Nonce or Reserved
Fix the Reserved field to cover just bit 7

## Slide 7: IEEE 802.15.4 Auxiliary Security Header
Security Level
Modify Security Level 4 as follows:
For Frame Types 0b00/0b01, AES-256 with MIC-128.
For Frame Type 0b10, extend via SECN IE’s (defined next)
Security levels available to the MAC sublayer |  |  |  |  | 
Security level | Security level field b2 b1 b0 | Security attributes | Data confidentiality | Data authenticity | MIC length (octets)
0 | 000 | None | OFF | NO | 0
1 | 001 | MIC-32 | OFF | YES | 4
2 | 010 | MIC-64 | OFF | YES | 8
3 | 011 | MIC-128 | OFF | YES | 16
4 | 100 | Reserved |  |  | 
5 | 101 | ENC-MIC-32 | ON | YES | 4
6 | 110 | ENC-MIC-64 | ON | YES | 8
7 | 111 | ENC-MIC-128 | ON | YES | 16

## Slide 8: IEEE 802.15.4 Enhanced Security Capabilities IE
Header IE
  Symmetric Key Size
    Specified by algorithm
    128 bit, 192 bit, 256 bit
    4 reserved fields
  Symmetric Encryption Algorithm
    AES
    7 reserved fields
  Encryption Mode
    None (Authentication only)
    CCM*
    CCM
    GCM
    Do we need CTR or CBC?
    At least 3 reserved fields

## Slide 9: IEEE 802.15.4 Enhanced Security Capabilities IE
Header IE (continued)
  Integrity Mechanism
    CCM Authentication Only
    CCM* Authentication Only
    GCM Authentication Only
    HMAC SHA-256
    4 reserved fields
  Integrity Size
    32 bit
    64 bit
    128 bit
    Questionable whether we need any other options

## Slide 10: IEEE 802.15.4 Enhanced Security Capabilities IE
Header IE (continued)
  Key Derivation Function
    SP800-108 CMAC (section 5.1)
    7 reserved fields

## Slide 11: IEEE 802.15.4 Enhanced Security IE
Header IE
  For a given established Key Index
    Agreed Symmetric Key Size, Agreed Symmetric Encryption Algorithm, Agreed Encryption Mode, Agreed Integrity Mechanism, Agreed Integrity Size

## Slide 12: IEEE 802.15.4 Enhanced Security Processing
During Key Establishment (presumably using IEEE 802.15.9 or using some other symmetric key placement scheme):
  Exchange Enhanced Security Capabilities IE between pairs of one-hop devices planning to share a Key Index with information on the Key Source (optional)/Key ID Mode/Key Index
During exchange of beacon frames/data frames/multipurpose frames/command frames using an established Key Index:
  Send Enhanced Security IE with agreed security settings reflected how the frame was secured.