## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IG DEP A dependable MAC protocol matched to bi-directional transmission in WBAN]
Date Submitted: [6 March 2018]
Source: [Toshikuni Miyazaki1, Ryuji Kohno1,2,3] [1;Yokohama National University, 2;Centre for Wireless Communications(CWC), University of Oulu, 3;University of Oulu Research Institute Japan CWC-Nippon]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
2; Linnanmaa, P.O. Box 4500, FIN-90570 Oulu, Finland FI-90014
3; Yokohama Mitsui Bldg. 15F, 1-1-2 Takashima, Nishi-ku,Yokohama, Japan 220-0011]
Voice:[1; +81-45-339-4115, 2:+358-8-553-2849], FAX: [+81-45-338-1157],
Email:[1: kohno@ynu.ac.jp, 2: Ryuji.Kohno@oulu.fi, 3: ryuji.kohno@cwc-nippon.co.jp] Re: []
Re: []
Abstract: [As a dependable MAC protocol for bi-directional wireless networks is proposed for remote feedback sensing and controlling loop is introduced.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: A dependable MAC protocol matched to bi-directional transmission in Wireless Body Area Network (WBAN)
Toshikuni Miyazaki*, Ryuji Kohno*†
＊Graduate School of Engineering Yokohama National University
† University of Oulu Research Institute Japan – CWC-Nippon, Co. Ltd.

## Slide 3: Background and Purpose

## Slide 4: WBAN(Wireless Body Area Network)
Fig. Intra-, Inter-, and Beyond-WBAN
IEEE 802.15.6 which is the international standard for WBAN was published in 2012.
In this study, focus on WBAN MAC layer and propose the dependable system for practical use.
As a background, there is an influence by the aging society around the world. For this reason, there is a trend which is considered combing such innovation with medical technology, health, and welfare.

## Slide 5: MAC(Medium Access Control) layer
Fig. Contention base and free protocols

## Slide 6: Hybrid MAC protocol in IEEE 802.15.6
Fig. Access mode 1(Beacon mode with superframes)
IEEE 802.15.6 defines three types of access mode, Beacon mode with superframes, non-beacon mode with superframes, and non-beacon mode without superframes
B(Beacon)
  For synchronization, sharing the superframe structure in network
EAP(Exclusive Access Phase)
  Specific frames(UP7) are allowed to transmit with contention base protocol
RAP(Random Access Phase)
  Contention base protocol with priority control based on CW
MAP(Managed Access Phase)
  Contention free protocol
Fig. Star topology in WBAN
WBAN has a coordinator node and its network is star topology. Therefore, both access protocols can be used in IEEE 802.15.6, like upper figure.
IEEE 802.15.6 define the structure of hybrid MAC and deal flexibility with complex traffic types in WBAN.

## Slide 7: Issues in medical WBAN MAC protocol
Issues of IEEE 802.15.6 and current study:
  Like IGdep and ETSI SmartBAN, current international standard is studied by a lot of researchers around the world in order to make a more practical standard.
Dependability in WBAN cannot be explained quantitatively
Definition of bi-directional transmission model, especially, MAC protocol for feedback-roop model was not considered.
Almost all of current study evaluate mean values.
  Considering application of medical WBAN, have to guarantee the variance performance.
UP(User Priority) of emergency frame is the highest.
  Considering feedback-roop model, have to define the UP of control frame.
Fig. Relation between average value and variance
Downlink frame based on all levels
Table. Relation between UP(User Priority) mapping and control frame(Downlink)
For practical use of WBAN we propose from the point of dependability(guaranteeing the latency of information) and improving bi-directional transmission model.

## Slide 8: Issues in medical WBAN MAC protocol
Although network system performance is used to be evaluated by using average performance or mean value in conventional researches, variance of performance between worst and best ones in frames and nodes has not been guaranteed.
In order to improve medical WBAN system in the point of dependability:
  Permissible values
  Contention free protocol
  Hybrid superframe structure
Bi-directional transmission is specific issue of WBAN. In the points of efficiency channel utilization, flexibility, and expandability in order to use multiple transmission channel, generally, this system is considered half duplex transmission. In addition, downlink transmission is not sufficiently supported in current standard.
In order to improve bi-directional system for medical WBAN in the point of dependability:
  Permissible values
  Contention free protocol
  Hybrid superframe structure
  User priority mapping

## Slide 9: Definition of dependable MAC protocol in one-directional transmission model

## Slide 10: Aim of this study
Focus on permissible values [1] for each medical and non-medical traffic, and propose the condition of quantitatively dependable latency performance in MAC layer:
  Dependable performance : “variance of performance permissible values ”
Nonmedical traffic
Medical traffic
[1] : IEEE P802.15 Wireless Personal Area Networks, "TG6 Technical Requirements Document (TRD), "IEEE P802.15-08-0644-09-0006, November 2008.
Achieve the permissible values which are different between medical and nonmedical traffic, and propose the system which guarantees each value in its network.
Main technology in this method
  Contention free protocol in hybrid MAC protocol
  Adaptive transmission slot assignment to each node
Table. UP(User Priority) mapping

## Slide 11: Proposal scheme for achieving the permissible values
In order to guarantee each permissible value in MAC layer:
  Update the transmission order for assignment based on Tpermission in every superframe.
addition
Update
Fig. Algorithm of updating transmission order table
The reason why we focus on MAP:
  The probability of frame collision, Pcollicion does not become zero in RAP.
  Otherwise, Pcollision in MAP become zero if consider only MAC layer. So, we focus on this phase.
But, there is a drawback in the point of superframe structure with hybrid MAC.
Fig. Constraint of proposal scheme
“Transmission slot interval < permissible values”

## Slide 12: Definition of evaluation index
Fig. Superframe structure in this performance evaluation
Fig. Polling method in response to time axis
In this performance evaluation, we use polling access for MAP in hybrid MAC protocol.
  Latency performance can not express the factor caused by MAP because we use hybrid MAC:
  Let TBusy, TBackoff , TCollision, TPoll, and TpSIFS denote the waiting time for channel busy, backoff time, collision, poll frame, and pSIFS respectively, the latency per frame TLatency is given as follows:
Propose the system in order to achieve this equation
, , : Latency caused by contention base
: Latency caused by contention free
: Latency caused by interval of MAC

## Slide 13: Evaluations considering permissible values
Data rate | 242.9 kbps
Payload length of frames | 128 octets
Size of transmission slot in MAP | 6 msec.
Superframe length | 124.5 msec.
Beacon length | 1 msec.
EAP length | 9.5 msec.
RAP-MAP length | 114 msec.
Simulation time | 60 sec.
Trial times | 1000
Fig. Network structure in this performance evaluation
Fig. Superframe structure in this performance evaluation
Table. Simulation parameters
Considering only sensing frame(uplink traffic), and downlink traffic is considered only acknowledge
The probability of transmitting UP7 frames in each node is one hundredth
For the simplicity, offered load of each node is the same, but UP5-6 node in Figure is valuable.

## Slide 14: Results of worst latency
Fig. Worst latency performance between IEEE 15.6(left) and proposal scheme(right) with permissible values
Conventional method cannot adaptively assign the transmission slots to each node under permissible values, so its worst latency is over limitation, permissible values.
Proposal method can assign the transmission slot to each node in superframe adaptively, therefore, achieve the limitation.
In this simulation, superframe size and structure is stable, and trial times is large, so worst latency became the same values in each type of node.
From the results, Tpermission is proved valid as expressing quantitatively dependable latency performance

## Slide 15: WBAN MAC protocol considering bi-directional transmission model

## Slide 16: Bi-directional transmission model
Including emergency frame(UP7)
Fig. A example of feedback model
Downlink frame based on all levels
Issues of bi-directional WBAN system in MAC layer
  Priority order become like this sign of inequality, but standard is not considered medical emergency control(downlink)
    Change a part of conventional UP mapping and EAP
  In order to consider the quantitatively dependable performance
Focus on these features, we propose a MAC protocol for WBAN bi-directional transmission model
Table. Relation between UP(User Priority) mapping and control frame(Downlink)
Parameters | Uplink | Downlink
Payload length | Short~Long* | Short
Interval of frame generation | Low~High* | Low
Priority | Low~High* | Highest
* : Depends on the types of node
Table. Benchmark of bi-directional model

## Slide 17: Modified methods of IEEE 802.15.6
Table. Modified UP mapping for bi-directional transmission
Control frame is calculated and transmitted based on sensing frames which include medical and emergency traffic
  Change the UP class like table
EAP is set in hybrid superframe structure in IEEE 802.15.6 based on UP mapping and allow to transmit only emergency frames(or implant event report)
  For this reason, in general, this phase becomes like a reserve field and performance in MAC layer(i.e. latency, throughput) decrease
We proposed M-EAP(Modified-EAP), which is allowed to transmit both emergency and control frame of downlink.
  Become more busy phase than EAP, so the performance can be improved
  Adapt to priority control based on modified UP mapping
  In case, if frame collision occurred between uplink and downlink traffic, coordinator node can find the frame collision based on the feature of acknowledge
This proposal scheme, M-EAP, is based on contention base, therefore it cannot guarantee the permissible values based on Pcollision

## Slide 18: G-Slot algorithm in order to achieve the dependability
Proposal scheme, G-Slot(Guaranteed Slot), is based on scheduled access and considered GTS(Guaranteed Time Slot: IEEE 802.15.4) method as reference in order to adapt to WBAN MAC protocol.
Branch condition in Figure is as follows;
  If control frame (downlink traffic) is or not
  Emergency frame is or not
    Especially, when a node transmits frame with emergency, the others also transmits frames with emergency because human behavior is consist of a lot of parameters.
  Superframe number is odd or even
    In order to achieve the permissible value certainly, the transmission slot assignment interval becomes less than 125 ms or 250 ms. In this method, we set the superframe length less than 125 ms, so this branch condition is.
Fig. G-Slot algorithm in MAP
Fig. GTS algorithm in IEEE 802.15.4
Fig. Relation between G-Slot and MAP
We propose from the sight of both contention base and free

## Slide 19: Evaluations using M-EAP and G-Slot
Fig. Network structure for bi-directional transmission model
Fig. Superframe structure for bi-directional transmission model
This phase is defined inactive in this simulation
The number of node | Sensor nodes：6 Coordinator node：1
Payload length of control frame | 8 octets
Size of transmission slot in MAP | 5.5 msec.
Superframe length | 120.5 msec.
Table. Simulation parameters
Condition in this simulation
  Control frames are calculated and transmitted when coordinator node received 10 frames by each node(No.4~6)
  Control frame can transmit in only M-EAP and G-Slot
Table. Modified UP mapping for bi-directional transmission

## Slide 20: Results of worst latency and throughput
Fig. Worst latency in bi-directional transmission model
Fig. Throughput evaluation in active condition
Latency performance
  Proposal method can assign the transmission slot to each node in every superframe adaptively by using G-Slot, therefore, achieve the permissible values. This algorithm is based on TDMA:
Throughput performance
  In this study, throughout is evaluated by using MAC payload length
  G-Slot algorithm set the transmission slot in MAP as needed. In other words, this algorithm decreases the waste slots.
  For fairness comparison, except the inactive phase to calculate the throughput, called active condition.
  Proposal scheme becomes busier than standard by using M-EAP, and decreases the waste slot by using G-Slot. It means that efficiency of transmission channel utilization of proposal scheme became higher than standard.

## Slide 21: Considering the superframe ratio
Both proposal methods, M-EAP and G-Slot will not be good performance in some cases. One of the big factor is network offered load like Figure.
Fig. Drawback of proposal scheme vs. offered load
G-Slot algorithm can decrease the waste slot, but the number of assignable transmission slot is limited if the MAP length is fixed. Therefore, its performance in high offered load condition become worse.
  In order to improve its performance, consider the superframe ratio which is specific issue in hybrid MAC protocol and not considered in IEEE 802.15.6 about.
For the simplicity, the superframe components are expressed by MAP, RAP, and inactive;
We focus on the ratio of superframe structure and propose the more dependable MAC protocol.

## Slide 22: Defines the borders of extreme conditions
It is indeed that in RAP, but permissible values can be achieved if network offered load is low;
: The number of retransmission
: Channel capacity
: data rate
: Ideal throughput
: MAC payload length
: Transmission slot in MAP
(using superframe which is composed of only MAP)
Fig. Border of low extreme condition
These borders are calculated by using simulation parameters in this study. The upper higher border is set as about 180 packet/s for only MAP superframe structure and lower border is set as about 60 packet/s for only RAP superframe structure.
These conditions are calculated by using only MAC layer.

## Slide 23: Defines the borders of middle condition
: Active transmission slot / Idle transmission slot, only MAP structure
Middle condition means that it is balanced between contention free and contention base as the same length(…line). Using the Rslot , estimate the network traffic and decide the superframe structure.
Fig. Rslot in only MAP superframe structure vs. offered load
Condition：
Condition：
Condition：
Condition：

## Slide 24: Extend the MAP length for offered load
In order to guarantee the permissible values, MAP is needed. But, if the length of MAP is long, its performance become worse
  Proposal scheme, G-Slot, is suitable to this condition because G-Slot algorithm set the transmission slot in MAP as needed. In other words, this algorithm decreases the waste slots.
  In this study, not consider the inactive phase for fairness in order to compare with IEEE 802.15.6
Fig. Extended G-Slot algorithm
In order to guarantee the permissible values, MAP is needed. In addition, if the length of RAP is long, its performance become worse.
  Propose extended G-Slot algorithm for offered load condition
Condition：
Condition：

## Slide 25: Evaluation of throughput comparison
We used IEEE 802.15.6 MAC protocol for the comparison, its detail is as follows
  A superframe length is the same between IEEE 802.15.6 MAC and proposal scheme
  Each phase length is constant in every offered load condition because it is not refer to in standard
Fig. Throughput evaluation in MAC layer vs. offered load
Condition：
  The superframe structure is only RAP, but Pcollision is quite lower. So the performance is close to ideal one.
Condition：
  The superframe structure is only MAP, so Pcollision is zero. The throughput curve is close to ideal one
Condition：
  Using G-Slot, the waste slot decrease. Therefore, the performance is close to ideal one.
Condition：
  To increase the length of MAP, Pcollision become low. The floor in graph which appears in early state can be restrained.

## Slide 26
Both latency performance curves are not considered the divergent value which occurred by frame discarded.
Latency is evaluated from transmission starting state to transmission completed state.
Fig. Mean latency evaluation in MAC layer vs. offered load
Condition：
  RAP is superior to MAP in the point of immediacy. So, achieve lower latency performance than IEEE 802.15.6 MAC
Condition：
  Appear the floor in performance curve because of buffering.
Condition：
  The length of RAP in proposal scheme is longer than standard one. Therefore, proposal is superior.
Condition：
  If RAP length is long in response to high offered load condition, there are a lot of latency caused by retransmission. Therefore, IEEE 802.15.6 MAC is inferior to our proposal scheme.
Evaluation of mean latency comparison

## Slide 27
Condition：
  It is indeed that in RAP, but permissible values can be achieved if network offered load is low. Therefore, worst performance can be achieved in every case.
Condition：
  In this study, the latency of discarded frames is not reflected in latency evaluation and consider only MAC layer. So, the latency depends on the interval of slot assignment.
Condition：
  If the percentage of RAP is larger than MAP in a superframe, worst performance is guaranteed by using the adaptive algorithm, G-Slot.
Condition：
  Using the proposal algorithm, G-Slot, it is achieved that worst performance is less than permissible values. In addition, the percentage of MAP is longer than RAP in a superframe, Pcollision is lower and latency performance improves.
Fig. Worst latency evaluation in MAC layer vs. offered load
Evaluation of worst latency comparison

## Slide 28: Conclusion
Considering the application of medical WBAN, we study the dependable MAC protocol.
Not only evaluate the average values, but also focus on the relation between variance and permissible values. In addition, define the evaluation index of quantitatively dependable performance
  Dependable performance index: “variance of performance permissible values ”
  Adaptive transmission slot scheme based on permissible values
Focus on contention free protocol, and propose the adaptive slot assignment scheme for both one-directional and bi-directional transmission models.
  M-EAP
  G-Slot
Finally, show the flexibility superframe management to network traffic and achieve the better performance, throughput, latency, and transmission success rate, than current standard method.
  Ratio of superframe structure
  Offered load issue using theoretical and estimated index