## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ULI profile and module organization for convenient programmability]
Date Submitted: [8 Mar 2018]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expy, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [Overview of IETF [lpwan] Working Group SCHC specification.]
Abstract: [Header compression plays a crucial role in enabling IPv6 over lpwan]
Purpose: [Describe SCHC to motivate further improvements by compressing 802.15.4 headers]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SCHC: Static Context Header Compression
draft-ietf-lpwan-ipv6-static-context-hc
  (…-10.txt)
Static Context --> not mobile
Basically a dictionary-ruleset approach
Technology-independent
  fragmentation needed for IPv6 adaptation
Star topologies
  All packets follow the same path
Slide 2
Notes: March 18
Page 2

## Slide 3: LPWAN Architecture, Compression
Radio Gateway (RG)
Radio Gateway (RG)
Radio Gateway (RG)
Network Gateway (NGW)
Internet
Compression from Dev  NGW

## Slide 4: SCHC applicability
predictable traffic flows
  new applications not easily installed
no out-of-sequence delivery
Up (Dev-->NGW), down, or bidirectional
Provisioning rulesets is out of scope[!]
Meaning of Rule IDs is Dev-specific
  NGW has to know the Dev layer-2 address as well as the Rule ID
Slide 4
Notes: March 18
Page 4

## Slide 5: SCHC fragmentation
Retransmission timer for fragments
Size of FCN (Fragment Compressed Number) is technology specific, >=3
All fragments of the same packet have the same DTag of size >= 0 bits
MIC over packet before fragmentation
Bitmap of fragments of the current window
Slide 5
Notes: March 18
Page 5

## Slide 6: Fragment reliability modes
No-ACK
ACK-Always
ACK-on-Error
Slide 6
Notes: March 18
Page 6

## Slide 7: Matching operators (directional)
Equal
  match result against a packet field value
Ignore
  No check is done against a field value
MSB(x)
  Match against the most significant x bits
match-mapping
  Target Value is list of values, output is index
Slide 7
Notes: March 18
Page 7

## Slide 8: Compression/Decompression Actions (CDA)
not-sent CDA
value-sent CDA
mapping-sent CDA
LSB(y) CDA
DEViid, APPiid CDA (~ device L2 addr)
Compute-*
  elided and computed (checksum, length…)
Slide 8
Notes: March 18
Page 8

## Slide 9: SCHC Compression for IPv6 and UDP headers
IPv6 version
IPv6 Traffic class
Flow label
Payload Length
Next Header
Hop Limit
IPv6 source and destination prefixes
IPv6 source and destination IID
IPv6 extensions (no compression actions defined yet)
UDP source and destination port
UDP length
UDP Checksum
Slide 9
Notes: March 18
Page 9