## Slide 1
802.15: “Wireless Specialty Networks”
Projects Summary Overview + Status
March 2018
Clint Powell
ZigBee Alliance - GB 868 MAC/PHY Editor
ZigBee Alliance - Certification Adv. Group Chair
SCE - FAN System Architect

## Slide 2: Disclaimer…
“At lectures, symposia, seminars, or educational courses, an individual presenting information on IEEE standards shall make it clear that his or her views should be considered the personal views of that individual rather than the formal position, explanation, or interpretation of the IEEE.”
IEEE-SA Standards Board Operation Manual (subclause 5.9.3)
Notes: 2
3/13/2018

## Slide 3: IEEE 802 Organization
Standards Activities Board
IEEE Standards Association
802.3
CSMA/CD
Ethernet
802.24
Vertical App. TAG
802.11
Wireless
WLAN
802.15
Wireless
Specialty
Networks
802.21
Media
Independent
Handoff
802.19
Co-existence
WG
Sponsor
IEEE 802
Local and Metropolitan Area Networks
(LMSC)
Sponsor
Sponsor
Sponsor
802.18
Radio
Regulatory
TAG
802.16
Wireless
Broadband
Access
802.22
Wireless
Regional
Area
Networks
802.1
Higher
Layer
LAN
Protocols
Privacy
Study
Group
Voting Members: 78
www.ieee802.org/15
OmniRan

## Slide 4: 802.15 Scope and Purpose
Initial activities focused on wearable devices hence “personal area networks”
Focus is on “specialty”, typically short range, communications. If it is wireless and not a LAN, MAN, RAN, or WAN, odds are its 802.15
Activities are diverse and varied
  Data rates from 2kbps to 100gbs
  Ranges from meters to kilometers
  Frequencies from 400MHz to 800THz
  Predominantly non TCP/IP applications
Only 802 Working Group with multiple MACs

## Slide 5: 802.15 Completed Projects
802.15.3 - High Rate (55 Mbps) Multimedia WPAN
  15.3 amendments:
  802.15.3c - High Rate (>1Gbps) mmWave 15.3 PHY
  802.15.3 Revision A - Roll-up of amendments b and c plus conversion from 64 bit to 48 bit MAC addressing
  802.15.3d - THz band 100Gb/s PHY layer for point to point data center applications
  802.15.3e - High-Rate Close Proximity Point-to-Point Communications (initial target use - Japan Olympics)
  802.15.3f - 60GHz Band Extension for 15.3

## Slide 6: 802.15 Completed Projects
802.15.4 - Low Rate (250kbps). Energy Efficient WPAN for WSN type applications (initial publication in 2003)
  15.4 Amendments/Revisions:
  802.15.4-2006 Revision - bug fixes, security update, and add higher rate sub-GHz PHY
  802.15.4a - Higher data rate 15.4 UWB PHY
  802.15.4c - Sub 1 GHz 15.4 PHY for China
  802.15.4d - Sub 1 GHz 15.4 PHY for Japan
  802.15.4e - 15.4 MAC Enhancements (GTS among others)
  802.15.4f - 15.4 PHY for Active RFID
  802.15.4g - 15.4 PHY for Field Area Smart Utility Networks
  802.15.4-2011 Revision - roll-up of amendments a, c, and d
  802.15.4j - 15.4 PHY using US dedicated medical band

## Slide 7: 802.15 Completed Projects
  15.4 Amendments/Revisions (cont):
  802.15.4k - 15.4 PHY for Low Energy Critical Infrastructure Monitoring
  802.15.4m - 15.4 PHY for operation in TV White Spaces
  802.15.4n - 15.4 PHY for Chinese Medical Applications
  802.15.4p - 15.4 PHY for Rail Communications and Control
  802.15.4q - Ultra Low Power 15.4 PHY
  802.15.4-2015 Revision - bug fixes and roll-up of amendments e, f, g, j, k, m, and p
  802.15.4t - 2 Mbps PHY (includes backwards compatibility mechanism to original 250 kbps O-QPSK)
  802.15.4u - 865 MHz to 867 MHz Band in India
  802.15.4v - Regional Sub 1GHz Band (RSB)
  802.15 Corrigendum

## Slide 8: 802.15 Completed Projects
802.15.5 - Mesh Networking Recommended Practice
802.15.6 - Body Area Networking for medical and entertainment applications
802.15.7 - Visible Light Communications using structured lighting
802.15.9 - KMP-Recommend Practice for a 15.4 Key Management Protocol
802.15.10 - Layer 2 Routing Recommended Practice

## Slide 9: 802.15 Project Stages
3 Main Types of Groups
  Interest Group
    Determines if sufficient interest to form a Study Group
  Study Group
    Studies general need
    Develops PAR and CSD docs if project is warranted
  Task Group
    Develops Draft
    Runs Letter Ballot - 802.15 Voters
    Runs Sponsor Ballot - Any SA Voters

## Slide 10: 802.15 Projects Status
Projects Status Color Key:
  BLACK: no status change
  BLACK: status update
  GREEN: new project
  …Projects continue to be published in 2018

## Slide 11: 802.15 Active Projects/Status
IEEE802.15.1 Standard Being Withdrawn:
  802.15.1 (Bluetooth) - Withdrawal to RevCom (unconditional)
    STATUS: Approved by SB and 802 EC, forwarded to Revcom for approval
IEEE802.15.2 Standard Being Withdrawn:
  802.15.2 (802.15 Coexistence) - Withdrawal to RevCom (unconditional)
    STATUS: Approved by SB and 802 EC, forwarded to Revcom for approval

## Slide 12: 802.15 Active Projects/Status
IEEE802.15.3 Amendments:
  802.15.3d - THz band 100Gb/s PHY layer for point to point data center applications
    STATUS: Published October 2017
  802.15.3f - 60GHz Band Extension for 15.3
    STATUS: Published December 2017

## Slide 13: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects:
  802.15.4 Corrigendum - Addressing bit/byte ordering error in 2015 revision
    STATUS: Approved, awaiting publication
  802.15.4md Revision - bug fixes and roll-up of amendments n, q, s, t, u, v, and Corrigendum
    STATUS: Roll up document has been generated, to be sent to outside Alliances and SDO’s for review
  802.15.4r - Common 15.4 ranging protocol for Location Based Services indoors or out
    STATUS: Morphed into 15.4z

## Slide 14: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects (cont):
  802.15.4s - MAC enhancement for improved spectrum resource utilization
    Includes Tx Pwr Control
    STATUS: Approved, awaiting publication
  802.15.4w - Low Power Wide Area Network (LPWAN) PHY
    STATUS: PAR and CSD Approved by 802.15 WG and 802 EC, forwarded to Nescom for Approval

## Slide 15: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects (cont):
  802.15.4x - Increase SUN OFDM PHY data rates up to 2.4Mb/s
    STATUS: PAR and CSD Approved by 802.15 WG and 802 EC, forwarded to Nescom for Approval
  802.15.4y - Adding AES-256 CCM plus a cipher suite/authentication method registry and a process for inclusion of additional algorithms
    STATUS: PAR and CSD Approved by 802.15 WG and 802 EC, forwarded to Nescom for Approval

## Slide 16: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects (cont):
  802.15.4z - Enhancements to the HRP and LRP UWB PHYs and associated ranging techniques
    STATUS: PAR and CSD Approved by 802.15 WG and 802 EC, forwarded to Nescom for Approval

## Slide 17: 802.15 Active Projects/Status (cont)
  Revision 1 to IEEE802.15.7 - 2012, Standard for Visible Light Communications.
  Extend spectral range to include near UV and near IR
  Rename to “Optical Wireless Communications”
  Add capability to specifically to address Optical Camera Communications for use with existing as well as future smart mobile devices
    STATUS: Finishing up Letter Ballot phase, 280 comments received on 2nd Letter Ballot, 148 resolved at March mtg., conditional request to start Sponsor Ballot approved by 802.15 WG and 802 EC

## Slide 18: 802.15 Active Projects/Status (cont)
802.15 New Standards Work:
  802.15.8 - Peer Aware Communications (PAC)
    Standard for Infrastructure-less Peer Aware Communications among Mobile Devices
    STATUS: Approved, awaiting publication
  802.15.10a - Routing Module Addressing (RMA)
    Amendment adding additional routing modes
    STATUS: Call for proposals issued

## Slide 19: 802.15 Active Projects/Status (cont)
802.15 New Standards Work (cont):
  802.15.12 - Upper Layer Interface (ULI) for 15.4:
    Make IEEE 802.15.4 easier to use, like 802.11 and 802.3
    Enable the use of many of the higher layer protocol stacks used by 802.11 and 802.3 without changes
    Allow 15.4 to address new applications, yet maintain backward compatibility with existing devices and applications
    Potentially consolidate L2R, KMP, 6T,& 6lowpan in one ULI
    Coordinated with 802.1 and IETF
    STATUS: Working on comment resolution from internal review

## Slide 20: 802.15 Active Projects/Status (cont)
802.15 New Standards Work (cont):
  802.15.13 - Multi-gigabit OWC
    Break out from 802.15.7a with a new MAC
    STATUS: Working on comment resolution from internal review

## Slide 21: 802.15 Active Projects/Status (cont)
802.15 Interest Groups:
  Dependability IG (DEP): seeking to identify non implementation based strategies, which could be standardized, that inherently improve wireless link reliability.
  Guide for 15.4 Use IG (Guide):
    STATUS: On hold
  High Rate Rail Communications IG (HRRC)
  THz IG: Review and discuss the latest advances for using THz bands for wireless date applications
  Vehicular Assistive Technology IG (VAT): Discussing PHY safety

## Slide 22: 802.15 Other Activity
Joint effort with IETF:
6Tisch Interest Group-formed to support collaboration and coordination of 802.15 activities/positions with IETF on an activity to utilize capabilities in 15.4e in conjunction with IPv6, specifically time slotted channel hopping (TSCH).
    STATUS: Ongoing effort

## Slide 23: 802.15 Future Projects
802.15:
Improved Coexistence – Interest in improving targeted coexistence between 802.15 and 802.11 networks.
    STATUS: Data was Presented on Coexistence Performance Between 802.11 and 802.15 Networks, at the Sept. Mtg. 802.15, and was Discussed by the 802.15 WG. 802.15 WG Voted to Seek Review by 802.19 Coexistence WG.
    - No activity since
    Presentation can be found at:
    https://mentor.ieee.org/802.15/dcn/17/15-17-0522-02-wng0-802-11ah-and-ieee-802-15-4g-coexistence-submission.pptx

## Slide 24: Questions? Clint Powell cpowell@ieee.org