## Slide 1
Proposal of Polling Mechanism in both CFP and CAP
Nikola Serafimovski (pureLiFi), Chong Han (pureLiFi)
Notes: Contention access period (CAP) and contention-free period (CFP)

## Slide 2
Superframe structure in D2
CFP and CAP are not fixed within the superframe. CAP starts immediately after beacon. CFP starts after CAP.
All contention-based transactions are completed before the CFP begins.
Each device transmitting in a GTS ensures that its transaction is complete before the time of the next GTS or end of CFP.

## Slide 3
Polling mechanism
Full Duplex Time Division Multiplex (FTDM) allows simultaneous transmissions on both DL and UL channels.
STAs may utilize the UL channel immediately after decoding the PHY header.
STAs may attach data frames after responding to poll request.
PC/AP polls the next STA if not hearing poll response from the polled STA.
PC/AP may reclaim the channel if a STA fails to transmit after being granted the access.
DL
UL
polls STA2; data for STA2 (d2)
STA1: Poll response
STA2: Poll response; Data from STA2 (d3)
STA1: ACK d1
polls STA1; data for STA1 (d1)
polls STA5; data for STA5 (d4); ACK d3
STA5: no response.
STA2: ACK d2
polls STA9; data for STA9 (d5)
STA9:Poll response
…
…

## Slide 4
Polling in CFP and CAP
Polling is initiated by the PC/AP. Hence, not pure contention based.
However, the duration of channel occupation depends on replies from STAs, length of packets, data transmission demands. Hence, not guaranteed services.
Allowing polling in both CFP and CAP enhances QoS (e.g., lower collision probability in CAP).
Polling within CAP could be regarded as a long duration gained by PC/AP via the contention with other STAs.
CAP starts
PC/AP gains the channel and starts polling
Superframe
CAP CFP
Polling
GTS
GTS
GTS
STA 2
STA1
…
Beacon