## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: pureLiFi’s Proposals for LB-OFDM PHY
Date Submitted: 27 April 2018
Source: Nikola Serafimovski, Chong Han, Stephan Berner, Mostafa Afgani (pureLiFi)
Address: 9 Haymarket Terrace, Edinburgh, UK, EH12 5EZ
Mobile:[+44-7503016565], E-Mail:[chong.han@purelifi.com]
Re:
Abstract: Proposals for LB-OFDM PHY
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
pureLiFi’s Proposal for
LB-OFDM PHY
Nikola Serafimovski (pureLiFi), Chong Han (pureLiFi), Stephan Berner (pureLiFi), Mostafa Afgani (pureLiFi)

## Slide 3
PPDU Format
Preamble
Basic PHY
header
Payload
1 OFDM symbol
variable
4 OFDM symbols
Notes: PHY header: 2 OFDM symbols after applying Hermitian symmetry.

## Slide 4
Preamble (1)
PN sequence
Hermitian symmetric long training sequence
2 OFDM symbols
2 OFDM symbols
PHY Preamble field consists of PN sequence training (used for AGC convergence, timing acquisition, and coarse frequency acquisition in the receiver) and two repetitions of a “Hermitian symmetric long training sequence” (used for channel estimation and fine frequency acquisition in the receiver), preceded by a guard interval (GI).
The preamble is a time domain sequence and does not have any channel coding or line coding.

## Slide 5
Preamble (2)
Generation of PN sequence training
  Select two 20-bit PN sequences:
    pn_seq_0 = 20'b01001011000001110111;
    pn_seq_1 = 20'b01101100111101010000;
  Up-sample the above sequences by 8
  Pulse shape with the following pulse which is on segment of the original 802.11 short sequence {-479, 416, -10, -409, 67, -409, -10, 416}
  Flip the sequence got by the last step to get two sequences for each original PN sequences

## Slide 6
PHY Header (1)
Rate
Advanced modulation header
PSDU length
11 bits
1 bit
3 bits
Tail
Parity
1 bit
6 bits
Reserved
1 bit
PHY header fields | Bit-width | Explanation on usage
Rate | 3 | Provide PHY type and data rates
Reserved bits | 1 | Reserved for future use
PSDU length | 11 | Length up to
Advanced modulation header | 1 | Indicating whether an Advanced Modulation Header is included in the next OFDM frame
High-reliable MAC header | 1 | Indicating whether a high-reliability MAC header encoding is used.
Parity | 1 | An even parity check bit for the information in bits 0 - 16.
Tail | 6 | 6 zero bits
PHY header fields | Bit-width | Explanation on usage
Rate | 3 | Provide PHY type and data rates
Reserved bits | 1 | Reserved for future use
PSDU length | 11 | 
Advanced modulation header | 1 | Indicating whether an Advanced Modulation Header is included in the next OFDM frame
High-reliable MAC header | 1 | Indicating whether a high-reliability MAC header encoding is used.
Parity | 1 | An even parity check bit for the information in bits 0 - 16.
Tail | 6 | 6 zero bits
High-reliability MAC Header
1 bit
Basic PHY Header:

## Slide 7
PHY Header (2)
Adaptive
CQI
1 bit
1 bit
1 bit
STR
Tail
eU
1 bit
1 bit
SC-FDMA
2 bits
6 bits
MIMO RS
1 bit
DFT
1 bit
Advanced Modulation Header:
1 bit
5 bits
Relaying enabled
Relaying mode
MIMO enabled
2 bits
Field | Bit | Explanation on usage | Field | Bit | Explanation on usage
Adaptive | 1 | Whether carriers are to be allocated dynamically | Relaying mode | 2 | Specify the mode of relaying operation to be performed
CQI | 1 | Indicate if CQIs should be calculated in the PHY for the current transmission frame | MIMO enabled | 1 | Indicate if a MIMO mode is enabled for the current PHY frame
eU-OFDM | 1 | Indicate if DATA is encoded using eU-OFDM | MIMO reference symbol | 1 | Indicate format of the reference symbols used for CQI estimation
STR | 1 | Indicate the number of eU-OFDM streams superimposed in the signal encoding procedure | Reserved bits | 2 | Reserved for future use
SC-FDMA | 1 | Indicate if DATA field is encoded using SC-FDMA | Parity | 1 | An even parity check bit for the information in bits 0 - 16.
DFT | 5 | DFT size used in the SC-FDMA pre-coding procedure | Tail | 6 | 6 zero bits
Relaying enabled | 1 | Indicate if relaying should be performed for the current PHY frame |  |  | 
Res
Parity
1 bit

## Slide 8
PHY Header (3)
The Header contains all information necessary for demodulating the subsequent frame payload.
It is always encoded in 1/2 FEC rate BPSK modulation using DCO-OFDM.

## Slide 9
Payload
Payload is transmitted at one of the supported data rates.
SERVICE bits: the first 0-6 bits are set to 0s to synchronize the descrambler in the receiver. The remaining 9 bits (7–15) shall be reserved for future use.
The PSDU field has a variable length and carries the data of the PHY frame. If eU-OFDM is enabled the Data shall be encoded in an eU-OFDM fashion.
Tail bits: The PPDU TAIL field shall be six bits of 0, which are required to return the convolutional encoder to the zero state.
Pad bits: Pad bits are appended to DATA field as to ensure the number of bits in the DATA field to be a multiple of .The appended pad bits are set to 0 and are subsequently scrambled with the rest of the bits in the DATA field.
PSDU
Tail
Up to aMaxPHYFrameSize
Pad
6 bits
Service
16 bits
variable

## Slide 10
R0-R3 | Modulation | FEC rate | Date rate (Mbps) (OCR 1 MHz) | Date rate (Mbps) (OCR 16 MHz) | Date rate (Mbps) (OCR 20 MHz) | Date rate (Mbps) (OCR 32 MHz)
0001 | BPSK | Inner CC(1/2) | 0.3 | 4.8 | 6 | 9.6
1011 |  | Inner CC(3/4) | 0.45 | 7.2 | 9 | 14.4
0010 | QPSK | Inner CC(1/2) | 0.6 | 9.6 | 12 | 19.2
0011 |  | Inner CC(3/4) | 0.9 | 14.4 | 18 | 28.8
0100 | 16-QAM | Inner CC(1/2) | 1.2 | 19.2 | 24 | 38.4
0101 |  | Inner CC(3/4) | 1.8 | 28.8 | 36 | 57.6
0110 | 64-QAM | Inner CC(2/3) | 2.4 | 38.4 | 48 | 76.8
0111 |  | Inner CC(3/4) | 2.7 | 43.2 | 54 | 86.4
Data Rates
The range of the available OCRs is [1, 32] MHz.
Intermediate frequencies are achievable by applying combined selection from dividers (1, 2, 3, 4), (1/2, 1/4, 1/6, …, 1/64), and (2, 4, 6, …, 128).
Finally, the OCR can be obtained by dividing the frequency by 8. The data rates for are times of the data rates for OCR 1MHz in the above table for each MCS accordingly.

## Slide 11
Interleaver/Deinterleaver
All encoded data bits shall be interleaved by a block interleaver with a block size corresponding to the number of bits in two OFDM symbols, .
The interleaver is defined by a two-step permutation.
The deinterleaver, which performs the inverse relation, is also defined by two permutations.

## Slide 12
Relaying (1)
Amplify and forward
  The PPDU shall be buffered at the receiving node and upon successful demodulation of the advanced modulation header and identification of the amplify and forward specification.
  The PPDU shall be retransmitted without any further processing at the PHY layer.
  In FD relaying mode, the relay STA shall simultaneously receive the information on the downlink and shall transmit it on the uplink.
  In HD relaying mode, the relay STA shall store the data packets in order to retransmit them to the STA during its designated transmission period.
  The relay STA can erase the stored packet after it receives the ACK.
  The method is proprietary.
  In both configurations, the PHY header shall be demodulated before a decision for relaying can be made.

## Slide 13
Relaying (2)
Decode and forward
  The PPDU shall be completely demodulated and upon successful identification of the decoded and forward specification.
  The PPDU shall be re-modulated and re-transmitted.
  The relay STA can erase the stored packet after it receives the ACK.
  The method is proprietary.