## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PM PHY Synch Evaluation
Date Submitted: 26 April 2018
Source: Malte Hinrichs, Volker Jungnickel [Fraunhofer HHI]
Address: Einsteinufer 37, 10587 Berlin, Germany
Voice:[+49-30-31002 284], E-Mail:[malte.hinrichs@hhi.fraunhofer.de]
Re:
Abstract: This document provides the evaluation results on preamble of PM PHY proposed by Fraunhofer HHI to TG13.
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15.13 Evaluation of PM PHY synchronization
Date: 2018-04-26 Place: Warsaw, Poland
Authors:

## Slide 3: PM PHY
Scope
  Low SNR operation
  E.g. IoT, uplink for mobile devices
  Hadamard- or 8B10B coded PAM, Reed-Solomon FEC
Sync
  Robust synchronization/frame start detection required
  Reliable operation even if SNR is too low for data transmission
  Proposed method: Cross-correlation with known preamble
  What length is needed for the preamble?

## Slide 4: Preamble structure
Sequence
  Enhanced Gold sequence AN: (N-1)-bit Gold sequence appended with a 1-bit for balancing
  Sequence lengths for AN : N = 16, 32, 64
Repetition pattern: + + – + – –
  Optimized for use of Minn auto-correlator
  Good autocorrelation properties (low side peaks)
  Resulting preamble: [AN AN –AN AN –AN –AN]
  Overall length is 6*N

## Slide 5: Simplified frame structure
Bit scaling
  Bipolar mapping around DC bias: 0/1  -1/+1
  Modulation signal power = 1
Simulated frame:
  Zeros (L = 6*N bits)
  Preamble (L bits)
  Random data (L bits)
   Emulates the beginning of the PHY frame
Random bits
Preamble
Zeros
96/192/384 bits each

## Slide 6: Channel simulation
Apply Channel Impulse Response (CIR)
  Upsampling, convolution with CIR, downsampling
Add AWGN
  Test 10,000 noise realizations
Detector: Cross correlation with ideal preamble
  Selection of first value > threshold per frame
  Count positive detection rate
Random bits
AWGN
CIR
n
n
X
+
Detector
Preamble
Zeros

## Slide 7: Detection threshold
Finding of threshold
  Generate frame with 100,000 noise samples
  SNR (relative to preamble power): -5 dB
  Perform cross-correlation of the preamble at all possible shifts
  100,000 random correlation values
  Random values are sorted (see CDF)
  Detection threshold is selected so that 0.1% of all random values lie above it
   0.1% false positive rate

## Slide 8: Detection threshold False Alarm Rate: 0.1%

## Slide 9: Evaluation
Synchronization reliability according to IEEE 802.15.13 evaluation framework
  AWGN channel
  Scenario 3, Device 3 (S3/D3): „clean“ CIR, little spreading
  Scenario 4, Device 7 (S4/D7): „dirty“ CIR, energy is spread over several peaks, frequency selective
  Optical Clock Rates 3.125..200 MS/s
  Requirement: Detection rate 99.9% at false positive rate 0.1%
Notes: Only showing 25/50 MS/s

## Slide 10: CIR Scenario 3, D3
Notes: Insert Scenario overview

## Slide 11: CIR Scenario 4, D7
Notes: Insert Scenario overview

## Slide 12: AWGN: Detection ratio for different preamble lengths
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 13: S3/D3: Detection ratio for different preamble lengths @3.125 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 14: S3/D3: Detection ratio for different preamble lengths @6.25 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 15: S3/D3: Detection ratio for different preamble lengths @12.5 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 16: S3/D3: Detection ratio for different preamble lengths @25 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 17: S3/D3: Detection ratio for different preamble lengths @50 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 18: S3/D3: Detection ratio for different preamble lengths @100 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 19: S3/D3: Detection ratio for different preamble lengths @200 MS/s
Notes: Compare to slide 11 (AWGN): Barely a difference (but there is one)

## Slide 20: S4/D7: Detection ratio for different preamble lengths @3.125 MS/s

## Slide 21: S4/D7: Detection ratio for different preamble lengths @6.25 MS/s

## Slide 22: S4/D7: Detection ratio for different preamble lengths @12.5 MS/s

## Slide 23: S4/D7: Detection ratio for different preamble lengths @25 MS/s

## Slide 24: S4/D7: Detection ratio for different preamble lengths @50 MS/s

## Slide 25: S4/D7: Detection ratio for different preamble lengths @100 MS/s

## Slide 26: S4/D7: Detection ratio for different preamble lengths @200 MS/s

## Slide 27: AWGN: required SNR vs. preamble length

## Slide 28: S3/D3: required SNR vs. preamble length @3.125 MS/s

## Slide 29: S3/D3: required SNR vs. preamble length @6.25 MS/s

## Slide 30: S3/D3: required SNR vs. preamble length @12.5 MS/s

## Slide 31: S3/D3: required SNR vs. preamble length @25 MS/s

## Slide 32: S3/D3: required SNR vs. preamble length @50 MS/s

## Slide 33: S3/D3: required SNR vs. preamble length @100 MS/s

## Slide 34: S3/D3: required SNR vs. preamble length @200 MS/s

## Slide 35: S4/D7: required SNR vs. preamble length @3.125 MS/s

## Slide 36: S4/D7: required SNR vs. preamble length @6.25 MS/s

## Slide 37: S4/D7: required SNR vs. preamble length @12.5 MS/s

## Slide 38: S4/D7: required SNR vs. preamble length @25 MS/s

## Slide 39: S4/D7: required SNR vs. preamble length @50 MS/s

## Slide 40: S4/D7: required SNR vs. preamble length @100 MS/s

## Slide 41: S4/D7: required SNR vs. preamble length @200 MS/s

## Slide 42: PM PHY: BER vs. SNR PAM-2, bipolar
Notes: Code Rates:
31/23: 0.7419
255/223: 0.8745
255/239: 0.9373

## Slide 43: Summary
Performance of preamble detection has been evaluated
Using AWGN and CIRs in Scenarios 3D3 and 4D7
Detection threshold was selected for 0.1% false positive rate
Results indicate minor impact of channel:
Similar performance for AWGN and Scenario 3D3 up to an OCR of 200 MS/s and for Scenario 4D7 up to 25 MS/s
~ 2dB degradation in Scenario 4D7 at 50 MS/s, no detection for 100 MS/s and 200 MS/s