## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Considerations on general MAC frame]
Date Submitted: [May, 2018]
Source: [John Li] Company [Huawei]
Address []
Voice:[86-15801539749], FAX: [+86-10-82882144], E-Mail:[john.liqiang@huawei.com]
Re: []
Abstract: [In this contribution, we discuss how to unify MAC frame format in 802.15.13]
Purpose: [Contribution to IEEE 802.15.13]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
MAC issues to be resolved
  MAC frame format
    General format
    Format of each frame type
  Security protocol
  Other functionalities such as Coordinated MAC
MAC frame format, what do we have right now
  Frame format from 15.7-2011
  Frame format in Annex H
In this contribution, we try to merge these two MAC frame structure

## Slide 3: General MAC frames
MHR
MSDU
MFR
Frame control
Sequence control
ACK information
Addressing field
Frame payload
FCS
Auxiliary Security header
Proposed general MAC frame format
15.7-2011
Annex H

## Slide 4: Frame control
Frame version
Proposed “frame control” field
Frame type / subtype
The Security Enabled subfield is 1 bit in length, and it shall be set to one if the frame is protected by the MAC sublayer and shall be set to zero otherwise. The Auxiliary Security Header field of the MHR shall be present only if the Security Enabled subfield is set to one.
Security enabled
ACK request
The Acknowledgment Request subfield is 1 bit in length and specifies whether an acknowledgment is required from the recipient device on receipt of a data or MAC command frame.
reserved
15.7-2011
Annex H

## Slide 5: Sequence control
Annex H
15.7-2011
Proposed “sequence control” field
Option 1: One octet
Option 2: Two octet

## Slide 6: ACK information
Proposed “ACK information” field
Device address
[to be confirmed]
Sequence number
ACK
reserved
Annex H

## Slide 7: Addressing field
The Receiver Address field is a 48-bit field indicating the network address of the STA for which the transmitted packet is intended.
The Transmitter Address field is a 48-bit field indicating the network address of the STA transmitting the packet.
The Destination OWPAN Identifier field, when present, is 2 octets in length and specifies the unique OWPAN identifier of the intended recipient of the frame.
The Destination Address field, when present, is either 2 octets or 8 octets in length, according to the value specified in the Destination Addressing Mode subfield of the frame control field, see G.1.1.6, and specifies the address of the intended recipient of the frame.
The Source OWPAN Identifier field, when present, is 2 octets in length and specifies the unique OWPAN identifier of the originator of the frame.
The Source Address field, when present, is either 2 octets or 8 octets in length, according to the value specified in the Source Addressing Mode subfield of the frame control field,
Proposed “Addressing field” field
Destination OWPAN ID (optional)
Destination address
Source OWPAN ID
Source address
15.7-2011
Annex H

## Slide 8: Auxiliary Security header
15.7-2011
15.4-2015

## Slide 9: Frame payload
Please explain ICV and higher layer overhead.
Do we need them?
If we do, where to define them?
Annex H
15.7-2011

## Slide 10: FCS
To be decided: which option to use
Annex H
15.7-2011

## Slide 11: To be decided
Can the proposed general MAC frame format be accepted?
  Yes
Can the proposed frame control format be accepted?
  Yes
Which sequence control format be accepted?
  Option 2: two octets
Can the proposed “ACK information” field be accepted?
  Yes
Can the proposed “Addressing field” be accepted?
  No, for further study
Should we adopt security protocol from 15.4-2015 as an optional feature?
  Yes
Which FCS to be used, four octets or two octets?
  Option 2: with 32 bits