## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Factory Vehicles Collision Avoidance Solutions using OWC Technology
Date Submitted: May 2018
Source: Jaesang Cha(SNUST, VTASK Co., Ltd.), Suhyung Cho(Hans ENS Co., Ltd.), Kirhyong Kim (Seil Technologies Co., Ltd.), Vinayagam Mariappan(SNUST)
Address: Contact Information: +82-2-970-6431, FAX: +82-2-970-6123, E-Mail: chajs@seoultech.ac.kr
Re:
Abstract: This documents introduce the V2X OWC Link design consideration for VAT. This proposed OWC solution helps to design the vehicles collision avoidance solution in factory. This VAT to operate on the application services like ITS, ADAS, etc. on indoor / outdoor road condition. Also this can be used for LED-ID based IoT/IoL, Digital Signage with connected information services etc.
Purpose: To provided concept models of OWC based collision avoidance solution for Vehicular Assistant Technology (VAT) Interest Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2
Contents
Needs for Factory Vehicle Collision Avoidance
OWC Link for Factory Vehicle Collision Avoidance
Conclusion
Slide 2

## Slide 3
OWC Link for Factory Vehicle Collision Avoidance
OWC Link for Factory Vehicle Collision Avoidance
  Tx : Vehicle Lights and Factory Installed lights
  Rx : In-Vehicle Camera and Factory Installed CCTV Camera
  Modulations :
    OOK, VPPM, Offset-VPWM, Multilevel PPM, Inverted PPM, Subcarrier PPM, DSSS SIK etc.
  Data Rate : 1K ~ 1Mb/s
  Supported LoS (Line of Sight)
  Day-Night Communication Mode
  Available Distance : more than 500m with lens
Slide 4

## Slide 4
Conclusion
Proposed the Factory Vehicles Collision Avoidance Solutions using OWC Technology
Utilize the already installed infrastructure in the factory like lighting devices to assign location ID and CCTV to decode the vehicle specific Information
The factory risk detection data is transmitted to the server based on the optical camera, and the server data is transmitted to the factory vehicles through the OWC technology, so that the collision can be prevented.
Slide 5