## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Static Context Header Compression]
Date Submitted: [8 March, 2018]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [Presentation of SCHC for discussion of potential work in TG 802.15.4w]
Purpose: [Presentation in TG 802.15.4w.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Static Context Header Compression (SCHC)
Joerg Robert (University Erlangen-Nuernberg)

## Slide 3: Motivation for SCHC
May IoT applications rely on the use of IPv6
The overhead caused by IPv6 is very significant (>40 bytes), even if the actual payload is only few bytes
Direct transmission of IPv6 over LPWAN not useful
Header compression absolutely necessary for LPWAN

## Slide 4: What is Special about SCHC
“Classical” IP header compression schemes “learn” the compression scheme
  Full IP header is transmitted once, afterwards only the delta is transmitted
Not useful for LPWAN, as overhead is still very significant and “learning” the compression may require multiple L2 packets
SCHC relies on static compression tables and does not learn during operation

## Slide 5: Latest IETF Revision
Latest revision of SCHC is available on the IETF website https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
The document just defines the general framework and leaves many degrees of freedom
Details have to be defined for each standard (e.g. 802.15.4) in implementation specific documents
Just very draft documents exist for other systems (e.g. LoRa)

## Slide 6: Potential Work Related to TG 802.15.4w
SCHC or similar schemes are required to achieve IPv6 connectivity for 802.15.4w
The IETF document only defines the framework, but not the actual implementation
Definition of implementation specific aspects of SCHC should be targeted in 802.15.4w

## Slide 7: Straw Poll
Should TG 802.15.4w take care of the 802.15.4 implementation specific aspects of SCHC?
Y/N/A

## Slide 8: What is Configurable
Number of different rules
Mapping of L2 and IPv6 addresses
Fragmentation
Acknowledgement modes (ACK-0, ACK-1, ACK-2)
DTAG (number of parallel packets)
Retransmission and inactivity timers
Number of MAX_ACK_REQUESTS

## Slide 9: Mapping of L2 and IPv6 Addresses
Do we want to define the mapping of L2 and IPv6 addresses?
Or should this definition be done by the network operator?

## Slide 10: Number of Rules
How many pre-defined rules do we need to compress the data?
How many bits do we have to assign for the specific field?

## Slide 11: Fragmentation
Do we require fragmentation of IPv6 packets into multiple L2 packets?

## Slide 12: Acknowledgement Mode
SCHC currently defines three different acknowledgement modes
The different modes assume different transmission reliabilities of the underlying layers
Should we allow all? Should we just select the No-Ack mode?

## Slide 13: DTAG
Do we require interleaving of multiple IPv6 packets?
  Transmission of IPv6 packet can be interrupted for other IPv6 packets
  Potential application if the transmission of “low latency” packets
However: DTAG would increase implementation complexity

## Slide 14: Timers and Max. Retries
Should we specify typical values for the timers and the max. number of retries?
Heavily depends on available payload bit-rate

## Slide 15: Possible Next Steps
Do we have to define typical application scenarios?
Should we provide input to IETF?
Who would take care of editing an implementation specific proposal?
...

## Slide 16: Thank You for Your Interest!