## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Coding example for the ULI
Date Submitted: 8 May, 2018
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: Hello world examples for ULI
Abstract:
Provide example how the ULI could be configured to send packet out.
Purpose: Provide example.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Code example for ULI
Tero Kivinen

## Slide 3
Example 1
Sending one IPv6 packet using O-QPSK on 2.4 MHz band using channel 1.
Use the Pan Id of 0x1234.
First send packet without security

## Slide 4
Creating PHY & MAC configuration
First we need to create configuration data for the phy & mac layer, i.e., something we can give to the PDE-MGMT-CREATE. The configuration could be Yang or some other format.

## Slide 5
Creating PHY & MAC configuration
PdeMgmtPhyConfig =
  pack(
    Phy: {
      Phy: O-QPSK,
      Band_designator: 2.4Ghz,
      Channel: 1 },
    Mac: {
      Pan_Id: 0x1234
    })

## Slide 6
Creating the profile id
Request the MPM to create a new profile based on our phy data.
PDE-MGMT-CREATE.request(
  PdeMgmtPhyConfig,
  &Handle)

## Slide 7
Getting the profile id back
MPM will allocate new profile id and configure it using the configuration data given, and return newly allocated profile id to the upper layer
→ PDE-MGMT-CREATE.confirm(
    Handle,
    &UliPhyProfileId)

## Slide 8
Sending packet
Now we have the profile id containing all the phy and mac layer settings, so we can use it to send packet to given destination.
PDE-DATA.request(
  0x123456789abcdef, # Dst Address
  0x86dd, # IPv6 Ethertype
  UliPhyProfileId, # Profile id to use
  PdeData, # IPv6 payload
  &Handle)

## Slide 9
Example 2
Same as before, but now enable KMP using IKEv2, and PSK.

## Slide 10
Creating KMP configuration
PdeMgmtKmpConfig = pack(
  Kmp: {
    KmpProtocol: IKEv2,
    PeerTable [ { # Host A
      address: 0x123456789abcdef,
      PSK: MakeMeTastyGoat
    }, { # Another host
      address: 0xac00000012345678,
      PSK: Foobar
    } ]
  })

## Slide 11
Now create new profile for KMP
PDE-MGMT-CREATE.request(
  PdeMgmtPhyConfig,
  &Handle)
→ PDE-MGMT-CREATE.confirm(
    Handle,
    &UliKmpProfileId)

## Slide 12
Combine two profiles
PDE-MGMT-COMBINE.request(
  UliPhyProfileId,
  UliKmpProfileId,
  &Handle)
→ PDE-MGMT-COMBINE.confirm(
    Handle,
    &UliCombinedProfileId)

## Slide 13
Sending packet
Now we have the profile id containing all the phy, mac and kmp layer settings, so we can use it to send packet to given destination.
PDE-DATA.request(
  0x123456789abcdef, # Dst Address
  0x86dd, # IPv6 Ethertype
  UliCombinedProfileId, # Profile id to use
  PdeData, # IPv6 payload
  &Handle)