## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discussion on Suitable Parameters for SCHC]
Date Submitted: [9 March, 2018]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [Presentation of SCHC for discussion within TG]
Purpose: [Presentation in TG 802.15.4w]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Discussion on Suitable Parameters for SCHC
Joerg Robert (University Erlangen-Nuernberg)

## Slide 3: Motivation
Discussion of technology specific SCHC parameters, as SCHC itself only defines a framework
Technology specific parameters are listed on the IETF LPWAN e-mail reflector (listed on next slides) https://mailarchive.ietf.org/arch/msg/lp-wan/SexnleQwBTL7XZ9-hC2h7tp79KU
Latest version of SCHC draft is available on the IETF website https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/

## Slide 4: List of Technology Specific Parameters
In the architecture explain the SCHC entities, how they will be represented in the corresponding technology architecture.
How to learn the context
Size of the Rule id
The way the Rule id is sent (L2 or L3) and how (describe)
Use of padding and how and when to use it
Fragmentation delivery reliability option used over your technology and why
Define the MAX_ACK_REQUEST
Define the number of bits needed for Rule-id, FCN (N) and DTag (T)

## Slide 5: List of Technology Specific Parameters (Cont’d)
The algorithm to be used for the MIC if it is different from the default
The timer size for Fragmentation ACK always
When to abort in ACK always
MAX_ATTEMPS counter size
In ACK on error the timer size between windows
The L2 CRC used to increase reliability

## Slide 6: IG LPWA Use-Cases
The Interest Group LPWA listed different use-cases that may be relevant for LPWAN in 15-16/770r5 https://mentor.ieee.org/802.15/dcn/16/15-16-0770-05-lpwa-lpwa-use-cases.xlsx
According to the discussed use-cases the typical LPWAN use-case has the following parameters
  Focusing on uplink data
  Typical Payload data length <= 16 bytes
  No strict latency requirements
Use-cases with longer payload data an higher bit-rate requirements may employ existing header compression schemes

## Slide 7: Open Questions
Who triggers the data transmission
  Initiated by LPWAN sensor node?
  REST model? (e.g. CoAP)
Do we assume uplink-only devices?
How many different IPv6 addresses are contacted by a LPWAN sensor node?
  Do we use different UDP ports?
  Do we use different protocols? What kind of protocols?
What is the maximum PSDU length?

## Slide 8: Working Assumptions
The following slides will define working assumptions for the different parameters in order to reflect the TG discussions
The idea is to be able to specify the requirements for the technology specific parameters

## Slide 9: Potentially Used IPv6 Protocols

## Slide 10: Number of Different Rule ID

## Slide 11: Fragmentation

## Slide 12: Fragmentation Acknowledgement Mode

## Slide 13: DTAG

## Slide 14: Device IPv6 Address Mapping

## Slide 15: Thank You for Your Interest!