## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discussion on Suitable Parameters for SCHC]
Date Submitted: [9 March, 2018]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [Presentation of SCHC for discussion within TG]
Purpose: [Presentation in TG 802.15.4w]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Discussion on Suitable Parameters for SCHC
Joerg Robert (University Erlangen-Nuernberg)

## Slide 3: Motivation
Discussion of technology specific SCHC parameters, as SCHC itself only defines a framework
Technology specific parameters are listed on the IETF LPWAN e-mail reflector (listed on next slides) https://mailarchive.ietf.org/arch/msg/lp-wan/SexnleQwBTL7XZ9-hC2h7tp79KU
Latest version of SCHC draft is available on the IETF website https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/

## Slide 4: List of Technology Specific Parameters
In the architecture explain the SCHC entities, how they will be represented in the corresponding technology architecture.
How to learn the context
Size of the Rule id
The way the Rule id is sent (L2 or L3) and how (describe)
Use of padding and how and when to use it
Fragmentation delivery reliability option used over your technology and why
Define the MAX_ACK_REQUEST
Define the number of bits needed for Rule-id, FCN (N) and DTag (T)

## Slide 5: List of Technology Specific Parameters (Cont’d)
The algorithm to be used for the MIC if it is different from the default
The timer size for Fragmentation ACK always
When to abort in ACK always
MAX_ATTEMPS counter size
In ACK on error the timer size between windows
The L2 CRC used to increase reliability

## Slide 6: IG LPWA Use-Cases
The Interest Group LPWA listed different use-cases that may be relevant for LPWAN in 15-16/770r5 https://mentor.ieee.org/802.15/dcn/16/15-16-0770-05-lpwa-lpwa-use-cases.xlsx
According to the discussed use-cases the typical LPWAN use-case has the following parameters
  Focusing on uplink data
  Typical Payload data length <= 16 bytes
  No strict latency requirements
Use-cases with longer payload data an higher bit-rate requirements may employ existing header compression schemes

## Slide 7: Open Questions
Who triggers the data transmission
  Initiated by LPWAN sensor node?
  REST model? (e.g. CoAP)
Do we assume uplink-only devices?
How many different IPv6 addresses are contacted by a LPWAN sensor node?
  Do we use different UDP ports?
  Do we use different protocols? What kind of protocols?
What is the maximum PSDU length?
Can we identify fields in the MAC header that we do not require?

## Slide 8: Working Assumptions
The following slides will define working assumptions for the different parameters in order to reflect the TG discussions
The idea is to be able to specify the requirements for the technology specific parameters

## Slide 9: MAC Header Compression
All parameters that are identical could be compressed, e.g.
  MAC address (TX or RX)
Parameters such as the time, frequency, or spreading code in case of DSSS could be used to identify the device
Additional work is needed to indicate how MAC parameters could be compressed in real applications

## Slide 10: Potentially Used IPv6 Protocols
LPWAN sensor nodes may have to be able to support multiple protocols, e.g.
  CoAP, MQTT
The protocols typically operate using UDP
Also REST models should be supported

## Slide 11: Number of Different Rule ID
LPWAN devices may have to support different protocols (e.g. CoAP, MQTT)
Typical LPWAN devices may have to be able to contact several IPv6 addresses
Typical configuration may require up to 8 different Rule ID  3 bits

## Slide 12: Fragmentation
Only LECIM DSSS PHY offers PHY fragmentation
SCHC fragmentation has to be used for current 802.15.4 systems (exception LECIM DSSS)

## Slide 13: Fragmentation Acknowledgement Mode
Layer 2 should do the acknowledgment because it offers higher energy efficiency
Use of No-ACK mode in addition to L2 acknowledgement should ensure the require reliability
Only use of No-ACK mode
No SCHC ACK packets required

## Slide 14: DTAG (Datagram Tag)
DTAG enables interleaving of multiple IPv6 fragments
Use of DTAG increases LPWAN sensor node complexity
No clear use-case found
No use of DTAG, i.e. DTAG is encoded with 0 bits
Similar functionality can be achieved by frame aborts

## Slide 15: Device IPv6 Address Mapping
The group agreed that the mapping between IPv6 and MAC addresses should be left to the network operator

## Slide 16: MIC (Message Integrity Check)
In case of SCHC fragmentation a MIC is required
CRC-16 or CRC-32 as defined in 802.15.4 could be used
Any suggestion?

## Slide 17: Resulting SCHC Parameters (Working Assumption)
Parameter | Value
Size of Rule ID | 3 bits
Fragmentation delivery reliability | No-ACK mode
DTAG | 0 bits (not used)
FCN | 1 bit
MIC | CRC-16/CRC-32
Retransmission Timer | N/A
Inactivity Timer | N/A
MAX_ACK_REQUESTS | N/A
MAX_WIND_FCN | N/A

## Slide 18: Thank You for Your Interest!