## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposal of modification of general MAC format
Date Submitted: 4 June 2018
Source: Nikola Serafimovski, Chong Han, Stephan Berner, Mostafa Afgani (pureLiFi)
Address: 9 Haymarket Terrace, Edinburgh, UK, EH12 5EZ
Mobile:[+44-7503016565], E-Mail:[chong.han@purelifi.com]
Re:
Abstract: Proposal of modification of general MAC format
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal of modification of general MAC format
Nikola Serafimovski (pureLiFi), Chong Han (pureLiFi), Stephan Berner (pureLiFi), Mostafa Afgani (pureLiFi)

## Slide 3
General MAC format
Proposal
Octets: 2 | 2 | 6 | 6 | 6 | 2 | 6 | 0/5/6/10/14 | variable | 4
Frame Control | ACK information | Receiver Address | Transmitter Address | Destination Address | Sequence Control | Source Address | Auxiliary security header | Frame Body | FCS
From the last meeting
Frame Control | Sequence Control | Ack information | Addressing field | Auxiliary security header (optional) | Frame Body | FCS
‘Addressing field’
  The field was subject to further study in the meeting at Warsaw.
  The field shall consist of RA, TA as well as DA and SA to perform relay function.
Adjust the position of ‘Sequence Control’
  Sequence Control is allocated after DA in order to improve efficiency. Device is capable to ignore the rest of the frame if the device detects the RA, TA and DA and finds irrelevance.
Notes: PHY header: 2 OFDM symbols after applying Hermitian symmetry.

## Slide 4
Frame Control field
Add ‘To DS’ and ‘From DS’ subfields
  The two subfields are needed to indicate if the transmission of frame involves Extended Service Set (ESS). ESS is the basic scenario required by TG13.
Add ‘Relay mode enabled’ subfield
  This subfield relates to DA and SA in the general MAC format. It could be removed if DA and SA are permanently inserted in general MAC format. Otherwise, it is used to indicate if relay mode is relevant.
Bits: 2 | 2 | 4 | 1 | 1 | 1 | 1 | 1 | 3
Frame Version | Type | Sub-type | To DS | From DS | Security enabled | ACK request | Relay mode enabled | Reserved
From the last meeting
Proposal
Bits: 2 | 2 | 4 | 1 | 1 | 6
Frame Version | Type | Sub-type | Security enabled | ACK request | Reserved