## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Explanations to subfields in Frame Control
Date Submitted: 18 June 2018
Source: Nikola Serafimovski, Chong Han, Stephan Berner, Mostafa Afgani (pureLiFi)
Address: 9 Haymarket Terrace, Edinburgh, UK, EH12 5EZ
Mobile:[+44-7503016565], E-Mail:[chong.han@purelifi.com]
Re:
Abstract: Explanations to subfields (i.e., To DS and From DS) in Frame Control
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Explanations to subfields in Frame Control
Nikola Serafimovski (pureLiFi), Chong Han (pureLiFi), Stephan Berner (pureLiFi), Mostafa Afgani (pureLiFi)

## Slide 3
Frame Control field
‘To DS’ and ‘From DS’ subfields
  The two subfields are needed to indicate if the frame is entering or leaving the wireless environment. The combinations of these two subfields reflect which address fields out of the four (RA, TA, DA and SA) are required by the frame.
Bits: 2 | 2 | 4 | 1 | 1 | 1 | 1 | 1 | 3
Frame Version | Type | Sub-type | To DS | From DS | Security enabled | ACK request | ACK info | Reserved
From the last meeting
Proposal
Bits: 2 | 2 | 4 | 1 | 1 | 6
Frame Version | Type | Sub-type | Security enabled | ACK request | Reserved

## Slide 4
Combinations of subfields (1)
Scenario 1:
Example 1) Device a sends a data frame to the destination Device b; 2) or Device a sends a data frame to Coordinator.
1) Frame control: … To DS=0; From DS=0; …
MAC header: …, RA=b, TA=a, A1=OWPAN ID, …
2) Frame control: … To DS=0; From DS=0; …
MAC header: …, RA=c, TA=a, A1=OWPAN ID, …
a
b
c
Scenario | To DS | From DS | Meaning | Receiver address | Transmitter address | Auxiliary address 1 | Auxiliary address 2
1 | 0 | 0 | A Data frame from one device to another device within the same local network | RA=DA | TA=SA | OWPAN ID | -
2 | 1 | 0 | A Data frame destined for the DS | OWPAN ID | TA=SA | DA | -
3 | 0 | 1 | A Data frame exiting the DS | RA=DA | OWPAN ID | SA | -
4 | 1 | 1 | Reserved | - | - | - | -

## Slide 5
Combinations of subfields (2)
Scenario 2:
Device a sends a data frame (e.g., request for IP address) to the destination d in the DS via Coordinator c.
Frame control: … To DS=1; From DS=0; …
MAC header: …, RA=OWPAN ID, TA=SA=a, A1=DA=d, …
a
Distribution System
d
c
Scenario | To DS | From DS | Meaning | Receiver address | Transmitter address | Auxiliary address 1 | Auxiliary address 2
1 | 0 | 0 | A Data frame from one device to another device within the same local network | RA=DA | TA=SA | OWPAN ID | -
2 | 1 | 0 | A Data frame destined for the DS | OWPAN ID | TA=SA | DA | -
3 | 0 | 1 | A Data frame exiting the DS | RA=DA | OWPAN ID | SA | -
4 | 1 | 1 | Reserved | - | - | - | -

## Slide 6
Combinations of subfields (3)
Scenario 3:
The packet is entering the wireless environment coming from the DS. DS sends a data frame to the destination Device a via Coordinator c.
Frame control: … To DS=0; From DS=1; …
MAC header: …, RA=DA=a, TA=OWPAN ID, A1=SA=d, …
a
Distribution System
d
c
Scenario | To DS | From DS | Meaning | Receiver address | Transmitter address | Auxiliary address 1 | Auxiliary address 2
1 | 0 | 0 | A Data frame from one device to another device within the same local network | RA=DA | TA=SA | OWPAN ID | -
2 | 1 | 0 | A Data frame destined for the DS | OWPAN ID | TA=SA | DA | -
3 | 0 | 1 | A Data frame exiting the DS | RA=DA | OWPAN ID | SA | -
4 | 1 | 1 | Reserved | - | - | - | -