## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal of LDPC (Low Density Parity Code) for LPWA]
Date Submitted: [6 July, 2018]
Source: [Seiji Kobayashi] Company [Sony Semiconductor Solutions Corporation]
Address [Astugi Tec. No2, 4-16-1 Okata, Atsugi-shi Kanagawa, 243-0021 Japan]
Voice:[+81 80 9976 0007], FAX: [+81 50 3809 1781], E-Mail:[Seiji.Kobayashi@sony.com]
Re: [IEEE P802.15.4w Low Power Wide Area Call for Proposals, 12 March 2018]
Abstract: [LDPC (Low Density Parity Code) as a Forward Error Correction.]
Purpose: [Contribution to IEEE 802.15.4w.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposal of LDPC (Low Density Parity Code) for LPWA
Seiji Kobayashi (Sony Semiconductor Solutions Corporation), Nabil Loghin (Sony European Technology Center, Stuttgart, Germany) and Ryoji Ikegaya (Sony Semiconductor Solutions Corporation)

## Slide 3
802.15.4k Forward Error Correction
Rate ½ convolutional coding with constraint length K = 7 has been specified in 802.15.4k.
In a practical implimentation, additional 6 bits are needed as a purpose of “termination”, which increases redundancy. 6bits of redundant information is not negligible for a system with small-size payload.
Current FEC scheme
uk-1
uk-2
uk-3
uk-4
uk-5
uk-6
uk
+
+
+
+
+
+
+
+
ak
ak
1
0

## Slide 4
LDPC (Rate ¼) performance comparison
In an example shown above, the LDPC (Rate ¼) outperforms 1.2dB (at BER=10-4 ) against Rate ½ convolutional code.
Reference: “A GPS Synchronized, Long-Range Uplink-Only Radio Designed for IoT,“ ICC2018 (SAC-IoT 01)
1.2dB

## Slide 5
LDPC Rate (1/4) for 802.15.4w
Porposal
Row and col index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 1 | 7 | 90 | 172 | 209 | 359 | 401 | 420 | 483 | 487
2 | 57 | 164 | 192 | 197 | 284 | 307 | 174 | 356 | 408 | 425
3 | 22 | 50 | 191 | 379 | 385 | 396 | 427 | 445 | 480 | 543
4 | 32 | 49 | 71 | 234 | 255 | 286 | 297 | 312 | 537 | 550
5 | 30 | 70 | 88 | 111 | 176 | 201 | 283 | 322 | 419 | 499
6 | 86 | 94 | 177 | 193 | 266 | 368 | 373 | 389 | 475 | 529
7 | 134 | 223 | 242 | 254 | 285 | 319 | 403 | 496 | 503 | 534
8 | 18 | 84 | 106 | 165 | 170 | 199 | 321 | 355 | 386 | 410
9 | 129 | 158 | 226 | 269 | 288 | 316 | 397 | 413 | 444 | 549
10 | 33 | 113 | 133 | 194 | 256 | 305 | 318 | 380 | 507 | 
11 | 317 | 354 | 402 |  |  |  |  |  |  | 
12 | 53 | 64 | 374 |  |  |  |  |  |  | 
13 | 83 | 314 | 378 |  |  |  |  |  |  | 
14 | 162 | 259 | 280 |  |  |  |  |  |  | 
15 | 166 | 281 | 486 |  |  |  |  |  |  | 
16 | 185 | 439 | 489 |  |  |  |  |  |  | 
17 | 119 | 156 | 224 |  |  |  |  |  |  | 
18 | 26 | 62 | 244 |  |  |  |  |  |  | 
19 | 8 | 246 | 482 |  |  |  |  |  |  | 
20 | 15 | 72 | 91 |  |  |  |  |  |  | 
21 | 43 | 69 | 390 |  |  |  |  |  |  | 
22 | 127 | 186 | 506 |  |  |  |  |  |  | 
23 | 55 | 81 | 412 |  |  |  |  |  |  | 
The table

## Slide 6
LPDC code with rate R=1/4 shall be applied to form Coded Block size of =4* where = SizeMPDU, i.e. 184-bit.
Input: 184 bits, denoted as with Kldpc = 184 Output: 736 code bits, denoted as , with Nldpc = 736 and Mldpc = 552. A systematic binary LDPC code with quasi-cyclic structure (information part) and dual staircase (parity part) shall be used, i.e., parities shall be accumulated (see below). Encoding shall be performed as follows:
First: Kldpc = 184 parities shall equal information bits:
Initialize:
Accumulate the first information bit, i0, at parity bit addresses specified in the first row of Table shown in previous page. For example, (all additions are in GF(2)):
For the next 7 information bits, im, m =1, 2, ..., 7, accumulate im at parity bit addresses [x + (m mod 8)×Qldpc] mod Mldpc, where x denotes the address of the parity bit accumulator corresponding to the first bit i0, and Qldpc = 69. So for example for information bit i1, the following operations are performed:
For the 9th information bit i8, the addresses of the parity bit accumulators are given in the second row of Table 5‑7. In a similar manner the addresses of the parity bit accumulators for the following 7 information bits im, m = 9, 10, ..., 15 are obtained using the formula [ x + (m mod 8)×Qldpc] mod Mldpc, where x denotes the address of the parity bit accumulator corresponding to the information bit i8 , i.e. the entries in the second row of Table 5‑7.
In a similar manner, for every group of 8 new information bits, a new row from the Table 5‑7 is used to find the addresses of the parity bit accumulators.
After all of the information bits are exhausted, the final parity bits shall be obtained by accumulation as follows:
Sequentially perform the following operations starting with i = 1:
Mldpc −1
Final content of pi , i = 0, 1,.., Mldpc −1 is equal to the parity bit pi.

## Slide 7: Encoder Complexity
Reference: Convolutional Code of memory 6 (133,171)
  184 info bits, 5 elements in mod-2 addition per code bit:
    (184+6)*(5-1 + 5-1)= 1.5k metrics
LDPC, CR 1/4
  552 parities, average check node degree 3 (3 elements in mod-2 additions)
  552*(3-1) = 1.1k metrics

## Slide 8: Consideration of TSMA in Japanese Regulation
0
3
2.5
2
1.5
1
0.5
time [sec] 
0
2
4
6
8
10
12
14
16
18
20
22
frequency channel 
3.5
Reference:.: IEEE 802.15-18-0310-01-004w “Initial proposal preview from Fraunhofer IIS for 802.15.4w”,
A radio channel shall consist of up to 5 consecutive unit radio channels which are defined that their center frequencies are located from 916.0 MHz to 916.8 MHz and from 920.6 MHz to 928.0 MHz with 200 kHz separation and their bandwidth are 200 kHz
ARIB STD T-108 (Version 1*)
200kHz
200kHz
2.3kHz
* Ver 1.2 has been issued recently (English version is not yet available.)

## Slide 9
Further possibilities
Extension of LDPC for longer MSDU sizes.
MAC format
  Fragmentation, Variable length payload, Headder
FSK modulation method.
Pre-amble and Sync for synchronization