## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal to 15.4z for enhancing UWB PHYs]
Date Submitted: [July 6, 2018]
Source: [Huan-Bang Li, Kenichi Takizawa, and Fumihide Kojima] Company [NICT, Japan]
[Hisashi Nishikawa] Company[Global Interface Technologies Japan Inc.]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
[590 Nojiri, Rittoh-shi, Siga, Japan]
Voice:[-], E-Mail:[lee (at) nict.go.jp]
Re: [Proposed changes to IEEE802.15.4-2015 for enhancing UWB PHYs]
Abstract: [Contribute a proposal to the enhanced impulse radio group 15.4z]
Purpose: [Propose the modifications of the HRP as well as LRP UWB PHYs]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposal to 15.4z for enhancing UWB PHYs

## Slide 3: ToC
Background/Motivation
Modulation Proposal for HRP UWB PHY
Band plan proposal for LRP UWB PHY

## Slide 4: Background
IEEE Std 802.15.4™-2015 includes two IR-UWB based PHY specifications with supporting MAC features.
  HRP UWB PHY (IEEE Std 802.15.4a – 2007)
  LRP UWB PHY (IEEE Std 802.15.4f – 2012)
Both were developed for low-rate WPAN with consideration/emphasis on ranging capbility.
Operating frequency bands
  HRP UWB PHY: low band and high band
  LPR UWB PHY: high band only

## Slide 5: Motivations
IR-UWB Ranging has different requirement/emphasis on PHY compared to communication.
Enhancing ranging capbility by modifying or expanding existing features of IR-UWB PHY in IEEE Std 802.15.4™-2015 .
Proposals are presented respectively for HRP UWB as well as for LRP UWB.
Harmonization with other proposals.

## Slide 6: Modulation Features of HRP UWB
Coherent (BPM+BPSK) for better performance.
Non-coherent (BPM) for simple structure.
00 | 0 -
01 | 0 -
10 | 1 -
11 | 1 -
0
1
31
32
33
63
15
16
47
48
0
1
31
32
33
63
15
16
47
48
0
1
31
32
33
63
15
16
47
48
0
1
31
32
33
63
15
16
47
48
S
-S
S
-S
coherent
シンボル間ガード区間
Non-coherent
Scramble interval
Guard interval
T/2
T/2
BPM+BPSK

## Slide 7: HRP UWB Improvement Proposal
OOK for simple structure.
BPSK for better performance
0
1
31
32
15
16
0
1
31
32
15
16
0
1
31
32
15
16
0
1
31
32
63
15
16
S
S
-S
Guard interval
1T
2T
OOK
BPSK

## Slide 8: HRP UWB Improvement Proposal (Cnt’d)
OOK or BPSK pulses
OOK or BPSK pulses
Add OOK – BPSK mode to Figure. 16-3
Figure 16-3—HRP UWB PHY symbol structure

## Slide 9: HRP UWB Improvement Proposal (Cnt’d)
Add a new ranging mode by replacing BPM+BPSK with an OOK and a BPSK, where OOK and BPSK are two seperated modulation options.
  Choose OOK for simlicity (reduce cost and power consumption)
  Choose BPSK for better performance
Cut the symbol duration by half to reduce the ToF
  Shortening TOA ranging time to save power
  Increase system capacity

## Slide 10: Large Bandwidth Features of LRP UWB
LRP UWB only uses high band with large bandwidth.
  Favorable for compansating distance loss compared to low band
  Ranging-favorited because of inherent high precision of time resolution
Adopted high bands are not comprehensive
  Only focus on 6 – 9 GHz
  Beyond 9 GHz is not included

## Slide 11
LRP UWB Improvement Proposal
3 | 8486.4
Add channel number 3 to Table 10-9 to effectively use beyond 9GHz
Notes: 19.7.3 LPR UWB PHY PSD mask
IEEE802.15.4-2015

## Slide 12
LRP UWB Improvement Proposal (Cnt’d)
3 | 8486.4 | <7587.84 | -18
 |  | 7587.84 to 7662.72 | -10
 |  | 7662.72 to 9809.28 | 0
 |  | 9809.28 to 9884.16 | -10
 |  | > 9884.16 | -18
Add PSD mask for channel number 3 to Table 19-9
Notes: 19.7.3 LPR UWB PHY PSD mask
IEEE802.15.4-2015

## Slide 13
LRP UWB Improvement Proposal (Cnt’d)
Add PSD mask illustration for channel number 3 to Figure 19-7
PSD mask satisfies Japan and Korea

## Slide 14: Harmonization With HRP Band Plan
LRP UWB Improvement Proposal (Cnt’d)
LRP Band number | HRP Band plan
0 | Ch.7
1 | Ch. 5, 6, 8, 9
2 | Ch.11
3 | Ch. 9, 10, 12, 13

## Slide 15: Reference Slides

## Slide 16
HRP Band Plan

## Slide 17
16.4.6 Transmit PSD mask
Calculation of PSD Mask