## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Extensions to IEEE 802.15.9 in support of 4y]
Date Submitted: [9 July, 2018]
Source: [Don Sturek] Company [Itron]
Address [230 W. Tasman Drive, San Jose, CA 95134]
Voice:[+1 669 770 4790], FAX: [+1 866 776 0015], E-Mail:[don.sturek@itron.com]
Re: [IEEE 802.15 WNG]
Abstract: [Contains a proposal for extensions to IEEE 802.15.9 in support of 4y]
Purpose: [Contains a proposal for extensions to IEEE 802.15.9 in support of 4y]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15 WNG July 2018
Don Sturek Itron

## Slide 3: Proposed 15.9 Amendment
Background:
  IEEE 802.15.9-2016 supports Key Establishment protocols over IEEE 802.15.4
  15.9 Annexes A-E describe specific Key Establishment protocols. Only Annex B on IKEv2 actually describes how to take the key material generated to derive a traffic key (needed for IEEE 802.15.4)
  SECN will allow for creation of traffic keys of different lengths using a variety of algorithms. Need to accommodate in 15.9 Annexes A-E
  Broadcast/multicast key generation and distribution in 15.9 should be addressed (only mentioned in Annex B now)

## Slide 4: Proposed 15.9 Amendment
Proposed Work Plan:
  Create a SG or WG to create the amendment
  Address the notion of algorithm selection
  Include requirements to address traffic key derivation from key material for 128, 192 and 256 bit traffic keys at a minimum (for each of 15.9 Annexes A-E)
  Address broadcast/multicast key derivation and distribution
  No other errata to date reported for 15.9-2016 (and at least in Wi-SUN we are using 15.9 extensively, particularly the MPX-IE and Annex A)