## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY/MAC functional description changes for Secure Authenticated Ranging]
Date Submitted: [6 July 2018]
Source: Prof. Dr. Srdjan Capkun (ETH Zurich), Prof. Dr. David Basin (ETH Zurich), Dr. Boris Danev (3db Access), Prof. Dr. Markus Kuhn (University of Cambridge), Shuiping Long (Huawei Technologies), Yunsong Yang (Huawei Technologies), Bernd Baer (Marquardt), Matthias Reinhardt (Daimler), [Ed Richley (Zebra Technologies)], Andy Ward (Ubisense), Peter Sauer (Microchip Technology), Paul Studerus (Dormakaba), Mihai Barbulescu (Dormakaba)
Re: [Changes proposal for the LRP UWB PHY]
Abstract: [Contribute a proposal to the enhanced impulse radio group w.r.t. the LRP UWB PHY ]
Purpose: [Propose elements of Secure Authenticated Ranging PHY/MAC descriptions 802.15.4z]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ToC
Scope
Motivation
Concepts
MAC functional descriptions for secure authenticated ranging
Summary
Future evolution

## Slide 3: Scope
Provably secure authenticated ranging for:
Mobile payments
Corporate and Home Buildings access control
Vehicle access control
Cryptographic device authentication combined with secure distance measurement (e.g., Banking transactions, Bitcoin location)
Provably secure authenticated ranging is only achievable by a set of PHY, for which energy carrying information is constrained on the shortest possible time period (such as LRP UWB PHYs).
Ultimate security measure against all known logical and physical-layer relay attacks!

## Slide 4: Scope
  Strong market demand across all verticals for:
  Low cost of ownership
  (minimum size and BOM)
  Ultra-low power consumption (coin cell battery, several years of battery life)
  Low complexity and easy set-up (robust design and tolerance to different propagation environments)
  Provable security (formally proven under state-of-art cryptographic models for worldwide industry adoption)

## Slide 5: Motivation
  Secure authenticated ranging using LRP UWB perfectly builds on legacy IEEE 802.15.4 Security
Fully complies with 802.15.4 Security as defined in Clause 9
Uses the security services as defined Clause 9
Matches the security levels defined in Clause 9
Provides the strongest security guarantees using one-way and mutual authentication
    Current state of the art in industrial security standards worldwide!
Ensures evolution towards stronger AES-256 shared cryptography and public/private key (PK) cryptography
    Future trend in all security standards
Formal proof

## Slide 6: Concepts (1/3)
  Secure authenticated ranging relies on 2 fundamental concepts
Secure authentication protocol (MAC layer)
Distance commitment principle (PHY layer)

## Slide 7: Concepts (2/3)
  Secure authentication protocol
  Challenge and Response
    Nonce
      Freshly generated random number (e.g., 128 bits)
    Cryptographic function
      Encryption (e.g., AES), Authentication (e.g., SHA)
Alice
Bob
Challenge (Nonce)
Response (Cryptographic function)

## Slide 8: Concepts (3/3)
  Distance commitment principle
    The sender claims to be in a certain distance by the transmission time of the preamble
    The exact arrival time of the preamble at the receiver tells the receiver when to sample the signal in order to demodulate the MAC payload symbols carrying the secure data of the authentication protocol
  Distance commitment provides the strongest security guarantees against all physical layer attacks such as Early-detect and Late-commit.
    Annex G provides the worst case maximum distance decrease

## Slide 9: MAC functional description changes for secure authenticated ranging
  Specify provably secure authenticated ranging in two modes:
  Secure ranging with one-way authentication
  Secure ranging with mutual authentication
  Provide formal security guarantees and proofs
  Annex G

## Slide 10: Secure ranging (1/7)
Purpose: A new MAC functional description is required for provably secure authenticated ranging
    Open Clause 6 in order to introduce a new subclause 6.17 “Secure authenticated ranging”
    Create Annex G (normative) in order to describe the security guarantees and provide the corresponding formal proofs
  Clause 6.17 named “Secure authenticated ranging” includes
    6.17 Secure authenticated ranging
    6.17.1 Secure ranging with one-way authentication
    6.17.2 Secure ranging with mutual authentication
    6.17.3 Distance commitment
    6.17.4 Protocol verification procedure

## Slide 11: Secure ranging (2/7)
    Security services
      Uses the security services for data authenticity defined in Clause 9
      Based on AES-128 CCM* as defined in Clause 9 and Annex B
    MAC frame format
      Uses the MAC data format for security
      macSecurityEnabled shall be set to TRUE
    Need of additional IEs for secure ranging modes ?
      Define two modes of operation: one-way and mutual authentication

## Slide 12: Secure ranging (3/7)
    With one-way authentication
      Generic access control where one party is authenticated
      Described in detail in 6.17.1

## Slide 13: Secure ranging (4/7)
    With mutual authentication
      Mobile payments, banking transactions, high security access control
      Described in detail in 6.17.2

## Slide 14: Secure ranging (5/7)
    Distance commitment
      Ensures that the PSDU carrying the nonces and MIC is decoded at the measured distance defined by the first path. This is essential to secure ranging and provable security as defined in Annex G.
      Described in detail in 6.17.3

## Slide 15: Secure ranging (6/7)
    Protocol verification procedure
      Received nonce(s) have to match
      Computed MIC(s) have to match
      Described in detail in 6.17.4
    Use of shared secret keys
      Mandate the use of link keys (i.e., pair-wise shared keys) between devices

## Slide 16: Secure ranging (7/7)
    Annex G (normative) Security guarantees of secure authenticated ranging
      Provides the formal proofs
      Summary Table 1 of security guarantees
      Full security proofs and publication references in Annex G
Security Level | Nonce length (bits) | Probability of guessing the nonce | Forging of MIC (as per AES CCM* in Clause 9) | Worst Case Maximum Distance Decrease
0 | N/A | N/A | N/A | N/A
1 | 32 | 1/2^32 (2.32e-10) | MIC-32 | 14 cm – 75 cm
2 | 64 | 1/2^64 (5.42e-20) | MIC-64 | 14 cm – 75 cm
3 | 128 | 1/2^128 (2.93e-39) | MIC-128 | 14 cm – 75 cm

## Slide 17: Optimal energy vs. security by LRP UWB
100
300
400
500
Total secure ranging
duration [us]
Authentication strength [Probability of forging the crypto authentication result]
1e-10
1e-20
1e-30
1e-40
40
30
20
10
5
Total secure ranging
energy [uJ]
200

## Slide 18: Summary
    We proposed a new MAC functional description for provably secure ranging in two modes
      One-way authentication and mutual authentication
    Proposed provably secure ranging builds on the available security services of 802.15.4 for data authenticity
    It provides the highest state-of-art security guarantees for scalability and worldwide industry adoption
    Annex G provides the security guarantees and formal proofs
    Extended Mode can also be secured

## Slide 19: Future evolution
    Wireless security standards evolve (e.g., NFC, 802.11)
      Shared cryptography will evolve to AES-256
      Public/private key cryptography is becoming more spread
    Assuming next generation 802.15.4 will support AES-256 and/or public/private key cryptography
      The proposed secure authenticated ranging can be simply used with public key signatures, replacing MICs
    Proposed secure authenticated ranging is build to evolve according to future security trends and worldwide industry adoption

## Slide 20: Q & A

## Slide 21: Secure ranging with pre-synchronization
    VNonce and PNonce are preshared and known to P and V
      Nonces are used only once for ranging (can be derived from shared keys and counters)
      Given that nonces are preshared, V and P can tolerate high BER.
      E.g., even if 90% of the VNonce and PNonce match, V and P can still accept the ranging as secure with very strong guarantees => Scheme provides configurable robustness to bit (pulse) loss
PNonce

## Slide 22: Secure ranging with pre-synchronization
    The scheme provides configurable robustness to cryptographic information bit loss
      Gain from BER of 0.1% to BER of 10% (not coded) leads to 5.5 – 7.5 dB improvement depending on the demodulation scheme
    Secure ranging with pre-synchronization further significantly enhances the reliability of the secure ranging!!!