## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SUN FSK spec extension to lower data rates]
Date Submitted: [10 July 2018]
Source: [Chris Calvert] Company [Landis + Gyr]
Address [30000 Mill Creek Ave, Alpharetta GA 30022]
Voice:[+1678 258 3165], FAX: [ ], E-Mail:[chris.calvert@landisgyr.com]
Re: []
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Proposed extending SUN FSK PHY specification to lower data rates in certain bands.]
Purpose: [Proposed spec changes for lower SUN FSK baud rates]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Overview – 802.15.4x PAR
Slide 2
“This amendment also defines additional channel plans to support emerging applications. Typical range of the radio is up to 5 kilometers with line of sight using omnidirectional antennas.”
Notes: July 18
Page 2

## Slide 3: Proposal from May
For SUN FSK PHY – add three optional PHYs as defined in table below:
Determine which ISM channel plans in table 20-7 to apply these to – but certainly include 902-928 MHz.
 | Mode 6 | Mode 7 | Mode 8
Data rate (kb/s) | 10 | 20 | 40
Modulation | 2FSK | 2FSK | 2FSK
Mod Index | 0.5 or 1.0 (TBD) | 0.5 or 1.0 (TBD) | 0.5 or 1.0 (TBD)
Channel spacing (kHz) | 100 | 100 | 100
Notes: July 18
Page 3

## Slide 4: Updates & Measurements
Decided having a 40kbps and 50kbps PHY did not make sense – so eliminated that from further consideration.
Looked at different silicon solutions widely used today and determined that best Mod Index for both 10kbps and 20kbps baud rates was 1.0
Captured ACP data to determine best suggested channel spacing
Based on the measurements – suggest moving forward with the spec additions on the next slide
Slide 4
 | 50kHz spacing |  | 100kHz spacing | 
 | Lower ACP | Upper ACP | Lower ACP | Upper ACP
10kbps | -35.37 | -35.25 | -44.88 | -44.68
20kbps | -26.44 | -26.11 | -34.87 | -35.12
 | All Measurements in dBc |  |  | 
Notes: July 18
Page 4

## Slide 5: Extension proposal
For SUN FSK PHY – add optional PHYs as defined in table below:
Depending on bands PHYs to be added to – actual mode numbers will vary.
The Transmit spectral mask (20.6.6) should use the original spec based on baud rate (R) and not what the spec added as part of 4V using channel spacing (S)
Slide 5
 | Mode a | Mode b
Data rate (kb/s) | 10 | 20
Modulation | 2FSK | 2FSK
Mod Index | 1.0 | 1.0
Channel spacing (kHz) | 50 | 100
Notes: July 18
Page 5

## Slide 6: Extension proposal
For SUN FSK PHY – frequency bands to add this PHY to:
From Table 20-6 – consider adding these options to all the bands in 20-6 which have 50kbps baud rate for Mode #1.
  Frequency Band Identifiers - 470-510, 779-787, 863-870, 865-867, 902-928, 917-923.5, 2400-2483.4
  Do we add two more Modes in this table to account for these?
From Table 20-7 – consider adding these options to ALL of the bands.
  Frequency Band Identifiers – 920 – 928, 902 – 928 (alternate), 902 – 907.5 & 915 – 928, 915 – 928, 915 – 921, 915 – 918, 919 – 923, 920.5 – 924.5 and 920 - 925
Slide 6
Notes: July 18
Page 6

## Slide 7: Extension proposal
Other changes necessary
  SUN Device Capabilities IE (Section 7.4.4.10)
    In Table 20-6 – would need to add new PHY Type 9 – FSK-C which is a continuation of FSK B – which is now a full table after 4V.
    Would need a new Table following 7-22 (7-22a for now) called FSK-C PHY mode encoding. Mode id 0 would be the 10kbps PHY and id 1 would be the 20kbps PHY
  Channel numbering for SUN and TVWS PHYs (Section 10.1.2.8 )
    Based on the frequency bands agreed to add the PHY’s to – Table 10-10 that specifies the channel numbering would have to be updated.
Slide 7
Notes: July 18
Page 7

## Slide 8: Conclusions
Slide 8
Upon agreement on PHY’s and frequency bands – ask editors to move forward with adding these changes to the 4x amendment specification.
Notes: July 18
Page 8