## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SRDEV Evaluation Criteria]
Date Submitted: [10 July, 2018]
Source: [Frank Leong (NXP Semiconductors), Jochen Hammerschmidt (Apple)]
Re: [Input to the Task Group]
Abstract: [Presentation, SRDEV, Evaluation Criteria, Key Performance Indicators]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SRDEV Evaluation Criteria

## Slide 3: Key Performance Indicators (Evaluation Criteria) I
STS ACF quality & first path dynamic range for Secure Ranging
  CDF (or CCDF) of sidelobe peak levels relative to main lobe of Normalized STS Autocorrelation (AC)
  E.g., max(abs(.)) of sidelobe levels in [dB] over a {-128 ns, +128 ns} temporal window of one random STS sequence; this represents one sample for CDF/CCDF curve
  Focus initially on DSLS-free implementation

## Slide 4: Key Performance Indicators (Evaluation Criteria) II
Average EIRP and Peak EIRP w.r.t. regulatory limits
  Compare potential to maximize link budget for short frames
    Consider potential impact of peak power limit on link budget
  Scope of Secure Ranging includes sub-ms frame lengths
Instantaneous (PA) Peak Power / PAPR (measurement w/o BW limitation, i.e., peak voltage)
  Consider link budget for (low-cost / low-power) transmitter implementations, including possible application losses

## Slide 5: Key Performance Indicators (Evaluation Criteria) III
PER associated with PHR and PSDU (incl. coding gain)
Budgeting of energy distribution across frame fields
Required on-air time
  Number of frames per ranging (e.g., avoid sending timestamp frames)
  Packet duration for given Performance / Features
    Reduce multi-user interference / increase network capacity

## Slide 6: Key Performance Indicators (Evaluation Criteria) IV
Backward compatibility
  Similarity to legacy standard
Future-proofness
Attack resilience (e.g., random STS acceptance rate)
Localization performance
  Achievable accuracy (effective amplitude resolution) of CIR estimation