## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IG DEP Space-time domain interference mitigation using based on OMF and TDL-AA for dependable UWB-BANs]
Date Submitted: [10 July 2018]
Source: [Takumi Kobayashi1, Ryuji Kohno1,2,3] [1;Yokohama National University, 2;Centre for Wireless Communications(CWC), University of Oulu, 3;University of Oulu Research Institute Japan CWC-Nippon]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
2; Linnanmaa, P.O. Box 4500, FIN-90570 Oulu, Finland FI-90014
3; Yokohama Mitsui Bldg. 15F, 1-1-2 Takashima, Nishi-ku,Yokohama, Japan 220-0011]
Voice:[1; +81-45-339-4115, 2:+358-8-553-2849], FAX: [+81-45-338-1157],
Email:[1: kohno@ynu.ac.jp, 2: Ryuji.Kohno@oulu.fi, 3: ryuji.kohno@cwc-nippon.co.jp] Re: []
Re: []
Abstract: [As a dependable PHY technology for wireless body area network(WBAN), schemes of Space-time domain interference mitigation using based on OMF and TDL-Array Antenna are introduced.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Space-Time Domain Interference Mitigation Using Based on OMF and TDL-AA for Dependable UWB Wireless Body Area Networks (UWB-WBANs)
Takumi Kobayashi*, Ryuji Kohno*†
＊Yokohama National University
† University of Oulu Research Institute Japan – CWC-Nippon, Co. Ltd.

## Slide 3: Issues on multiple BAN environment
  Inter-user interference
    IR-UWB uses the same pulse as all users signal in the same standard.
    Other users signal and/or the other network signal would be interference.
  Inter-system interference
    Interference from the other wreless system using overlapped frequency band. ⇒ Unknown
＊ 802.11a (wi-fi) （5GHz） overlaps
user C
user ？
user B
User A wants to connect to“B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4a
user ？
user ？
interference
interference

## Slide 4
Purpose and Suggestion
  Sparate and Recognize each interference from different source. ⇒ Apply suitable interference mitigation method according to source of interference.
  Using both of Spatial and Temporal signal processing.
Inter-user interference
Recognize and demodulate
Remove
Interference canceller
Multi-user detection
Pulse shape multiple access
“IUI” in this presentation
“ISI” in this presentation
Interference from a system using the same pulse
Inter-system interference
Interference from a system using overlapped frequency
known
unknown
Notes: 4

## Slide 5
Interference mitigation techniques and related researches
2.1 Orthogonal Matched filter
2.2 Tapped Delay Line Array Antenna
2.3 IR-UWB Communication using Modified Hermite Pulse
Chapter 2
Notes: 5

## Slide 6
OMF； orthogonal matched filter
  consists a matched filter （MF1） and MF Group（MFG）
  Tap coefficients of MF1 are the same as sequence of desired signal.
  Coefficients of MF1 and each MFk that constituting MFG are orthogonal.
  Desired signal does not through MF2～K-1 because orthogonality. →only interference can through.
  MFG makes replica of interference signal by lenear combination with weight vector w of linear combiner; LC.
  Subtract interference replica from the output of MF1 .
Principle of OMF
  OMF can remove interference without any pre-knowledge of interference.
Notes: 6

## Slide 7
TDL-AA；Tapped delay line array antenna
  Array antenna by using multiple antenna elements and tapped delay line.
  Each antenna branch has coefficients.
  Transfer function of this antenna has parameters of signal incoming angle;θ and frequency; ω.
  ⇒has characteristics of both of spatial and time domain.
Principle of TDL-AA
  TDL-AA can work as interference canceller on both of time and space domains
（Tapped delay line array antenna）
Notes: 7

## Slide 8
Modified Hermite pulse; MHP applied to IR-UWB communication (Mohammad Ghavami et al,)
  Pulse function generated by modified Hermitian polynomials.
  Pulses are orthogonal each other in sync.（t=0）condition.
  Cross correlation =0. ⇒no interference
  In async.（t≠0） condition, not orthogonal.
Notes: 8

## Slide 9
Orthogonality of MHP
  MHP: Modified Hermite Pulse
  Each user uses unique order MHP as its transmission signal.
  n-th order MHP is generated by n-th order modified Hermite polynomial.
  In sync.（t=0） and no distortion condition, MHPs are orthogonal. (cross correlation = 0)
  Channel propagation makes it distortion. ⇒NOT orthogonal.
Interference canceller
Notes: 9

## Slide 10
overview
Proposal 2
Chapter 4
Space-Temporal interference mitigation using TDL AA based on OMF using pulse orthogonality
Pulse shape based OMF
Proposal 1
Chapter 3
OMF based on orthogonality of random sequence
（existing）
TDL Array antenna （existing）
Notes: 10

## Slide 11
Time domain interference mitigation for inter-user and inter-system interference
  3.1 Purpose
  3.2 System model and theoretical analysis
  3.3 Numerical Evaluation and results
Chapter 3
Interference Cancellation for Intra and Inter UWB systems Using Modifed Hermite Polynomials Based Orthogonal Matched Filter
Notes: 11

## Slide 12
  Inter-user interference
    Typical UWB uses same pulse.
    The interference from the other user in same network.
  Inter-system interference
    The interference from the other system using same frequency band.
    Unknown interference.
user C
user ？
user B
User A wants to connect to“B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4a
user ？
user ？
  UWB system takes several types of interference.
interference
interference
Notes: 12

## Slide 13
Purpose and Suggestion
  Sparate and Recognize each interference from different source. ⇒ Apply suitable interference mitigation method according to source of interference.
  Using both of Spatial and Temporal signal processing.
Inter-user interference
Recognize and demodulate
Remove
Interference canceller
Multi-user detection
Pulse shape multiple access
“IUI” in this presentation
“ISI” in this presentation
Interference from a system using the same pulse
Inter-system interference
Interference from a system using overlapped frequency
known
unknown
Notes: 13

## Slide 14
Proposed OMF with Multi-user detection
    MUD and ISI mitigation
  As MF and MFG of OMF,
    Use discrete sampled MHP.
    Gramm-Schmidt orthonormalization is used for fill deficit in MFG.
  By utilizing the MHP as a MFG…
    Known user’s signal which uses same MHP as MFG can be retrieved.
    Unknown interference can be cancelled
    Works at the same time
Proposed system for 2 users detection.
MUD
ISI mitigation
Notes: 14
therefore

## Slide 15
System model and theoretical analysis.
  Rx signal
is desired user’s pulse
k-th orthogonal vector
In vector form
output included in
Notes: 15
therefore

## Slide 16
System model and theoretical analysis
is desired user’s pulse
k-th orthogonal vector
Interference is cancelled in condition satisfies…
signal included in
Interference
Desired signal is assumed as a1
Desired signal
Notes: 16
therefore

## Slide 17
System model and theoretical analysis
is desired user’s pulse
k-th orthogonal vector
In matrix
Optimum weight vector
Interference is cancelled in condition satisfies…
*without noise
Notes: 17
therefore

## Slide 18
Numerical evaluation
    Assumed MHP-UWB which uses MHP as transmission pulse.
    Each user uses unique order MHP as a transmission pulse.
    MAC frame has generally known SHR preamble on its head. → Adaptive algorithm estimates an optimum solution by using this known preamble.
    IUI and ISI exist.
Notes: 18
therefore

## Slide 19
  MUD and ISI canceller – Numerical evaluation.
DIR [dB] | -40 to +40 | 
Known user | 2 (0th and 3rd MHP) | １ (0th MHP)
Unknown interference | Gold sequence DS-UWB, 29 users | Chirped pulse UWB, 1user
Channel (dist. / noise) | IEEE 802.15.6 CM3 path loss model + AWGN | 
Iteration for LMS / NLMS | 2,000 ~ 32,000 / 4,000 ~ 64,000 | 250 ~ 3,000 / 80 ~ 1280
Scenario 1
Scenario 2
user 1
user 2
user 2
user 5
Notes: 19

## Slide 20
  Results of SC.1
Square error (SC.1).
Adaptive algorithm makes approx. solution.
Weight coefficients converge to optimum solution wopt.
Multiple user’s signal retrieved with interference reduction.
Weight coefficients (SC.1) Eb/N0=+60dB, DIR=0dB.
LMS & NLMS algorithm towards to minimum square error.
Eb/N0=+60dB, DIR=0dB
Notes: 20

## Slide 21
  Results (LMS algorithm)
DIR vs. BER (SC.1) Eb/N0=+35dB.
In low DIR situation, this system LMS algorithm cannot be used.
DIR vs. BER (SC.2) Eb/N0=+25dB.
More iteration number makes higer capacity of interference reduction
Notes: 21

## Slide 22
  Results (NLMS algorithm)
DIR vs. BER (SC.1) Eb/N0=+35dB.
DIR vs. BER (SC.2) Eb/N0=+25dB.
More iteration number makes higer capacity of interference reduction
Normalized LMS algorithm can be used even in extremely low DIR condition.
Notes: 22

## Slide 23
  Results (Without noise)
DIR vs. BER (SC.1) Eb/N0=+∞dB.
DIR vs. BER (SC.2) Eb/N0=+∞dB.
More iteration number makes higer capacity of interference reduction
Notes: 23

## Slide 24
  Results of SC.1
Square error characteristics in various DIR(SC.1).
Adaptive algorithm does not find an optimum weights in low DIR and low Eb/N0. ⇒ ⇒ ⇒ Theoretical analysis with Noise
Eb/N0=+120dB, DIR=-40dB ~ +40dB
Square error characteristics in various DIR (SC.1).
Eb/N0=+25dB, DIR=-40dB ~ +40dB
Notes: 24

## Slide 25
Simulation results
  (noise free channel)
DIR vs. BER Eb/N0=+∞dB.
More iteration number makes higer capacity of interference reduction

## Slide 26
Simulation results
  (noise & interference channel)
DIR vs. BER (SC.2) Eb/N0=+25dB.
Wopt which is generated by theory does not satisfies minimum error In high DIR condition. ⇒ Wopt is not optimal solution in environment in which noise exists.
High DIR  dominant cause of bit error is noise
Noise
enhancement

## Slide 27
  Theoretical analysis
Analyze a theoretical solution which satisfies MMSE criteria
Residual interference
Enhanced noise
Adaptive algorithm try to find MMSE “as smaller as possible ⇒ not optimum
Size reduction of weight vector by a coefficient Δ
noise
Suppression of noise enhancement by Δ
When W ≠ Wopt , interference remains.
⇒residual interference is increased
⇒noise enhancement is suppressed
Δ becomes smaller
Notes: 27

## Slide 28
  Smaller Δ makes
Wopt is shrinked by Δ ≦ 1.
Δ which satisfies MMSE in various DIR (SC.2) Eb/N0=+25dB.
Δopt depends on power of interference and noise
Adaptive algoeithm cannot find Δopt but it can find approximate solution.
Δopt in -20dB
Δopt in -10dB
Δopt in 0dB
Δopt in 10dB
Δopt in 20dB
⇒residual interference is increased
⇒noise enhancement is suppressed
Notes: 28

## Slide 29
  Theoretical performance
Size reduction of weight vector by a coefficient Δ
Square error using various fixed Δ and Δopt in each DIR (SC.2) Eb/N0=+25dB.
Optimum solution
  Smaller Δ
⇒residual interference is increased
⇒noise enhancement is suppressed
  Larger Δ
⇒residual interference is suppressed
⇒noise enhancement is increased
Notes: 29

## Slide 30
Theoretical analysis results
Δopt value in each Eb/N0 and DIR conditions
MSE in optimum slution
In High DIR and Low Eb/N0 channel, Δopt becomes close to 0 (zero).
In Low DIR and High Eb/N0 channel, Δopt becomes close to 1 (one).
Optimal solution Δoptwopt provides a performance limit of our proposing system.
Although our system cannot remove noise, MSE can be reduced in low noise situation.
MSE in dB

## Slide 31
Space-time domain interference mitigation using TDL array antenna for MHP based IR-UWB
  4.1 Proposed system model and theoretical analysis
  4.2 Numerical evaluation and results
Chapter 4
(2) Space Temporal Interference Cancellation Using TDL Array Antenna and Waveform Based OMF for IR-UWB Systems
Notes: 31

## Slide 32
TDL-AA；Tapped delay line array antenna
  Array antenna by using multiple antenna elements and tapped delay line.
  Each antenna branch has coefficients.
  Transfer function of this antenna has parameters of signal incoming angle;θ and frequency; ω.
  ⇒has characteristics of both of spatial and time domain.
Principle of TDL-AA
  TDL-AA can work as interference canceller on both of time and space domains
（Tapped delay line array antenna）
Notes: 32

## Slide 33
Apply pulse based OMF to spatial signal processing
  TDL array antenna
    Configured by multiple antennas and tapped delay line （TDL）
    TDL-AA can separate the signals which comes from the same direction by using time-domain signal processing.
  By applying OMF to TDL-AA
    Interference reduction is performed on the both of domains of time and space.
Space-temporal signal processing
Notes: 33
therefore

## Slide 34
System model and optimum parameters.
  Beam forming,
    Delay time of each antenna brunch is adjusted to achieve Maximum Power of desired signal
    N ：number of antennas, ν： propagation speed ds ：antenna distance
  Null-steering,
    MHP based OMF is used as a TDL.
    arrival time difference of u-th users signal in n-th antenna is
Notes: 34
therefore

## Slide 35
System model
  Delay time for beam forming is
  OMF of n-th brunch has coefficients cn(t) that satisfy bellow
Matrix form
is desired user’s pulse
k-th orthogonal vector
is u-th user’s pulse (undesired)
where, wk is determined as
Notes: 35
therefore

## Slide 36
  Characteristics evaluation on each arrival angle
Number of antennas / placement | 5 / Linear array | 
Distance between antennas; ds [m] | 0.45 | 
Desired user’s pulse | 0th order MHP | 
Interference user’s pulse | 2nd order MHP (IUI) and chirped pulse UWB (ISI) | 
Arrival angle of desired signal [degree] | 10 | 0
Arrival angle of interference signal [degree] | 30 and -60 | 0 and 0
Scenario 6
Scenario 7
Notes: 36

## Slide 37
Space-temporal interference reduction (SC.7)
System has gain against an interference →residual interference
Interference signal is reduced
TDL-AA without null-steering（ SC.6）
No gain
Gain≠0
Gain≠0
Notes: 37

## Slide 38
Space-temporal interference reduction(SC.7)
TDL-AA without null-steering （ SC.6）
Gain≠0
No gain
MHP orthogonality
System has gain against an interference →residual interference
Interference signal is reduced
Notes: 38

## Slide 39
Number of antennas / placement | 5 / Linear array
Distance between antennas; ds [m] | 0.45
Desired user’s pulse | 1st order MHP
Interference user’s pulse | 1st order MHP
Arrival angle of desired signal [degree] | -30
Arrival angle of interference signal [degree] | 30
Scenario 8
    2 users use the same pulse
    Time-domain signal processing cannot reduce the interference
  Characteristics evaluation on each arrival angle
Notes: 39

## Slide 40
Space-temporal interference reduction(SC.8)
Interference can be eliminated if either one is different from the desired signal
TDL-AA without null-steering （ SC.8）
Gain≠0
reduction
Max gain
Max gain
System has gain against an interference→residual interference
Notes: 40

## Slide 41
Conclusion
  OMF based on Modified Hermite pulse have been proposed.
  Interference mitigation (reduction) in Time-domain.
  By using layered structure, MHP based OMF combined with Code-based OMF.
    Reduce computation cost, and expand number of users (capacity)
  MHP based OMF is combined with TDL-AA.
    Interference mitigation on Time and space domains signal processing.
Notes: 41

## Slide 42: References
Takumi Kobayashi Chika Sugimoto, Ryuji Kohno, “Theoretical analysis of interference canceler using modified hermite polynomials based orthogonal matched filter for IR-UWB systems in AWGN and interference channel,” Proc. 2017 20th International Symposium on Wireless Personal Multimedia Communications (WPMC) 2017, DOI: 10.1109/WPMC.2017.8301793
Takumi Kobayashi, Masato Suzuki, Chika Sugimoto, Ryuji Kohno, “Space temporal interference cancellation using TDL array antenna and waveform based OMF for IR-UWB systems,” ICT Express, Volume 1, Issue 2, pp.71-75, 2015. ISSN 2405-9595, https://doi.org/10.1016/j.icte.2015.09.006.
Takumi KOBAYASHI Chika SUGIMOTO Ryuji KOHNO, “Interference Cancellation for Intra and Inter UWB Systems Using Modified Hermite Polynomials Based Orthogonal Matched Filter,” IEICE TRANSACTIONS on Communications Vol.E99-B No.3 pp.569-577, 2016.