## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SCHC (Static Context Header Compression) IETF draft overview]
Date Submitted: [12 July 2018]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: [draft-(perkins,robert)-lpwan-schc-802154-00.txt]
Abstract: [overview of proposed IETF draft for SCHC (Static Context Header Compression) for 802.15.4w]
Purpose: [Presentation in TG 802.15.4w.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SCHC (Static Context Header Compression) IETF draft overview
Charlie Perkins / Futurewei
Joerg Robert / FAU Erlangen-Nuernberg

## Slide 3: Motivation for SCHC
Many IoT applications rely on the use of IPv6
The overhead caused by IPv6 is very significant (>40 bytes), even if the actual payload is only few bytes
Direct transmission of IPv6 over LPWAN not useful
Header compression absolutely necessary for LPWAN

## Slide 4: IETF SCHC status
SCHC relies on static compression tables and does not learn during operation
Data unit out-of-sequence delivery will not happen between the compressor and the decompressor
SCHC is in Last Call; available on the IETF website https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
Details are needed in implementation specific documents for each standard (e.g. 802.15.4w)

## Slide 5: What is Configurable
Number of different rules
Mapping of L2 and IPv6 addresses
Fragmentation
Acknowledgement modes (ACK-0, ACK-1, ACK-2)
DTAG (number of parallel packets)
Retransmission and inactivity timers
Number of MAX_ACK_REQUESTS

## Slide 6: Mapping of L2 and IPv6 Addresses
Do we want to define the mapping of L2 and IPv6 addresses?
Or should this definition be done by the network operator?
Depends on the address space provided for the particular kind of device

## Slide 7: Use of Padding
Pad to a multiple of 8 bits in the L2 payload (SCHC does not specify this)

## Slide 8: Message Integrity Check: L2 CRC
The CRC32 as 0xEDB88320 (i.e. the reverse representation of the polynomial used e.g. in the Ethernet standard [RFC3385]) is recommended as the default algorithm for computing the MIC
Either CRC-16 or CRC-32 as defined in 802.15.4 could be used

## Slide 9: Fragmentation
802.15.4 link acknowledgement should be used, since the static context as defined should be decompressed after delivery over a single link
no specification is made here for the following:
  The timer size for Fragmentation ACK Always
  When to abort in ACK Always
  MAX_ATTEMPTS counter size
  The timer size between windows in ACK On Error

## Slide 10: Acknowledgement Mode
FCN SHOULD be set to 0, since unfragmented traffic is expected for most use cases under consideration in 802.15.4w.

## Slide 11: DTAG
Similarly, DTag SHOULD be set to 0, since unfragmented traffic is expected for most use cases under consideration in 802.15.4w.

## Slide 12: Possible Next Steps
Should we define context tables for typical 802.15.4w application scenarios?
If so, which use cases should be considered first?
Should we design for 802.15.4 in general, or 802.15.4w only, or both?