## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal of LDPC (Low Density Parity Check) Code for LPWA – additional results]
Date Submitted: [05 September, 2018]
Source: [Nabil Loghin] Company [Sony Europe Limited, ZN Deutschland]
Address [Hedelfinger Str. 61, 70327 Stuttgart, Germany]
Voice:[+49 711 5858 734], FAX: [+49 711 5858 734 99], E-Mail:[nabil.loghin@sony.com]
Re: [IEEE P802.15.4w Low Power Wide Area Call for Proposals, 12 March 2018]
Abstract: [LDPC (Low Density Parity Code) as a Forward Error Correction.]
Purpose: [Contribution to IEEE 802.15.4w]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposal of LDPC (Low Density Parity Check) Code for LPWA -- additional results
Nabil Loghin, Dana Ciochina (Sony European Technology Center, Stuttgart, Germany), Seiji Kobayashi, Ryoji Ikegaya (Sony Semiconductor Solutions Corporation)

## Slide 3: Introduction
In [1], LDPC FEC proposal for 802.15.4w was presented with initial results. The group asked to measure performance w.r.t. packet error rate (PER) of 1%, and comparing with best rate 1/4 convolutional code, incl.
  erasure channel (from interference)
  mobile fading channel
  MSK modulation
In [2], first results have been shown for erasure and fading channel. Comments have been made to include
  higher erasure rates
  fading channel with time/frequency hopping
This presentation will update
  erasure channel results
  mobile fading channel
  summarize previously shown results

## Slide 4
Rate ½ convolutional coding with constraint length K = 7 has been specified in 802.15.4k.
In a practical implementation, additional 6 bits are needed as a purpose of “termination”, which increases redundancy. 6 bits of redundant information is not negligible for a system with small-size payload.
uk-1
uk-2
uk-3
uk-4
uk-5
uk-6
uk
+
+
+
+
+
+
+
+
ak
ak
1
0
Review: Baseline Forward Error Correction

## Slide 5
Row and col index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 1 | 7 | 90 | 172 | 209 | 359 | 401 | 420 | 483 | 487
2 | 57 | 164 | 192 | 197 | 284 | 307 | 174 | 356 | 408 | 425
3 | 22 | 50 | 191 | 379 | 385 | 396 | 427 | 445 | 480 | 543
4 | 32 | 49 | 71 | 234 | 255 | 286 | 297 | 312 | 537 | 550
5 | 30 | 70 | 88 | 111 | 176 | 201 | 283 | 322 | 419 | 499
6 | 86 | 94 | 177 | 193 | 266 | 368 | 373 | 389 | 475 | 529
7 | 134 | 223 | 242 | 254 | 285 | 319 | 403 | 496 | 503 | 534
8 | 18 | 84 | 106 | 165 | 170 | 199 | 321 | 355 | 386 | 410
9 | 129 | 158 | 226 | 269 | 288 | 316 | 397 | 413 | 444 | 549
10 | 33 | 113 | 133 | 194 | 256 | 305 | 318 | 380 | 507 | 
11 | 317 | 354 | 402 |  |  |  |  |  |  | 
12 | 53 | 64 | 374 |  |  |  |  |  |  | 
13 | 83 | 314 | 378 |  |  |  |  |  |  | 
14 | 162 | 259 | 280 |  |  |  |  |  |  | 
15 | 166 | 281 | 486 |  |  |  |  |  |  | 
16 | 185 | 439 | 489 |  |  |  |  |  |  | 
17 | 119 | 156 | 224 |  |  |  |  |  |  | 
18 | 26 | 62 | 244 |  |  |  |  |  |  | 
19 | 8 | 246 | 482 |  |  |  |  |  |  | 
20 | 15 | 72 | 91 |  |  |  |  |  |  | 
21 | 43 | 69 | 390 |  |  |  |  |  |  | 
22 | 127 | 186 | 506 |  |  |  |  |  |  | 
23 | 55 | 81 | 412 |  |  |  |  |  |  | 
Parity bit addresses table
details in separate Word document for spec. extensions
info (184 bits)
Proposed LDPC Rate (1/4) for 802.15.4w
September 2018

## Slide 6: Erasure Performance: Conditions
interference by other devices modelled by complete signal erasures
assuming telegram splitting with 24 telegrams
  lost frames result in complete erasure
  if interleaving is applied, resulting frame has iid erasures with erasure rates = n/24, integer n
 simulated AWGN, followed by iid erasure channel

## Slide 7: AWGN Performance
1.54dB
1.21dB

## Slide 8: Erasure Performance ( = 1/24)
1.56dB
1.27dB

## Slide 9: Erasure Performance ( = 8/24)
1.75dB
1.36dB

## Slide 10: Erasure Performance ( = 12/24)
2.30dB
1.71dB

## Slide 11: Erasure Performance ( = 14/24)
convolutional codes have error floor above PER 1%

## Slide 12: Erasure Performance ( = 16/24)
at  = 16/24, PER 1% cannot be achieved

## Slide 13: Erasure Performance: Summary
LDPC gain at 1% PER |  = 0 |  = 1/24 |  = 2/24 |  = 4/24 |  = 6/24 |  = 8/24 |  = 10/24 |  = 12/24 |  = 14/24 |  = 16/24 |  = 18/24
vs. baseline FEC [dB] | 1.54 | 1.56 | 1.58 | 1.60 | 1.66 | 1.75 | 1.92 | 2.30 | Inf(*) | N/A(**) | N/A(**)
vs. best CC of rate 1/4 [dB] | 1.21 | 1.27 | 1.23 | 1.27 | 1.29 | 1.36 | 1.45 | 1.71 | Inf(*) | N/A(**) | N/A(**)
erasure rates (remaining results: see appendix)
LDPC gains increasing with larger erasure rates
(*): convolutional codes do not reach PER = 1%
(**): all codes do not reach PER = 1%

## Slide 14: Mobile Performance: Conditions
TU6 channel has very short delay spread of 5µs << symbol duration
consider only 1-tap Rayleigh fading with Jakes’ psd @fD,max = 25Hz (900MHz, 30km/h)
12kbaud, corresponding to 3kbps data rate
genie-aided equalization (of each tap)
Maximum ratio combining for CR=1/2 baseline code with 2 frame repetitions
each frame transmitted at random time / freq. slot
  new seed for fading generation
assumed idealalized random interleaver over all frames

## Slide 15: Mobile Performance: 1 frame for CR 1/4
3.34dB
>15dB

## Slide 16: Mobile Performance: 2 frames for CR 1/4
1.43dB
4.29dB

## Slide 17: Mobile Performance: 12 frames for CR 1/4
1.33dB
1.29dB

## Slide 18: Mobile Performance: Summary (1/2)
LDPC gains especially large in high SNR regime, when only limited number of frames need to be transmitted
LDPC gain at 1% PER | with 1 frame for CR 1/4 | with 2 frames for CR 1/4 | with 4 frames for CR 1/4 | with 8 frames for CR 1/4 | with 12 frames for CR 1/4
vs. baseline FEC [dB] | 3.34 | 1.43 | 1.27 | 1.28 | 1.33
vs. best CC of rate 1/4 [dB] | > 15 | 4.29 | 1.90 | 1.37 | 1.29
remaining results: see appendix

## Slide 19: Summary
Comparison of LDPC vs. baseline FEC vs. convolutional code of rate 1/4
  LDPC encoding complexity [2]
    13% larger than for baseline FEC
    100% smaller than conv. code of same rate 1/4
  AWGN + erasure: LDPC gains:
    1.54 … 1.75dB vs. baseline FEC
    1.21 … 1.36dB vs. conv. code of same rate 1/4
  mobile fading channel
    3.34 … 1.33dB gain vs. baseline FEC (1 frame … 12 frames)
    ~16 … 1.29dB gain vs. conv. code of same rate 1/4

## Slide 20: References
[1] S. Kobayashi, N. Loghin, R. Ikegaya, “proposal-of-ldpc-low-density-parity-code-for-lpwa”, 15-18-0289-01-004w
[2] S. Kobayashi, N. Loghin, R. Ikegaya, proposal-of-ldpc-low-density-parity-check-for-lpwa, 15-18-0289-02-004

## Slide 21
APPENDIX

## Slide 22: AWGN / Erasure Performance: All Results
 = 18/24 is capacity limit of (pure) erasure channel for R = 1/4
critical error floors for  = 16/24
significant error floors for  = 12/24 and 14/24 for convolutional codes (LDPC still quasi-error free)
increasing erasure rates

## Slide 23: Mobile Performance: All Results
increasing number of frames
converging towards AWGN curves, if frame no.  Inf

## Slide 24: Mobile Performance
Observation (sanity check):
  fading performance with multiple frames transmitted at different time/freq. locations approaches AWGN performance under optimum Maximum Ratio Combining (MRC) and ideal interleaving
Convolutional code (CC) of rate 1/4 inferior to CC of rate 1/2 and double frame repetitions, due to lack of diversity
  coding gain of LDPC and inherent repetition (at variable node decoding step during message passing) still superior to CC 1/2

## Slide 25: Mobile Performance: Comments
previously shown results in [2]:
  results 3dB too good,since Matlab AWGN block generated diff. noise power, depending on real vs. complex input (now corrected)
  channel was not reset, also for 2 repetitions in case of CR 1/2  no significant time diversity, which can be gained from time/freq. hopping
  only all-0 codeword transmitted  in case of heavy fading, Viterbi outputs mostly all-0  over-optimistic results for convolutional codes

## Slide 26: Encoder Complexity
Reference: Convolutional Code of memory 6 (133,171)
  184 info bits, 5 elements in mod-2 addition per code bit:
    (184+6)*(5-1 + 5-1) = 1.5k metrics
Conv. Code, CR 1/4 of memory 6 (117 127 155 133)
  184 info bits, 5 elements in mod-2 addition per code bit:
    (184+6)*(5-1)*4 = 3.4k metrics
LDPC, CR 1/4
  552 parities, average check node degree 4 (4 elements in mod-2 additions)
  552*(4 -1) = 1.7k metrics