## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE P802.15.13 – MAC layer support for multiple optical frontends
Date Submitted: 15. November 2018
Source: Kai Lennert Bober, Volker Jungnickel [Fraunhofer HHI]
Address: Einsteinufer 37, 10587 Berlin, Germany
Voice:[+49-30-31002 302], E-Mail:[kai.lennert.bober@hhi.fraunhofer.de]
Voice:[+49-30-31002 768], E-Mail:[volker.jungnickel@hhi.fraunhofer.de]
Re:
Abstract:
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15.13 MAC Layer support for Multiple Optical Frontends
Date: 2018-11-15 Place: Bangkok, Thailand
Authors:

## Slide 3: Content
This doc. contains a proposal for protocol procedures and frame types, necessary to support distributed optical frontends and MIMO techniques in the star topology.

## Slide 4: Descriptive: Targets of the Distributed Optical Frontend (OFE) Approach
Coordinator
Fronthaul
Optical Frontend
Device
OWC signal
Introduction of spatial diversity on the signal level
Enable spatial reuse with smooth handover performance and high QoS
Low level “soft handover”: OFE form virtual cells following the device’s movement, fully transparent to the management protocol
Fig 1: Coordinator in star topology with distributed OFEs serving two devices simultaneously

## Slide 5: Descriptive: Superframe Structure for Spatial Reuse and Joint Transmission + Reception
Slotted uplink random access without carrier sensing (ALOHA) in CAP. For association and reconnection only; collisions may occur.
GTS allocations per device for regular collision-free transmission and in the CFP.
Different GTS allocated in same superframe slot but different OFE slots (SDMA).
GTS spans over multiple OFE slots, implying a “virtual cell” for joint transmission / reception.
CAP
CFP
Beacon
“Superframe slots” = TIME
“OFE slots“
=
SPACE
Receive A
Receive C
Receive D
Receive B
Concept of superframe structure. Only receive (downlink)
direction is considered for simplicity. A,B,C,D = devices.
GTS = TIME + SPACE reservation

## Slide 6: Descriptive: Channel Estimation, CSI Feedback and GTS Update
Multicell channel estimation is based on multi-cell pilots in the beacon. For individual virtual cell transmissions, additional desired BAT or MCS feedback can be generated.
The coordinator schedules GTS based on feedback and selects adaptive transmission.
Dynamic GTSs are updated via control frames and valid during next superframe, if validity=0, otherwise for multiple superframes. Previous dynamic GTS allocations lose validity. GTS update is acknowledged in next feedback frame.
Coordinator
Device
BP
CFP
CAP
feedback
dynamic GTS
Multi-cell channel est.
channel est.
channel est.
control frame
beacon
scheduling

## Slide 7: Multi-cell channel estimation feedback
TAP format for the setting of variable resolutions for the taps
Symbol (1-7) + division (1-32) for pilot / OFE identification.
Strength for first tap is SNR [dB].
For other TAPs it is the ratio [dB] between first and current TAP
First OFE / TAP is the one with lowest delay.
Bits: 0-3 | 4-7 | Variable | 
Number of OFEs | TAP format | OFE descriptor 1 | …
Bits: 0-2 | 3-7 | 8-15 | Variable | 
Symbol | Division | Number of TAPs | TAP descriptor 1 | …
Bits: 0-7 ? | 8-15 ? | 16-23 ?
Strength | Integer delay | Decimal delay

## Slide 8: Adaptive bitloading feedback: requested BAT control frame format
Valid BAT bitmap indicates applicability of each of the 24 runtime BATs for transmissions from the recipient towards the sender of the BAT request frame.
The “Updated BAT” field indicates a BAT for transmissions from the recipient towards the sender of the requested BAT frame that shall be updated.
If all runtime BATs are invalid, the frame contains only two octets of zeros
FEC schemes: code rates (CR) 1/2, 2/3, 5/6, 16/18, 20/21 & block sizes (BS) 960, 4320
List of groups of subcarriers to load different numbers of bit on:
  Grouping: 1, 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, 4096
  Loaded bits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12
Last group is the one exceeding the actual number of subcarriers present in the PHY
Bits: 0-23 | 24-28 | 29-31 | 32-34 | 35-39 | Variable | 
Valid BATs | Updated BAT | FEC block size | FEC code rate | Reserved | Group 1 | …
Bits: 0-3 | 4-7
Grouping | Loaded bits

## Slide 9: Adaptive bitloading feedback: protocol
When the channel changes and a formerly valid BAT gets unusable, a new BAT is set (“updated”). The old BAT is marked invalid.
The reuse of a BAT ID in an update is only allowed if the updated BAT ID was invalid before. The updated BAT ID must be marked valid.
The reception of the requested BAT frame is confirmed by the recipient by using the latest updated BAT for a transmission towards the sender of the requested BAT frame.
Loss of a requested BAT frame can be detected through usage of invalid BAT IDs in a subsequent reception.
Coordinator
Device
control frame
update BAT 2 invalid: BAT 1
update BAT 2 invalid: BAT 1
data / management frame
using BAT 1
using BAT 2
update BAT 1 …
invalid: BAT 2
retransmit
… until update needed …
invalid!
frame is lost

## Slide 10: Requested BAT frame example
Example of the requested BAT frame for the HB-PHY with 512 subcarriers:
Here it is indicated that only the BATs 1, 5 and 14 can be used for transmissions towards the sender of the requested BAT frame.
BAT 1 is updated for the given FEC and two groups of subcarriers, loaded with 8 and 6 bits respectively
The recipient of the requested BAT frame knows that the second group of subcarriers is the last group as it specifies more than the actual number of subcarriers.
The excess subcarriers of the second group are ignored and not modulated
Valid BATs | Updated BAT | FEC | Grouping of Group 1 | Loaded Bits in Group 1 | Grouping of Group 2 | Loaded Bits in Group 2
1, 5, 14 | 1 | CR: 5/6 BS: 960 | 128 | 8 | 512 | 6
Excess carriers
that do not
apply are
ignored

## Slide 11: Adaptive modulation and coding feedback
Requested MCS control frame sent to request the usage of a specific MCS.
Same procedure as for requested BAT frame, but an MCS is requested.
When transmitter does not apply a correct MCS, control frame is repeated.
Bits: 0-7
Requested MCS

## Slide 12: Dynamic GTS Descriptor
GTS descriptor
GTS allocations via the GTS update frame or via the beacon frame as already present in the standard
Validity field specifies number of superframes the GTS is valid in
Only the first applying GTS directions are considered. Excess bits are ignored
GTS descriptor list
Bits: 0-7 | 8 | 9-15 | variable | variable
GTS Descriptor Count | Validity Present | reserved | GTS Directions | GTS Descriptors
? | ? | 0/8
GTS Start Slot | GTS Length | Validity

## Slide 13: Typical superframe
New devices or devices that lost the connection and do not have GTSs allocated can transmit association requests and reconnection feedback frames in the CAP.
All other control- management- and data transmissions are performed in GTS in the CFP
CO
DEV
BP
CFP
CAP
beacon
Multi-cell channel est.
channel est.
macro slot
control frame
management frame
IDLE
IDLE
IDLE
data frame