## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: OWC Link Using Transparent Display for Automatic Railroad Switching Solution
Date Submitted: September 2018
Source: Jaesang Cha, Minwoo Lee (SNUST), Hyoungkyu Song(Sejong Univ.), Soonho Jung(Sunil Elecomm Co., LTD.), Sooyoung Chang (SYCA) , Vinayagam Mariappan (SNUST)
Address: Contact Information: +82-2-970-6431, FAX: +82-2-970-6123, E-Mail: chajs@seoultech.ac.kr
Re:
Abstract: This documents introduce the V2X camera communication Link design consideration for VAT. This proposed OWC Link Using Transparent Display for automatic railroad switch guiding solution. This VAT to operate on the application services like ITS, ADAS, IoT/IoL, etc. on road condition. Also this can be used for LEDIT, Digital Signage with connected information services etc.
Purpose: To provided concept models of VLC technology solution for Vehicular Assistant Technology (VAT) Interest Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2
Contents
Need for Automatic Railroad Switching Solution
OWC Link Using Transparent Display Technology
Conclusion
Slide 2

## Slide 3
Slide 3
Need for Automatic Railroad Switching Solution
Needs
  Railroad switch is a mechanical installation enabling railway trains to be guided from one track to another, such as at a railway junction or where a spur or siding branches off.
  Some times it happens that switch mechanism position is poorly visible or is set to the wrong way even though it shows correct switching position
  Wrong switched way may steer a train in the wrong direction or even worse, lead to an accident.
  Needs to provide proper track switching to avoid train accidents
Basic Concept
  Propose the OWC technology solutions to for right automatic railroad switch based on Train pathway to prevent train collisions
  Uses the Train Engine Windshield as Transmitter and CCTV installed in Railroad station as a receiver
  The switch mechanism operated remotely using an electric motor or hand-operated lever or from a nearby ground frame .
  Avoids wrong path directions and Train accidents
GOOGLE
  < Railroad Switching Scenario >

## Slide 4
Slide 4
OWC Link Using Transparent Display Technology
  < OWC Link Using Transparent Display Technology in Train >
OWC Link Using Transparent Display Technology
  Tx : Train Windshield Transparent Display
  Rx : CCTV Camera
  Day-Night Communication Mode
  Modulations :
    VTASC, SS2DC, OOK, VPPM, Offset-VPWM, Multilevel PPM, Inverted PPM, Subcarrier PPM, DSSS SIK etc.
  Data Rate : 1K ~ 1Mb/s
  Supported LoS (Line of Sight)
  Available Distance : 2m ~ 200m

## Slide 5
Proposed the OWC Link Using Transparent Display for Automatic Railroad Switching Solution
Uses the Train Engine Windshield as Transmitter and CCTV installed in Railroad station as a receiver
This solution may prevent railway wrong path guidance and accidents or collisions.
Slide 5
Conclusion