## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE P802.15.13 – Variable MAC frame format using information elements
Date Submitted: 23 Okt. 2018
Source: Kai Lennert Bober, Volker Jungnickel [Fraunhofer HHI]
Address: Einsteinufer 37, 10587 Berlin, Germany
Voice:[+49-30-31002 302], E-Mail:[kai.lennert.bober@hhi.fraunhofer.de]
Voice:[+49-30-31002 768], E-Mail:[volker.jungnickel@hhi.fraunhofer.de]
Re:
Abstract:
Purpose: Contribution to IEEE P802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15.13 Variable MAC frame format using information elements
Date: 2018-10-23
Authors:

## Slide 3: Content
This doc. contains a proposal to introduce variable information elements (IEs) in the MAC frame, similar to the MAC frame defined by IEEE 802.15.4.

## Slide 4: Current state of the MAC frame
The general MAC frame format was covered in documents
  15-18-0185-01-0013
  15-18-0269-00-0013
  15-18-0270-05-0013
Frame formats for management and control frames were proposed in document
  15-18-0393-02-0013

## Slide 5: Latest proposed general MAC header format
Octets: 2 | 0/2 | 6 | 0/6 | 0/6 | 0/2 | 0/6 | 0/5/6/10 /14 | variable | 4
Frame control | ACK information | Receiver Address | Transmitter Address | Auxiliary Address 1 | Sequence control | Auxiliary Address 2 | Auxiliary security header | Frame payload | FCS
MHR |  |  |  |  |  |  |  | MSDU | MFR
Bits: 0-1 | 2-7 | 8 | 9 | 10 | 11 | 12 | 13-15
Frame version | Frame type / subtype | To backhaul | From backhaul | Security enabled | ACK request | ACK info | Reserved
General MAC frame format
Frame control field
Bits: 0-4 | 5-13 | 14-15
Device address | Sequence number | ACK
ACK information field
Bits: 0-3 | 4-15
Fragment Number | Sequence number
Sequence control field
? | ?
? | ?
Auxiliary security header

## Slide 6: Open questions regarding frame fields
Some polling-specific functionality is present in the general MAC frame format. Can we omit it for the reservation-based scheme?
Can the short address be reintroduced in the MAC frame header?
Is the Auxiliary Address 2 ever used?
Why does the device address in the ACK info field only have 5 bits?
  Is it required at all?
Why 2 bits for ACK?
  ACK, NACK, ?
If we have a fragment number in the MAC header, we also need at least a “more fragments” bit.

## Slide 7: Option 1: restructure MAC frame format based on the use of information elements
MAC header includes core information
Information required for specific purposes is kept in so called Information Elements (IEs)
Variable number of IEs is added between “core header” and payload
Octets: 2 | 2/6 | 2/6 | 0/2 | variable | variable | variable | variable | 4
Frame control | Receiver Address | Transmitter Address | Sequence Control | Auxiliary Security Header | IEs |  | Frame Payload | FCS
 |  |  |  |  | Header IEs | Payload IEs |  | 
MHR |  |  |  |  |  | MSDU |  | MFR

## Slide 8: Essential fields contained in “core header”
Bits: 0-1 | 2-7 | 8 | 9 | 10 | 11 | 12-15
Frame version | Frame Type / Subtype | Short Address Used | Sequence Enabled | Security Enabled | IEs Present | Reserved
Frame control field
TBD | TBD
TBD | TBD
Auxiliary security header field
Bits: 0-3 | 4 | 5-15
Fragment Number | More Fragments | Sequence Number
Sequence control field

## Slide 9: Move specific fields into IEs in header and in payload
Bits: 0-48 | 5-13 | 14-15
Device Address | Sequence Number | ACK
Example: IE Content for ACK IE
Other IEs:
  Backhaul integration (auxiliary address fields)
  …
Bits: 0-6 | 7-14 | 15 | Octets: 0-127
Length in octets | Element ID | Type = 0 | Content
Bits: 0-6 | 7-14 | 15 | Octets: 0-127
Length in octets | Element ID | Type = 1 | Content
Header IE format:
Payload IE format:

## Slide 10: Option 2: preserve currently proposed MAC frame header and only add IEs
Keep the proposed general MAC header
But: (re-)enable short representation for receiver and transmitter addresses via bit in frame control
Add optional header and payload IEs after MAC header
Add „IEs present“ field to Frame Control
Add addressing mode field to Frame Control
Octets: 2 | 0/2 | 2/6 | 0/2/6 | 0/6 | 0/2 | 0/6 | variable | variable | variable | variable | 4
Frame Control | ACK Information | Receiver Address | Transmitter Address | Auxiliary Address 1 | Sequence Control | Auxiliary Address 2 | Auxiliary Security Header | IEs |  | Frame Payload | FCS
 |  |  |  |  |  |  |  | Header IEs | Payload IEs |  | 
MHR |  |  |  |  |  |  |  |  | MSDU |  | MFR

## Slide 11: What happens with the frame type?
If IEs are used, why do we need a frame type?
In theory, a single general MAC frame format could be used with all types of frame
For further discussion…