## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4w Fraunhofer IIS proposal performance enhancements]
Date Submitted: [13 November, 2018]
Source: [Johannes Wechsler] Company [Fraunhofer Institute for Integrated Circuits IIS]
Address [Nordostpark 84, Nuremberg, 90411, Bavaria]
Voice:[ +49 911 58061-3334], FAX: [+49 911 58061-3299], E-Mail:[johannes.Wechsler@iis.fraunhofer.de]
Re: [802.15.4w Fraunhofer IIS proposal discussion slides, IEEE 802.15-18-0447-01-004w]
Abstract: [Enhancements for the proposal of Fraunhofer IIS for 802.15.4w.]
Purpose: [Show minor adjustments to the initial proposal which have impact on PHY performance.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4w Fraunhofer IIS proposal performance enhancements
Johannes Wechsler
Fraunhofer IIS

## Slide 3: Topics
Interleaver for Rate 1/3 Convolutional Code
SFD for Sub-Packets
SFD for Synchronisation Sub-Packets

## Slide 4: Interleaving Proposal Recap (1)
Standard block interleaver with a number of columns that corresponds to the number of sub-packets J
Input
c0 , c1 , c2 , c3 , …… , cIJ-3 , cIJ-2 , cIJ-1
c2J
c0
cJ
c(I-1)J
c2J+1
c1
cJ+1
c(I-1)J+1
c2J+2
c2
cJ+2
c(I-1)J+2
c3J-2
cJ-2
c2J-2
cIJ-2
c3J-1
cJ-1
c2J-1
cIJ-1
read I rows sequentially
write J columns sequentially
Output
c0 , cJ , c2J , c3J , …… , c(I-2)J-1 , c(I-1)J-1 , cIJ-1

## Slide 5: Current Performance
c2J
c3J
c0
cJ
c(I-1)J
pM-1
p1
pM-2
p0
c2J+1
c3J+1
c1
cJ+1
c(I-1)J+1
pM-1
p1
pM-2
p0
c2J+2
c3J+2
c2
cJ+2
c(I-1)J+2
pM-1
p1
pM-2
p0
c2J+3
c3J+3
c3
cJ+3
c(I-1)J+3
pM-1
p1
pM-2
p0
c3J-2
c4J-2
cJ-2
c2J-2
cIJ-2
pM-1
p1
pM-2
p0
c3J-1
c4J-1
cJ-1
c2J-1
cIJ-1
pM-1
p1
pM-2
p0
SHR
sub-packet 1
sub-packet 2
sub-packet 3
sub-packet 4
sub-packet J-1
sub-packet J
PSDU

## Slide 6: Performance for Rate 1/3 Convolutional Code
18 Sub-packets per transmission
  Rate 1/3 should theoretically allow successful reception when only 6 sub-packets are received
Actual performance of the standard block interleaver lacks behind expectation

## Slide 7: Performance of proposed interleaver
green: collision probability
black: performance of proposed block interleaver

## Slide 8: Performance for Rate 1/3 Convolutional Code
Introduce cyclic shift of rows:
  1st row is shifted by 0
  2nd row is shifted by 1
  3rd row is shifted by 2
  …
Performance of cyclically shifted achieves close to the expected performance to withstand loss of 12 sub-packets

## Slide 9: Cyclic shift of PSDU bits
c3J-2
c4J-3
c0
c2J-1
cIJ-2
pM-1
p1
pM-2
p0
c3J-1
c4J-2
c1
cJ
cIJ-1
pM-1
p1
pM-2
p0
c2J
c4J-1
c2
cJ+1
c(I-1)J+1
pM-1
p1
pM-2
p0
c2J+1
c3J
c3
cJ+2
c(I-1)J+2
pM-1
p1
pM-2
p0
c3J-4
c4J-5
cJ-2
c2J-3
cIJ-4
pM-1
p1
pM-2
p0
c3J-3
c4J-4
cJ-1
c2J-2
cIJ-3
pM-1
p1
pM-2
p0
SHR
sub-packet 1
sub-packet 2
sub-packet 3
sub-packet 4
sub-packet J-1
sub-packet J
PSDU

## Slide 10: Performance of cyclically shifted interleaver
green: collision probability
black: performance of cyclic shifted block interleaver

## Slide 11: TG Motion #
Move to incorporate the cyclically shifted interleaver into the draft, replacing the previously suggested non-shifted block interleaver.
Moved by:
Seconded by:
Motion

## Slide 12: SFD for sub-packets
Current SFD is designed for compatibility and good phase estimation
Proposed SFD includes 101010 sequence which might be problematic
  Detection in fragmented systems with preamble not ideal
New SFD with same performance characteristics
Bits | 0–3 | 4–15
Bit map | 0101 | 1101 1110 1000

## Slide 13: TG Motion #
Move to replace the originally proposed SFD for sub-packets in the draft with the one suggested in this slide deck on slide 12.
Moved by:
Seconded by:
Motion

## Slide 14: Synchronization sub-packets

## Slide 15: SFD for synchronization sub-packets
SFD for normal sub-packets ideal for phase estimation
Detection with only 3 sub-packets difficult and computationally expensive
Phase estimation performance irrelevant for initial detection
New SFD for synchronisation sub-packets:
  Modulated MSK sequence of 1111 1111 0101 0101
  Which leads to two distinct peaks in the frequency spectrum
  Simple to detect
  Processing required only FFT, no sophisticated algorithms
  Good support for low-power receivers
  Simulations show detectability at Low-SNR required for LPWAN

## Slide 16: Synchronization on Low Power / Low Performance Receivers
Limited computational power
Step-by-step Algorithm
  FFT of sufficient resolution over the search window
  Check absolute values of frequency bins against threshold
  Check distance between bins above threshold
    Distance equals expected distance
    synchronization sub-packets detected  try to decode information
    No bins above threshold OR Bins above threshold are not in expected distance to one another
     no synchronization sub-packets detected  continue search / sleep

## Slide 17: Rx Sample Bandwidth determination

## Slide 18: Example for synchronization sub-packets
Symbol Rate: 2380 Hz
Channel Spacing: 12 * 2380 Hz = 28.6 kHz
  12 sub-channels, synchronization always on sub-channel 0
3 synchronization sub-packets
  Transmit signal bandwidth: (12 + 12 + 1) * 2380 = 59.6 kHz
+-20 ppm crystal tolerance at 1 GHz = +- 20 kHz
   Tolerance at transmitter and at receiver  +- 40 kHz total
Rx reception window bandwidth required  140 kHz

## Slide 19: TG Motion #
Move to incorporate the usage of the newly proposed SFD for synchronization sub-packets into the draft.
Moved by:
Seconded by:
Motion

## Slide 20: Thank you!
Any questions or suggestions?