## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Inclusion of Multicast/Broadcast Ranging in Information Element
Date Submitted: November 2018
Source: Seongah Jeong, Yi Yang, Hyunchul Kim, Sejong Yoon, Jong-Hoon Jang, Moon-Seok Kang, Jonghyo Lee, Aditya V. Padaki, Zheda Li, Boon Loong Ng (Samsung), Frank Leong, Brima Ibrahim, Rias Al-kadi (NXP)
Company: Samsung
E-Mail: sa.jeong@samsung.com,yi83.yang@samsung.com,hc77.kim@samsung.com,sejong.yoon@samsung.com,jh0.jang@samsung.com,moonseok.kang@samsung.com,jonghyo.lee@samsung.com,a.padaki@samsung.com,zheda.li@samsung.com,b.ng@samsung.com,frank.leong@nxp.com,brima.ibrahim@nxp.com,rias.al-kadi@nxp.com
Abstract: []
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: The aim of this presentation:
We support on-going discussion for ranging method in TG4Z
  Using ranging methods and information element (IE) from 802.15.8 in <15-18-0108-03-004z-hrp-uwb-phy-enhancements.pptx>
  Revising text 15-15-0429-01-0008 for TG4z in <15-18-0503-00-004z-status-of-draft-editing-wk4218.pptx>
Note: Notation/nomenclature based on 15-15-0429-01-0008 and 802.15.8

## Slide 3: The aim of this presentation:
We suggest multicast/broadcast ranging method based on double-sided two-way ranging (DS-TWR)
  Multicast/broadcast ranging method is conceptually introduced in <15-18-0286-01-004z-hrp-uwb-srdev-ppdu-text-contribution>
We suggest improvements on the existing IE in 802.15.8 for supporting multicast/broadcast ranging method
Note: Notation/nomenclature based on 15-15-0429-01-0008 and 802.15.8

## Slide 4: Overview
Need for Multicast/Broadcast Ranging
Proposed Multicast/Broadcast DS-TWR
Proposed Improvements on IE
Conclusions

## Slide 5: Need for Multicast/Broadcast Ranging
The symmetric DS-TWR in Annex D1.3.2 of 802.15.4a-2007 is discussed in 802.15.8 as DS-TWR with payload IEs for each transmission
The DS-TWR is defined for one-to-one case in 802.15.8
For use cases where one device needs to simultaneously range with N multiple nodes, N number of sequential one-to-one DS-TWR procedures need to be considered with the existing payload IEs
This will increase traffic considerably and will lead to increased power/energy consumption and increased latency

## Slide 6: Reference (802.15.8)
For DS-TWR between two devices, A and B, we need three messages
  Transmitted message from A initiating ranging procedure (“ranging poll”)
  Response message from B initiating 2nd round trip measurement (“ranging response”)
  Retransmitted message from A completing DS-TWR exchange (“ranging final”)
For Device B to calculate the estimated time of flight (ToF) Tprop,
  Device A needs to communicate its round-trip time Tround1 & reply time Treply2 to Device B
802.15.8 employs payload IEs to control DS-TWR and transfer ranging data in a ranging exchange
Figure 116 —Double-sided two-way ranging with three messages

## Slide 7: Reference (802.15.8)
Figure 121 —Message sequence chart for DS-TWR
with three messages
DS-TWR is initiated by a ranging data frame carrying a Ranging Control Double-sided TWR IE (RCDT IE) with control field set to 0 or 1 according to Table 147
The responding side initiates the second with ranging data frame carrying a Ranging Control Double-sided TWR IE (RCDT IE) with control field set to 2 according to Table 147 and also carrying a Ranging Request Reply Time IE (RRRT IE)
The original initiator completes the exchange by sending a final ranging data frame carrying the first round trip time measurement (Tround1) in an Ranging Round Trip Measurement IE (RRTM IE) and the reply time (Treply2) of this second first round trip measurement in an Ranging Reply Time Instantaneous IE (RRTI IE)
Octets: 1
Control Info
Control Info value | Meaning
0 | This frame is initiating DS-TWR and indicates that the initiating end does not require the ranging result.
1 | This frame is initiating DS-TWR and requesting that the ranging result is sent back at end of exchange
2 | This frame is continuing the DS-TWR, forming the request for the 2nd TX-to-RX round trip measurement
Table 147 —Values of the Control Info field in the Ranging Control Double-sided TWR (RCDT) IE
Figure 111 —Ranging Control Double-sided TWR (RCDT) IE Content field format

## Slide 8: Need for Multicast/Broadcast Ranging
For use cases where one device needs to simultaneously range with N multiple nodes, N number of sequential one-to-one DS-TWR procedures need to be considered with the existing payload IEs
  This will increase traffic considerably and will lead to increased power/energy consumption and increased latency
  Each ranging/secure ranging device (RDEV/SRDEV) calculates ToF from the equation in 802.15.8
(Ranging final)
(Ranging poll)
(Ranging response)
Device A
Device 1
(Ranging poll)
(Ranging response)
Ranging
Device 2
Device N
...
Ranging
Ranging
(Ranging final)
(Ranging final)
(Ranging poll)
(Ranging response)

## Slide 9: Proposal
We propose to consider Broadcast/Multicast DS-TWR following multicast/broadcast ranging in <15-18-0286-01-004z-hrp-uwb-srdev-ppdu-text-contribution.docx>
  Ranging poll and ranging final messages are broadcasted/multi-casted from initiating RDEV/SRDEV which is an efficient way in the aspect of number of transmissions
    Each RDEV/SRDEV still can calculate ToF from the equation in 802.15.8
    The timestamp measurements maybe encrypted for different users with different keys for security (Ranging final/Multicast)
Device A
Device 1
Broadcast/multicast (Ranging poll)
(Ranging response)
Broadcast/multicast (Ranging final)
Ranging
Device 2
Device N
...
(Ranging response)
(Ranging response)
Ranging
Ranging
*Broadcast/multicast single-sided TWR can be considered

## Slide 10: Proposal
For the support of the broadcast/multicast DS-TWR, we propose the additional control info value of RCDT IE
The newly defined control info values 3~7 for content field of RCDT IE are proposed as below
Control Info Value | Meaning
0 | This frame is initiating DS-TWR and indicates that the initiating end does not require the ranging result.
1 | This frame is initiating DS-TWR and requesting that the ranging result is sent back at end of exchange
2 | This frame is continuing the DS-TWR, forming the request for the 2nd TX-to-RX round trip measurement
3 | This frame is initiating broadcast/multicast DS-TWR and indicates that the initiating end does not require the ranging result
4 | This frame is initiating broadcast/multicast DS-TWR and requesting that the ranging result is sent back at end of exchange
5 | This frame is initiating broadcast/multicast DS-TWR with additional report message for time stamp measurements and indicates that the initiating end does not require the ranging result
6 | This frame is initiating broadcast/multicast DS-TWR with additional report message for time stamp measurements and requesting that the ranging result is sent back at end of exchange
7 | This frame indicates Ranging Final message without timestamps in the broadcast/multicast DS-TWR
Octets: 1
Control Info
Content field of RCDT IE
Device A
Device B
RCDT IE (Ranging poll)
RCDT(2) IE, RRRT IE (Ranging response)
Ranging
…
RCDT IE (Ranging final)

## Slide 11: Example of RCDT (3) IE
Device A
Device 1
RCDT(3) IE (Ranging poll)
RCDT(2) IE, RRRT IE (Ranging response)
[RRTI IE, RRTM IE] [RRTI IE, RRTM IE] … [RRTI IE, RRTM IE] (Ranging final)
Ranging
Device 2
Device N
...
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(2) IE, RRRT IE (Ranging response)
Ranging
Ranging
This frame is
initiating broadcast/multicast DS-TWR and
indicates that the initiating end does not require the ranging result (ToF)

## Slide 12: Example of RCDT (4) IE
Device A
Device 1
RCDT(4) IE (Ranging poll)
RCDT(2) IE, RRRT IE (Ranging response)
[RRTI IE, RRTM IE] [RRTI IE, RRTM IE] … [RRTI IE, RRTM IE] (Ranging final)
Ranging
Device 2
Device N
...
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(2) IE, RRRT IE (Ranging response)
Ranging
Ranging
RTOF IE (Ranging measurement)
RTOF IE (Ranging measurement)
RTOF IE (Ranging measurement)
This frame is
initiating broadcast/multicast DS-TWR and
requesting that the ranging result (ToF) is sent back at end of exchange

## Slide 13: Example of RCDT (5)/RCDT (7) IE
Device A
Device 1
RCDT(5) IE (Ranging poll)
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(7) IE (Ranging final)
Ranging
Device 2
Device N
...
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(2) IE, RRRT IE (Ranging response)
Ranging
Ranging
[RRTI IE, RRTM IE] [RRTI IE, RRTM IE] … [RRTI IE, RRTM IE] (Additional report)
The frame with RCDT (5) IE is
initiating broadcast/multicast DS-TWR with additional report message for time stamp measurements (RRTI IE, RRTM IE), not in Ranging final message and
indicates that the initiating end does not require the ranging result (ToF)
The frame with RCDT (7) IE indicates Ranging Final message without timestamps in the broadcast/multicast DS-TWR

## Slide 14: Example of RCDT (6)/RCDT (7) IE
Device A
Device 1
RCDT(6) IE (Ranging poll)
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(7) IE (Ranging final)
Ranging
Device 2
Device N
...
RCDT(2) IE, RRRT IE (Ranging response)
RCDT(2) IE, RRRT IE (Ranging response)
Ranging
Ranging
[RRTI IE, RRTM IE] [RRTI IE, RRTM IE] … [RRTI IE, RRTM IE] (Additional report)
RTOF IE (Ranging measurement)
RTOF IE (Ranging measurement)
RTOF IE (Ranging measurement)
The frame with RCDT (6) IE is
initiating broadcast/multicast DS-TWR with additional report message for time stamp measurements (RRTI IE, RRTM IE), not in Ranging final message and
requesting that the ranging result (ToF) is sent back at end of exchange
The frame with RCDT (7) IE indicates Ranging Final message without timestamps in the broadcast/multicast DS-TWR

## Slide 15: Conclusions
We support using ranging methods and payload IEs from 802.15.8
For use cases where one device needs to simultaneously range with multiple nodes, efficient support for DS-TWR is required for traffic, power/energy consumption and latency
Considering multicast/broadcast DS-TWR with the additional control info value of RCDT IE is proposed

## Slide 16
THE END