## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Inclusion of Ranging FoM in Information Element
Date Submitted: November 2018
Source: Seongah Jeong, Yi Yang, Hyunchul Kim, Sejong Yoon, Jong-Hoon Jang, Moon-Seok Kang, Jonghyo Lee, Aditya V. Padaki, Zheda Li, Boon Loong Ng (Samsung), Rias Al-kadi (NXP)
Company: Samsung
E-Mail: sa.jeong@samsung.com,yi83.yang@samsung.com,hc77.kim@samsung.com,sejong.yoon@samsung.com,jh0.jang@samsung.com,moonseok.kang@samsung.com,jonghyo.lee@samsung.com,a.padaki@samsung.com,zheda.li@samsung.com,b.ng@samsung.com,rias.al-kadi@nxp.com
Abstract: []
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: The aim of this presentation:
We support on-going discussion for ranging method in TG4Z
  Using ranging methods and Information Element (IE) from 802.15.8 in <15-18-0108-03-004z-hrp-uwb-phy-enhancements.pptx>
  Revising text 15-15-0429-01-0008 for TG4z in <15-18-0503-00-004z-status-of-draft-editing-wk4218.pptx>
We suggest improvements on timestamp measurement-related payload IE in 802.15.8

## Slide 3: Overview
Need for Inclusion of Ranging FoM in IE
Proposed Improvements on IE
Conclusions

## Slide 4: Need for Inclusion of Ranging FoM in IE
There are timestamp measurement-related payload IEs in 802.15.8 for
  Rx-to-Tx reply time
    Ranging reply time instantaneous (RRTI) IE
    Ranging reply time deferred (RRTD) IE
  TX to RX round-trip time
    Ranging round trip measurement (RRTM) IE
Ranging FoM (Figure of Merit) of ranging counter is needed so that the application can decide whether the timestamp measurements are usable or not
Also, we may need a measure to check whether timestamp measurements are obtained via Scrambled timestamp sequence (STS) so that the receiver-side can distinguish it in IE for efficiency
Octets: 4
RX to TX reply time or TX to RX round-trip time
Content field of RRTI IE/RRTD IE/RRTM IE

## Slide 5: Proposal
We propose the addition of 1byte content field for Ranging FoM to the existing 4byte content field defined in 802.15.8
  Ranging FoM field follows the same frame structure defined in IEEE Std 802.15.4-2015
    Except modifying the meaning of extension bit 7 based on STS’s success or failure
  The content fields of timestamp measurement-related IEs are proposed as below
Octets: 4 | Octets: 0/1
RX to TX reply time or TX to RX round-trip time | Ranging FoM
Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Extension | Confidence Interval Scaling Factor field |  | Confidence Interval field |  | Confidence Level field |  | 
RRTI IE/RRTD IE/RRTM IE

## Slide 6: Proposal
Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Extension | Confidence Interval Scaling Factor field |  | Confidence Interval field |  | Confidence Level field |  | 
Confidence level | Bit 2 | Bit 1 | Bit 0
No FoM | 0 | 0 | 0
20% | 0 | 0 | 1
55% | 0 | 1 | 0
75% | 0 | 1 | 1
85% | 1 | 0 | 0
92% | 1 | 0 | 1
97% | 1 | 1 | 0
99% | 1 | 1 | 1
Confidence interval | Bit 4 | Bit 3
100 ps | 0 | 0
300 ps | 0 | 1
1ns | 1 | 0
3ns | 1 | 1
Confidence interval scaling factor | Bit 6 | Bit 5
Confidence interval x 1/2 | 0 | 0
Confidence interval x 1 | 0 | 1
Confidence interval x 2 | 1 | 0
Confidence interval x 4 | 1 | 1
FoM value meaning with the extension bit set | Bit 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ranging FoM value if the timestamp measurement is obtained without STS | 0 | Any nonzero value |  |  |  |  |  | 
The timestamp report is uncorrected | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ranging FoM Value if the timestamp measurement is obtained with STS | 1 | Any nonzero value |  |  |  |  |  | 
Bit 6 to 0 are equivalently defined in Ranging FoM definition in 802.15.4-2015
FoM value meaning according to extension bit set is modified based on STS consideration
Octets: 4 | Octets: 0/1
RX to TX reply time or TX to RX round-trip time | Ranging FoM

## Slide 7: Conclusions
We support using ranging methods and payload IEs from 802.15.8
Application requires Ranging FoM to decide whether the timestamp measurements are usable or not
Addition of content field for Ranging FoM to timestamp measurement-related IEs is proposed

## Slide 8
THE END