## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Open points in IEEE P802.15.13
Date Submitted: 13. November 2018
Source: Kai Lennert Bober [Fraunhofer HHI]
Address: Einsteinufer 37, 10587 Berlin, Germany
Voice:[+49-30-31002 302], E-Mail:[kai.lennert.bober@hhi.fraunhofer.de]
Re:
Abstract:
Purpose: Contribution to IEEE P802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: Open points in the IEEE P802.15.13
Date: 2018-11-13 Place: Bangkok, Thailand
Authors:
Name | Company | Address | Phone | Email
Kai Lennert Bober | Fraunhofer HHI |  |  | kai.lennert.bober@hhi.fraunhofer.de

## Slide 3: Content
This doc. lists unresolved issues and open points that are, in the author’s opinion, required for the finalization of the standard.

## Slide 4: IEEE 802 LAN integration
Will 802.15.13 networks appear as general purpose LANs?
  IEEE 802-2014: new standards shall support Ethertype Protocol Discrimination (EPD) 
    MSDU format must include Ethertype (e.g. like in IEEE 802.15.3-2016, Multi-Potocol Data Frame)
    OR: Ethertype must be part of the MAC data frame
Current state of the draft: upper layer like e.g. ZigBee for 802.15.4. No generic integration with e.g. Ethernet / LANs

## Slide 5: Aggregation
Problem: if a PPDU is transmitted for every MSDU, throughput at the MAC-SAP is suboptimal for small (but also reasonably sized) MSDUs.
  Imagine 64 byte MSDU occupying the channel for ~40µs (due to PHY preamble, PHY header + data symbol)
  Actual payload takes maybe 1 symbol in the PPDU
  BUT: Theoretical throughput limit at 12.2 Mbit/s
Possible solutions: MSDU aggregation

## Slide 6: Fragmentation
Problem: large MSDUs may take long to be transmitted
  Imagine 1518 byte being transmitted at PHY rate 10 Mbit/s
  Data transmission takes 1.1 ms
  11 ms at 1 Mbit/s
Transmitters monopolize channel time.
GTSs may not be long enough to transmit MSDU at all
Fragmentation is partially present in the data frame format (fragment number in sequence control).
  Last fragment indication is needed

## Slide 7: Security
Security is a skeleton currently
Proposed solution:
  Copy existing security (via auxiliary security header & payload encryption) from ongoing update to 802.15.4 security

## Slide 8: Quality of Service
PAR states industrial communication as use case
No mechanisms for QoS are present
  MSDU priority?
  Flow resource reservation / TSPECs?