## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY/MAC enhancements for Secure Ranging Devices]
Date Submitted: [14 November 2018]
Source: Dr. David Barras, Dr. Boris Danev (3db Access), Bernd Baer (Marquardt), Dr. Peter Sauer (Microchip Technology)
Re: [Frame format and modes revision for LRP UWB PHY]
Abstract: [Contribute a proposal to the enhanced impulse radio group w.r.t. the LRP UWB PHY ]
Purpose: [Propose elements of Secure Authenticated Ranging PHY/MAC descriptions 802.15.4z]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Scope
Definition of a frame format for 4z LRP SRDEV
Revision of modes for 4z LRP SRDEV
Motivation
Enhanced performance with authentication schemes
Interoperability

## Slide 3: 15.4 Frame format
    802.15.4 PHY and MAC are providing a frame format for secure ranging protocol (such as distance bounding protocols enabled by LRP PHY)
    802.15.4 frame format enables secure ranging with one-way and mutual authentication
    LRP with distance commitment on data portion (enabled distance bounding mechanisms) is thus fully compliant with PHY, MAC and MAC Security of 15.4 as defined in Clause 9
(Default, mandatory)
SHR
PHR
PHY Payload

## Slide 4: Frame format
    Optimized frame format for secure ranging with tolerance to bit errors (cf. 15-18-0301-01-004z)
    Proposal for a optimized frame format for LRP SRDEV
    PHY Payload
      Contains only the Nv and Np pulses (challenges)
      No frame number nor other MAC related overhead
    Benefits
      Enables increased link budget because all pulse energy is used only for packet synchronization and security proof
      Improves secure ranging link budget by 5.5 – 7.5 dB when some bit error are tolerated (on the demodulation scheme and #errors)
SHR
PHY Payload
(Mandatory)

## Slide 5: Frame format
    PHY Payload definition
      Nv/Np between 64 and 512 pulses for interoperability
      Define Nv/Np number of pulses for standardized Security Levels
      With distance commitment on top, 4z LRP provides a distance bounding protocol with well-defined and quantified security guarantees  application-specific flexibility
Security Level | Nv/Np # pulses | Security guarantee
0 | 64 | >= 32 bits (@BER<10%)
1 | 128 | >= 64 bits (@BER<10%)
2 | 256 | >= 128 bits (@BER<10%)
3 | 512 | >=256 bits (@BER<10%)

## Slide 6: Preamble and SFD
    Frame format for secure ranging with one-way and mutual authentication
      Extend to max. 256 in all modes (esp. Base mode) to improve preamble strength for tolerating up to 10% errors in Nv/Np
      Define SFD of 32 pulses in addition to SFD 16 pulses for more robust synchronization
      Evaluation of SFD is ongoing in coordination with other LRP vendors
SFD (b0 – b31)
0000 xxxx ….

## Slide 7: Modes for LRP and LRP SRDEV
    To add in Clause 17:
      Revised 15-18-0218-01-004z-changes-proposal-for-lrp-uwb-phy.docx
Dual-frequency 4.0 6 4 Mb/s 2-FSK mandatory Mode (SRDEV) Extended dual-freq 4.0 7 1 Mb/s 2-FSK optional Mode (SRDEV)
mandatory (SRDEV)

## Slide 8: Summary
    We proposed a optimized frame format for one-way and mutual authentication in LRP to improve performance
    LR dual-frequency modes with higher PRF to reduce packet durations in SRDEVs

## Slide 9: Q & A