## Slide 1: IEEE 802.15.4-2015 HRP UWB PHY Suggested Changes
Robert Golshan
Apple Inc.
15 January 2019

## Slide 2: Page 447: Last paragraph
FROM: “Table 16-1 and Table 16-2 show how the SHR field, H0-H18, PHY Payload field, D0-DN-1, and Tail field, T0-T1, are mapped onto the symbols.”
TO: “Table 16-1 and Table 16-2 show how the PHR field, H0-H18, PHY Payload field, B0-BN-1, and Tail field, T0-T1, are mapped onto the symbols.”
Comments: “SHR” is a typo. Also, use “B” instead of “D” to avoid confusion with “D” used in Section 16.3.3.1 (c), page 462, which denotes input information symbols into the Reed-Solomon encoder. “B” is consistent with the notation used in Figure 16-10, page 461.

## Slide 3: Page 448-9: Tables 16-1 and 16-2
Table captions:
  FROM: “Mapping of SHR field bits, ...”
  TO: “Mapping of PHR field bits, ...”
  Comments: SHR is a typo.
Table entries:
  Change all instances of “D” to “B” to avoid confusion with “D” used in Section 16.3.3.1 (c), page 462, which denotes input information symbols into the Reed-Solomon encoder. “B” is consistent with the notation used in Figure 16-10, page 461.

## Slide 4: Page 454: 1st paragraph of 16.5.4
FROM: “Four mandatory preambles are defined: a default preamble, a short preamble, a medium preamble, and a long preamble. The preamble to be used in the transmission of the current frame is determined by the value of the HrpUwbPreambleSymbolsRepetitions parameter in the MCPS-DATA.request primitive.”
TO: “Four mandatory preamble durations are defined: a default preamble duration, a short preamble duration, a medium preamble duration, and a long preamble duration. The preamble duration to be used in the transmission of the current frame is determined by the value of the HrpUwbPreambleSymbolsRepetitions parameter in the MCPS-DATA.request primitive.”
Comments: This paragraph is referring to the number of symbols in the sync sequence (denoted in Table 16-5), i.e. the number times a given ternay sequence is repeated, not the sequence itself (there are more than four sequences defined in Tables 16-6 and 16-7). Inserting the word “duration” will make it clear and also bring this text into agreement with Table 16-9 (on page 458), where “duration” is also mentioned.

## Slide 5: Page 452: Table 16-4 (change 1 of 3)
From:
To:
Comments: Adds clarity to formula on page 456, and Figure 16-5 on page 457 (see next 2 slides).
Channel Number | Code Length | Peak PRF (MHz) | Mean PRF (MHz) | Delta Length | #Chip Per Symbol | Symbol Duration (ns) | Base Rate Msymbol/s
Channel Number |  | Peak PRF (MHz) | Mean PRF (MHz) |  | #Chip Per Symbol |  | Base Rate Msymbol/s
Channel Number | Code Length | Peak PRF (MHz) | Mean PRF (MHz) | Separation Factor | #Chip Per Symbol | Symbol Duration (ns) | Base Rate Msymbol/s
Channel Number |  | Peak PRF (MHz) | Mean PRF (MHz) |  |  |  | Base Rate Msymbol/s

## Slide 6: Page 456: Equation (change 2 of 3)
From:
To: “For a WPAN using the ternary code indexed by , the SYNC field shall consist of repetitions of the symbol , where consists of the ternary code elements separated by zero chips as depicted in Figure 16-5 and expressed below mathematically:
where denotes the chip index, is the Kronecker delta function, and values of and are given in Table 16-4.”
Comments: Delta function is not used correctly. Just use to denote the spacing between elements. Also, for clarity, the chip index and (the ternary code length) should be explicitly included in the formula.

## Slide 7: Page 457: Figure 16-5 (change 3 of 3)
From: (appears in two places)
To:
Comments: sets the spacing between the sequence elements and is incorrectly used here to denote the length of the sequence. Use to denote the length of sequence.

## Slide 8: Page 458: Figure 16-7
FROM:
TO:
Comments: for consistency with the PPDU encoding process as described in Section 16.2.1 (page 447) and Tables 16-1 and 16-2 (page 448).
Systematic
RS (K+8, K)
Systematic Convolutional Encoder, R = 1/2
PSDU
(rest of the figure is correct)
PHR bits encoded as described in Section 16.2.6
Tail bits

## Slide 9: Page 461: Figure 16-10
FROM:
TO:
Comments: for consistency with the PPDU encoding process as described in Section 16.2.1 (page 447) and Tables 16-1 and 16-2 (page 448).
Systematic
RS (K+8, K)
Systematic Convolutional Encoder, R = 1/2
M bits
(rest of the figure is correct)
PHR bits encoded as described in Section 16.2.6
Tail bits
, …,