## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: LB Resolutions from kivinen
Date Submitted: 15 January, 2019
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: LB Resolutions from kivinen
Abstract:
Here is resolutions to comments assigned to Kivinen.
Purpose: Provide information which kind of changes are needed to the standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
4md LB Resolutions from Kivinen
Tero Kivinen

## Slide 3
CID 64
Comment: This text here says that “appropriate operating mode description IE shall be generated”, but I have not found a list of operating mode IEs that can be used here.
Proposed Change: Create a table here listing different IEs that can be used to deliver the operating modes, especially as some of those are not very well named (for example is “Mode Switch Parameter IE” one of those, most likely not as table 7-19 does not list 6.10 for use?). Checking table 7-19 the list could be O-QPSK PHY Mode IE, LECIM DSSS Operating Mode IE, LESIM FSK Operating Mode IE, RCC PHY Operating Mode IE. There is also TVWS PHY Operating Mode Description IE, which use does not list 6.10, so perhaps it cannot be used here?
Resolution: Revised
Proposed Resolution: Add table as shown in next page, and modify text to say “appropriate operating mode description IE as described in table x-y shall be generated”.

## Slide 4
CID 64, Table x-y

## Slide 5
CID 95
Comment: Paragrah mentions the Frame Type field, Security Enabled field, and Frame Version field, and Frame Pending field, and thens says says "If the Frame Version field is not 0b10, all other fields in the Frame Control field shall be set to zero and ignored on reception." But this is in conflict with the list beginning line 16 which says how the addressing mode filed needs to be set up for frame versions 0b00 to 0b10.
Proposed Change: Not sure, what is the easiest fix, perhaps make the sentence explicit, "If the Frame Version field is not 0b10, fields XXXXX in the Frame Control field shall be set to zero and ignored on reception." where XXXXX is is list of the fields that should be zeroed.
Resolution: Revised
Proposed Resolution: Change text as shown on next page.

## Slide 6
CID 95, cont
The Frame Type field shall contain the value that indicates a Beacon frame, as shown in Table 7-1. The Security Enabled field shall be set to one if security is enabled and the Frame Version field is not zero. If a broadcast frame is pending, the Frame Pending field shall be set to one. If the Frame Version field is not 0b10, all other fields in the Frame Control field shall be set to zero and ignored on reception.
The Sequence Number field shall contain the current value of macBsn if it is a Beacon frame or macEbsn if it is an Enhanced Beacon frame. As a device may be sending both Beacon frames and Enhanced Beacon frames, separate sequence numbers shall be maintained. If sending an Enhanced Beacon frame (Frame Version field is 0b10), the sequence number may be suppressed by setting the Sequence Number Suppression field in the Frame Control field. When the frame version field is 0b00-0b01 the Sequence Number field shall be present.
When the Frame Version field is 0b00-0b01:
The Source Addressing mode field shall be set to indicate that the Source Address and Source PAN ID fields are present.
The Destination Addressing mode field shall be set to indicated that the Destination Address and Destination PAN ID fields are not present.
The Source PAN ID field and Source Address field shall contain macPanId and the address, respectively, of the device transmitting the beacon.
All other fields in the Frame Control field shall be set to zero and ignored on reception.

## Slide 7
CID 209
Comment: There is several tables and hierarchical structures in our PIB, but this MLME-GET does not explain how those structures or values from those structures are accessed.
Proposed Change: Add text explaining how hierarchical structures are accessed using MLME-GET, this also might affect the MLME-GET.confirm as it might need to return.
Resolution: Revise
Proposed Resolution: Add paragraph to Section 8.2.6.1 page 272 end of page: “The MAC PIB contains some hierarchical data structures (for example the TSCH macLinkTable, or security MAC PIBs described in section 9.5), and the PibAttribute parameter needs to be able to address them. i.e., it needs to be possible to get macNodeAddress (Table 8-96) from macLinkTable that matches given macLinkHandle. As and conceptual interface no exact format how PibAttribute is defined.” Also add paragraph to Section 8.2.6.2 page 273 line 13.5 i.e., end of the section: “As MAC PIB contains some hierarchical data structures, it is also possible to provide interface where MLME-GET.confirm returns more complicated structure (for example whole macLinkTable matching given macLinkHandle).”

## Slide 8
CID 210
Comment: There is several tables and hierarchical structures in our PIB, but this MLME-SET does not explain how those structures or values in those structures are written.
Proposed Change: Add text explaining how to write hierarchical structures or values in them.
Resolution: Revise
Proposed Resolution: Add paragraph to Section 8.2.6.3 page 273 end of page: “The MAC PIB contains some hierarchical data structures (for example the TSCH macLinkTable, or security MAC PIBs described in section 9.5), and the PibAttribute parameter needs to be able to address them. For example it needs to be possible to set secExempt (Table 9-14) of secDeviceDescriptor that matches given secExtAddress inside the secDeviceList (Table 9-8). Note, that it is not possible to fetch the whole secDeviceDescriptor and modify it and set it back, as there is read only fields inside the secDeviceDescriptor (secDeviceMinFrameCounter). In some cases there might be need to remove or add elements to hierarchical tables, but no interface is defined in this standard how it is done.”

## Slide 9
CID 223
Comment: The IeStatusList, first mentioned here, is defined as a return parameter from the incoming frame security procedure (in clauses 9.2.3, 9.2.4, 9.2.7 and 9.2.8) but there is no mention of this parameter in any text outside of these clauses to define how it is used outside of clause 9. That is, one would expect it to be mentioned in clause 6.7.2 "Reception and rejection", and perhaps communicated to the upper layers in MLME-COMM-STATUS.
Proposed Change: Define the intended external use of this parameter, in the appropriate place e.g. clause 6.7.2, and if appropriate add parameters to the MLME-COMM-STATUS.indication to report when such issues are encountered.
Resolution: Revised
Proposed Resolution: Change 2nd last paragraph in section 6.7.2 as follows “All IEs received in a valid frame that are marked as PASSED in the IeStatusList by the incoming frame secrity procedure shall be processed by the MAC sub-layer, and if required, passed to the next higher layer. If any of the IEs in a valid frame were marked as FAILED, then those IEs are not passed to next higher layer, or processed by MAC, but MLME shall issue MLME-COMM-STATUS.indication primitive with the Status parameter set to IMPROPER_IE_SECURITY.” In section 8.2.5.2 add IeStatusList to MLME-COMM-STATUS.indication between KeyIndex and Status (line 13.5). Add IeStatusList to table 8-13 after KeyIndex with Type of “List of Status for each IE”, and Valid Range of “PASSED or FAILED for each IE in frame”, and Description “Status of each IE in the frame telling whether they passed or failed the security policy checks as defined in 9.2.7 and 9.2.8.” Add IMPROPER_IE_SECURITY to Valid range of Status in table 8-13. Add new entry between lines 13 and 14 in page 270 saying: “ – IMPROPER_IE_SECURITY – One of the IEs in the frame failed security processing. Note, that the rest of the IEs are passed to upper layer, and IEs which did pass security processing are processed by MAC. This MLME-COMM-STATUS.indication call is done in addition to corresponding confirm (if applicable).”

## Slide 10
CID 229
Comment: Annex C has a number of issues: It is an example only for 2006 frames. Need examples that use v2 frames. The current examples cover beacon frames but not enhanced beacons. It shows a MAC command frame which was not encrypted in v1 frames but is for v2 frames. Need examples with v2 frames including header and payload IE's. Need to include v2 frame types like multipurpose frames.
Proposed Change: Back when Annex C was created, this section was populated by hand. It is strongly recommended that the new examples come from a Wireshark trace since the industry has gravitated towards that and there is good agreement among the current 15.4 chipset vendors.
Resolution: Revised
Proposed Resolution: Two examples of Annex C is kept (C.2.1 and C.2.3). The example C.2.2 using Security Level 4 (which was removed in 2015) is removed. Remove Section C.2.2, Add new sections as specified in CID 224.

## Slide 11
CID 232
Comment: This example uses frame version 0 and 1 MAC frames. The processing rules for frame version 2 MAC frames are different. This should be noted in the beginning of section.
Proposed Change: Add note explaining that this is using old frame format in the example and in this format the MAC command is actually not encrypted, but in the frame format 2 the MAC command byte itself will be encrypted.
Resolution: Revised
Proposed Resolution: Add text as new paragraph to beginning of C.2.3.1 “This example uses frame version 1 MAC Command frames. The processing rules for frame version 2 MAC Commands is different. In the frame version 1 the MAC command (first byte after MHR) is not encrypted, in frame version 2 MAC Command frames everything after MHR is encrypted if security level is > 4.”

## Slide 12
CID 234
Comment: Add new examples for following frames: MAC command frames using frame version 2 with Payload IEs and using security level 7. Enhanced beacon with Payload IEs using security level 3. Data frame with both header IEs and Payload IEs using security level 6. Enhanced ACK using header IEs and security level 5.
Proposed Change: Generate the examples and add them. The examples does not need to have all internal calculations as we have for current examples, it would be enough to have actual frame in hex, and the resulting final packet in hex.
Resolution: Defer
Proposed Resolution: Generate examples as proposed in the Comment.