## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [History and Summary of 802.15.10a]
Date Submitted: [16 January 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [TG10a.]
Abstract: [TG10a Opening Report for the January 2019 Interim Session]
Purpose: [Provide status information, etc. relevant to opening TG10a session at 802.15 meeting]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: History and Summary of 802.15.10a
Problem Statement
PAR, CSD, and TG formation
Initial proposal
Evolution into “route table” formulation
Current status
Some things that a Chair can do wrong

## Slide 3: Problem Statement
15-17-0517-02-0mag-802-15-10-non-storing-cor (all related to non-storing)
  E2E acknowledgement from mesh root
  P2P routing using a combination of up/down routing
  On-demand P2P routing for E2E acknowledgement
  On-demand path storing when sending unicast

## Slide 4: PAR, CSD, and TG formation
PAR: dcn 15-17-0565-01-0000
CSD: dcn 15-17-0566-01-0000
First meeting in January 2018
Chair: Charlie Perkins
Vice Chair: Jörg Robert

## Slide 5: Problem: non-storing P2P (Up  Down)
MAC
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.ind can’t issue a data frame
From S to D
DATA.req from R cannot send a frame as if S is source. It just a sends a frame from R to D.
S
..hops..
R(root)
D
NHL
Solution I: Let L2R have a record of the paths. Insert text specifying that the record is attached when a data is sent.
Solution II: Add a new primitive to indicate the event (up  down) and add a new primitive to send a frame so that it keeps its source address as the originator not mesh root.
S
D
A
B
R
..hops..

## Slide 6: Problem: non-storing E2E Ack
MAC
MMI
L2R
NHL
MAC
MMI
L2R
MAC
MMI
L2R
NHL
DATA.req from R cannot send a L2R Ack frame
D
..hops..
R
S
NHL
Solution I: Let L2R have a record of the paths. Insert text specifying that the record is attached when a data is sent.
Solution II: Add a new parameter to the DATA.indication primitive, to indicate L2R ack request. Add another to send a frame as if its source address were the originator, not themesh root.
S
D
A
B
R
..hops..
Sending Acknowledgment should be done by L2R layer (e.g. handling timeout)

## Slide 7: Initial proposal: storing more path lists
Add an entry to the mesh table 5-1 (MT)
  Path List
    Consists of ‘Destination Address’ and ‘Address List’ pair
    Enabled only when non-storing mode
Add new specification after the following text in 5.2.4.2
  When the mesh root receives the RA IE or the SRA IE, it delivers the path and the source address therein to the next higher layer with the L2LME-INTERMEDIATE-ADDR-LIST.indication primitive, and stores them as the pair of the address list and the destination address into the ‘Path List’ in the MT.
Add to IntermediateAddrList description of L2RDATA.request (7.2.1.1):
  Addresses to be inserted in the Intermediate Address List of the L2R Routing IE. When IntermediateAddrList is ‘NULL’, the ‘Address List’ in the ‘Path List’ in the MT is used, where the destination address matches to the one in this primitive. Omitted if source routing is not used.
No format change. No change of protocol between devices S, D, R.

## Slide 8: Evolved proposal: storing more routes
Change the P2P path list in the mesh table 5-1 (MT) to be a Route Table
    Type: Reachable destination information
    Description: Information needed to route a frame to each reachable destination
Add new specification after the following text in 5.2.4.2
  When the mesh root receives the RA IE or the SRA IE, it delivers the path and the source address therein to the next higher layer with the L2LME-INTERMEDIATE-ADDR-LIST.indication primitive., and stores them as the pair of the address list and the destination address into the ‘Route Table’ in the MT (Table 5-1)..
Add to IntermediateAddrList description of L2RDATA.request (7.2.1.1):
  Addresses to be inserted in the IntermediateAddressList of the L2R Routing IE. When IntermediateAddrList is ‘NULL’, the ‘Address List’ in the Route Table in the MT is used, where the destination address matches to the one in this primitive. Omitted if source routing is not used.
Change all instances of path list to route entry (address list)
No format change. No change of protocol between devices S, D, R.

## Slide 9: Other corrections
Corrected arithmetic in mesh examples
Corrected equation for Expected Airtime metric
l2rBCSecurityLevel  l2rBCSecSecurityLevel

## Slide 10: Schedule
Slide 10
TASK | Start | Completed
TG10a | Jan, 2018 | May, 2018
Problem Statement | Jan, 2018 | Jan, 2018
Agree on solution approach | Jan, 2018 | May, 2018
Draft | May, 2018 | May, 2018
TG Comment Collection | May, 2018 | July, 2018
WG Letter Ballot | July, 2018 | Sept, 2018
WG Recirculation Ballot | Sept 11, 2018 | Sept 27, 2018
BRC Conference Call | Oct 3, 2018 | Oct 3, 2018
Notes: January 19
Page 10

## Slide 11: Schedule, continued
Slide 11
TASK | Start | Completed
EC Approval for Sponsor Ballot | Oct, 2018 | Oct, 2018
Sponsor Ballot | Oct, 2018 | Nov, 2018
Resolve Sponsor Ballot Comments | Nov, 2018 | Nov, 2018
Sponsor Ballot Recirculation | Nov, 2018 | Dec, 2018
RevCom / IEEE SASB Approval | Jan 19, 2019 | March 21, 2019
IEEE-SA Publication | May, 2019 | July, 2019
Notes: January 19
Page 11

## Slide 12: Sponsor Ballot finals, Revcom submission
BRC December 19 meeting results
  Minutes available: DCN 15-18-0620-01-010a
Draft submitted for RevCom Jan. 19 mtg
VOTERS | 75
VOTED | 64
YES | 58
ABSTAIN | 6
NO | 0
% VOTERS | 85%
% YES | 100%
% ABSTAIN | 9%

## Slide 13: What can possibly go wrong?
Not make a BRC, even if you don’t think it’s needed. It’s always needed.
Not pay close attention to the IEEE Style Guide
Not use the IEEE Add-Ins
Put the draft document on mentor
Submit .doc for Letter Ballot (use .pdf)
What can go wrong? Everything!

## Slide 14: About 802.15.10
Designed to handle thousands of devices, with topology discovery, mesh maintenance, address management, multiple metrics, and features for more robust routing
DCN 15-17-205-00-0010 has a good description of the overall protocol