## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Secure Ranging Definitions and Interoperability]
Date Submitted: [16 January 2019]
Source: Dr. Boris Danev [3db Access, Switzerland],
Prof. Dr. Srdjan Capkun [ETH Zurich, Switzerland]
Re: [Changes proposal for the LRP/HRP UWB PHY]
Abstract: [Contribute to a proposal to the enhanced impulse radio group w.r.t. 4z Security ]
Purpose: [Discussion, current 4z LRP/HRP Security, definitions, questions, interoperability]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Scope
Discussion on LRP/HRP Security including Security Definitions & Interoperability
Motivation
Provide status on defining security for SRDevs and discuss IEEE standard compliance and interoperability

## Slide 3: Agenda
Introduction of Security Definitions
Current Status and Questions
Standard Compliance and Interoperability

## Slide 4: Security Definitions
  Security Verification
    Procedures of verification of ranging sessions to ensure secure ranging transaction
    PHY layer and MAC layer (Clause 9)
Security Levels
  Definition of SRDev Security Levels with respect to entropy bits of security (as mandated by IEEE standards)
Security Proofs
  Definition of threat model for analysis
  Resistance to known attacks such as Cicada, Early/Detect & Late Commit, Preamble Injection, Guess-and-Compensate, First path injection, etc.
  Investigation of new attacks (if appropriate)

## Slide 5: Current Status and Questions (1/2)
 | 4z LRP SRDev | 4z HRP SRDev
Security Verification |  | 
PHY layer | - Distance Bounding approach - Defined in the contributions - Being integrated and refined in Clause 6 MAC Func Description | - How is the threshold defined for secure timestamp? - What is the procedure to qualify as secure timestamp?
MAC layer | - Complies to Clause 9 (Security) - Verification is defined in Clause 9 | - How is the secure exchange of the timestamps planed? - Would an exchange procedure be defined?
Security Levels |  | 
IEEE 802.15.4 | - IEEE Security Level 1 (32 bits) - IEEE Security Level 2 (64 bits) - IEEE Security Level 3 (128 bits) - Other SLs are possible | - What Security Levels can be achieved (bit-equivalent entropy)? - What are the RX implementation details to ensure security and Security Levels?
Security Proofs | Next slide | Next slide

## Slide 6: Current Status and Questions (2/2)
 | 4z LRP | 4z HRP
Security Proofs |  | 
 | - Thread model of Distance Bounding (well defined in security literature) - Resilience to all known PHY & MAC layer attacks is proven in Annex G | - What is the threat model? STS concept is not documented in open security literature - What is the resilience of proposed scheme with respect to known PHY, TIMESTAMP & MAC attacks? - Are their more attacks? - Does a security analysis exist?

## Slide 7: Standard Compliance & Interoperability
Standard compliance
  Ensure precise security definitions for threat analysis
  E.g., IEEE 802.11az Secure Ranging
    11-17-1122-00-00az-cp-replay-threat-model-for-11az.docx
Interoperability
  Precisely defined security is a must for interoperability between vendors
  Precisely defined security is a must for application-level standards (e.g., ISO/ECMA)

## Slide 8: Summary and Conclusions
  Security definitions need to be carefully elaborated for standard compliance and interoperability
  Preliminary analysis of STS-based schemes raise security concerns