## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4 Profile for IETF SCHC]
Date Submitted: [17 January 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [TG10a.]
Abstract: [How to use SCHC with 802.15.4]
Purpose: [Develop document text for IETF [lpwan] submission]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SCHC – Static Context Header Compression
Static Context:
  Topology
  Application (i.e., kind of traffic)
  Packets always delivered in order
Fragmentation modes
  Never Ack
  Always Ack
  Ack on Error

## Slide 3: SCHC Fragment Header sizes
RuleID: two or three bits minimum
Dtag: can be zero
W: at least one bit if windows are used
FCN: probably at least two bits
Let’s say one byte.
Plus, MIC

## Slide 4: Comparing Fragmentation
For SCHC, overhead is ~1 byte / fragment plus MIC
For 802.15.4 …?

## Slide 5: Minimal 802.15.4 frame format
General frame format defined in 7.2
3 bits for Frame type
0 bits for PAN IDs, Source/Dst Address
0 bits for IEs
2/4 bytes for FCS

## Slide 6: 802.15.4 Fragment overhead
802.15.4 only defines for LECIM
All fragments are acknowledged
FCSD IE required prior to fragments
Fragment header is 2 bytes
FICS on every fragment – 2 or 4 bytes
This seems to always be substantially more overhead than SCHC

## Slide 7: Goal 1: Optional SCHC MIC
No need to have FCS and MIC on every reassembled frame, may well be identical
Can ask as individual, but would be likely be better to also have validation from the SC IETF composed of 802.15 experts

## Slide 8: Possibility for a new Frame Type
Frame type 0b’100’ is “Reserved”
Frame type 0b’111’ is “Extended”
If a new frame type is possible, the next bits could be the SCHC header
RuleID, DTAG, W, …

## Slide 9: Questions
This slide was added after presentations
Does IETF SCHC “assume” PHY frame check? If not, then problems with false positive
How to minimize 802.15.4 MAC header overhead?
Should the document be only for 15.4w?
Extended frame type?