## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4 Profile for IETF SCHC]
Date Submitted: [17 March 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [SC IETF topic for SCHC header compression]
Abstract: [Discussion about ways to use SCHC with 802.15.4]
Purpose: [Develop document text for IETF [lpwan] submission]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SCHC – Static Context Header Compression
Static Context:
  Topology
  Application (i.e., kind of traffic)
  Packets always delivered in order
Fragmentation modes
  Never Ack
  Always Ack
  Ack on Error

## Slide 3: SCHC Fragment Header sizes
RuleID: two or three bits minimum
Dtag: can be zero
W: at least one bit if windows are used
FCN: probably at least two bits
Let’s say one byte.
Plus, MIC

## Slide 4: Comparing Fragmentation
For SCHC, fragmentation overhead is:
  ~1 byte / fragment
  + SCHC MIC
  Request SC IETF to recommend Profile setting MIC=0, since 802.15.4 *will* check
  + 802.15.4 header per fragment (5-7 bytes)
  How much can we compress MHR?

## Slide 5: Goal 1: Optional SCHC MIC
No need to have FCS and MIC on every reassembled frame, may well be identical
Can ask as individual, but would be likely be better to also have validation from the SC IETF composed of 802.15 experts

## Slide 6: Frame Composition
Slide 6
Figure 4a
Figure 3
Figure 4b
IEEE
802
.
15
.
4
MAC frame
2
1
2
Variable
0
Frame
Control
Sequence
Number
Addressing Fields
Auxiliary Security
Header
(
optional
)
0
/
1
Octets
:
2
Header
IEs
Payload
IEs
Variable
Variable
Data Payload
Variable
MIC
0
/
4
/
8
/
16
FCS
2
/
4
4
1
4
1
2
0
2
0
/
2
Dest
PAN ID
2
MHR
MAC Payload
MFR
1
0
/
4
0
/
1
/
5
/
9
Security
Control
Frame
Counter
Key
Identifier
0
/
2
/
8
0
/
2
/
8
0
/
2
Source
Addr
Dest
Addr
Source
PAN ID
Max Frame Size
-
?all other fields
Transaction
Control
EtherType
/
Dispatch
MPX ID
2
2
1
802
.
15
.
12
Payload
Variable
5
ULI
-
6
lo ID
2
IPHC
2
/
7
1
802
.
15
.
12
NHC
6
LoWPAN
Payload IE
Payload
Variable
Variable
Using IEs to convey higher layer data
IEEE
802
.
15
.
4
MAC frame
2
1
2
0
0
Frame
Control
Sequence
Number
Addressing Fields
Auxiliary Security
Header
(
optional
)
0
/
1
Octets
:
2
Data Payload
Variable
MIC
0
/
4
/
8
/
16
FCS
2
/
4
4
1
4
1
2
0
2
0
/
2
Dest
PAN ID
2
MHR
MAC Payload
MFR
1
0
/
4
0
/
1
/
5
/
9
Security
Control
Frame
Counter
Key
Identifier
0
/
2
/
8
0
/
2
/
8
0
/
2
Source
Addr
Dest
Addr
Source
PAN ID
6
LoWPAN
Header
4
Max Frame Size
-
?all other fields
4
EtherType
/
Dispatch
ULI header
2
2
IPHC
2
/
7
1
802
.
15
.
12
NHC
6
LoWPAN
MAC Payload
4
3
ULI Header
3
/
8
3
Using Data Payload to convey higher layer data
3
2
Payload IE
Layers
5
-
7
Layers
5
-
7
L
3
Header
Variable
Variable
Layer
3
L
4
Header
Variable
Layer
4
Notes: March 19
Page 6

## Slide 7: 802.15.4 Fragmentation overhead
802.15.4 only defines for LECIM
FCSD IE required prior to fragments (4)
Fragment acknowledge – Table 23-4
Fragment header (2)
FICS on every fragment – (2) or (4)
===============================
This seems to always be substantially more overhead than SCHC

## Slide 8: Minimal 802.15.4 frame format
General frame format defined in 7.2
3 bits for Frame type
0 bits for PAN IDs, Source/Dst Address
0 bits for IEs
2/4 bytes for FCS

## Slide 9: Frame type values
Frame type value | Description
b2 b1 b0 | 
'000 | Beacon
'001 | Data
'010 | Acknowledgment
'011 | MAC command
'100 | Reserved
'101 | Multipurpose
'110 | Fragment or Frak
'111 | Extended
The Fragment and Frak formats are defined in 23.3.3 and | 
23.3.6.2, respectively. | 

## Slide 10: Possibility for a new Frame Type
Frame type 0b’100’ is “Reserved”
Frame type 0b’111’ is “Extended”
If a new frame type is possible, the next bits could be the SCHC header
RuleID, DTAG, W, …

## Slide 11: Questions
How to minimize 802.15.4 MAC header overhead?
Should the document be only for 15.4w?
Should we consider specifying an extended frame type?