## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4 Profile for IETF SCHC]
Date Submitted: [15 May 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [SC IETF topic for SCHC header compression]
Abstract: [Discussion about ways to use SCHC with 802.15.4]
Purpose: [Develop document text for IETF [lpwan] submission]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SCHC – Static Context Header Compression
Static Context:
  Topology [static endpoints over one hop]
  Application (i.e., kind of traffic)
  Packets always delivered in order
Fragmentation modes
  Never Ack
  Always Ack
  Ack on Error

## Slide 3: SCHC versus 802.15.4 fragmentation
Need to determine whether or not to specify fragmentation parameters for the IETF [lpwan] document for 802.15.4
Every SCHC fragment needs an 802.15.4 header
But 802.15.4 fragmentation mandates some things that SCHC can do without

## Slide 4: SCHC Fragment Header sizes
At last IETF, I heard agreement to rename the SCHC MIC, and that it *could* be 0 bytes, since 802.15.4 *will* check
So, perhaps one byte, minimum, as follows:
RuleID: two or three bits minimum
Dtag: can be zero
W: at least one bit if windows are used
FCN: probably at least two bits

## Slide 5: Comparing Fragmentation
For SCHC, fragmentation overhead is:
~1 byte / fragment (+ 0 for SCHC MIC )
+ 802.15.4 header per fragment
  (4-6 bytes ?) [see next page]
  How much can we compress MAC header?

## Slide 6: Compressing 802.15.4 MAC header
Slide 6
IEEE
802
.
15
.
4
MAC frame
Frame
Control
Sequence
Number
Addressing Fields
Auxiliary Security
Header
(
optional
)
0
/
1
Octets
:
2
Header
IEs
Payload
IEs
Variable
Variable
Data Payload
Variable
MIC
0
/
4
/
8
/
16
FCS
2
/
4
0
/
2
Dest
PAN ID
MHR
MAC Payload
MFR
1
0
/
4
0
/
1
/
5
/
9
Security
Control
Frame
Counter
Key
Identifier
0
/
2
/
8
0
/
2
/
8
0
/
2
Source
Addr
Dest
Addr
Source
PAN ID
Minimal 802.15.4 header
  2 bytes Frame Control
  0 byte Auxiliary Security Header
  2-4 bytes FCS
So, minimum size = 4-6 bytes … ? Call it min
So, SCHC fragmentation overhead = 5-7 bytes
Notes: May 19
Page 6

## Slide 7: 802.15.4 LECIM Fragmentation overhead
Let n = # of fragments, min as on last page
FCSD IE needed first: (4+min)/n
Fragment acknowledge – Table 23-4
  At least one Frak is required  (4+min)/n
Fragment header (2)
FICS on every fragment – (2) or (4)
More overhead than SCHC, but not catastrophic, depending on n

## Slide 8: Frame types (15.4-2015, Table 7-1)
b2 b1 b0 | Description
000 | Beacon
001 | Data
010 | Acknowledgment
011 | MAC command
100 | Reserved
101 | Multipurpose
110 | Fragment or Frak
111 | Extended
The Fragment and Frak formats are defined in 23.3.3 and 23.3.6.2, respectively. | 

## Slide 9: Possibility for a new Frame Type
Frame type 0b’100’ is “Reserved”
Frame type 0b’111’ is “Extended”
Frame type 0b’110’ is “Interesting”
If a new frame type is possible, the next bits could be the SCHC header
RuleID, DTAG, W, …

## Slide 10: Hypothetical 802.15.4 new frame type
General frame format defined in 7.2
3 bits for Frame type
0 bits for PAN IDs, Source/Dst Address
0 bits for IEs
2/4 bytes for FCS
  Less overhead than SCHC, but way more intrusive design-wise

## Slide 11: Questions
How to minimize 802.15.4 MAC header overhead?
Is 16-bit FCS in common use?
Should we specify an extended frame type?
Does SCHC require security? How shall we compare 802.15.4 security versus SCHC security?
SCHC MIC is a CRC checksum and not secure. Should not call it MIC. But SCHC doesn’t emit “frames”, so it shouldn’t be FCS. What to call it?

## Slide 12: Observations
I believe that SC IETF decided that the IETF [lpwan] document should be for all of 15.4
802.15.4 MIC is cryptographically secure and typically is done on-chip
Probably need separate SCHC profiles depending on the fragmentation mode