## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [HRP UWB PHY CCA mode 5 text]
Date Submitted: [8th March 2019]
Source: [Billy Verso] Company [Decawave Ltd.]
Address [Peter Street, Dublin 8, Ireland]
Voice:[+353.87.233.7323], E-Mail:[billy.verso (at) decawave.com]
Re: [Proposed enhancements to the HRP UWB PHY]
Abstract: [Proposal to correct issues with the current CCA mode 5 text]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Background:
The author submitted a comment in LB150 on the 802.15.4 revision project, asking TG4md to correct the text pertaining to the HRP UWB PHY CCA Mode 5
Not being UWB experts and noting that the TG4z group with many UWB experts is active working on amending UWB, the TG4md CRG decided to refer this to TG4z to make the appropriate correction in the 4z amendment
This submission is describing the issue and the proposed resolution, and asking TG4z to review this and agree and include the appropriate remedy in the 802.15.4z draft

## Slide 3: Current CCA mode 5 text
In IEEE Std 802.15.4™-2015
  Clause 10.2.7 Clear channel assessment (CCA)
It says:
    — CCA Mode 5: HRP UWB preamble sense based on the SHR of a frame. CCA shall report a busy medium upon detection of a preamble symbol as specified in 16.2.5. An idle channel shall be reported if no preamble symbol is detected up to a period not shorter than the maximum packet duration plus the maximum period for acknowledgment.

## Slide 4: Issues with the current CCA mode 5 text
  First sentence needs to be clearer in terms of what preamble symbol is detected.
  Second sentence is not at all clear in meaning.
  Just saying “maximum packet duration” is questionable. It is unreasonable to make the medium be reported as busy for an appreciable length of time, especially where the shorter frames are being used. There is a large variation in the possible frame length in UWB depending on the data rate, e.g. at 110 kbps with 4096 PSR a frame and its ACK would be almost 20 ms long while at 6.81 Mbps with a 64 PSR preamble this is < 375.5 µs, which over 50 times shorter. (A typical 1023 octet 4z frame at 27 Mb/s is ~ 330 µs)
  In a typical UWB PHY implementation preamble detection is based on a period of correlation not just a single symbol, i.e. depending on the operating mode may be 8 to 200 symbol times (the longer times being used where a longer preamble sequence is expected). This should be reflected in the text.

## Slide 5: Proposed text to revise CCA mode 5:
  In 10.2.7 replace the text for dash list entry “CCA Mode 5:” with the following:
    — CCA Mode 5: HRP UWB preamble sense based on the SHR of a frame. In this mode, the CCA shall operate to detect the UWB preamble as specified in 16.2.5 and selected by the phyCurrentCode. The device shall spend at least its normal operational preamble detection time looking for this preamble before reporting an idle medium in the case where no preamble is detected. In the case where the preamble is detected, the CCA shall report a busy medium, and thereafter, shall not report an idle medium until a period has elapsed that is not shorter than time required at the current network operational data rate and PSR, (e.g. as specified by the DataRate and UwbPreambleSymbolRepetitions parameters of the MCPS-DATA.request), to complete the transmission of a frame of 127 octets, or 1023 octets for the HRP-SRDEV in the HPRF mode, and to receive its acknowledgment.

## Slide 6: Discussion / Action:
The author recommends including the proposed text in the P802.15.4z draft, and asks TG4z to:
  Review the proposed revised CCA Mode 5 text
  Make any changes necessary
    A revised submission will be uploaded if changes are made
  Agree its inclusion in the draft

## Slide 7
THE END