## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed Resolution for comment CID 1035]
Date Submitted: [12 March, 2019]
Source: [Chris Hett, Ruben Salazar] Company [Landis+Gyr]
Address: [30000 mill creek avenue Alpharetta GA USA]
Voice: [], E-Mail: [chris.hett@landisgyr.com, ruben.Salazar@landisgyr.com]
Re: [Comment resolution for 802.15.4md REV]
Abstract: [This contribution proposes a resolution for comment CID1035 of the current ballot]
Purpose: [Discussion and Approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 1035
8.2.19.1 | 15 | There needs to be a way to identify which configured slotframes and links should be advertised in Enhanced Beacons. | Add a boolean parameter to the MLME-SET-SLOTFRAME.request primitive. It could be named “advertise”, “publicize”, etc. If true, then the slotframe and all its links represent network-wide information applicable to all devices, and should be added to the TSCH Slotframe and Link IE. If false, it would not be added.
Proposed Resolution: Revise

## Slide 3: Revised text - 1
Section 8.2.19.1 – MLME-SET-SLOTFRAME.request
Add parameter called ‘Advertise’ to the primitive:
MLME-SET-SLOTFRAME.request (
SlotframeHandle,
Operation,
Size,
Advertise
)

## Slide 4: Revised text - 2
Name | Type | Valid range | Description
Advertise | Boolean | TRUE, FALSE | If TRUE, this Slotframe should be advertised in Enhanced Beacon frames using the “TSCH Slotframe and Link IE.” If FALSE, this Slotframe should be added locally only.
Add entry in table 8-45 – MLME-SET-SLOTFRAME.request parameters:

## Slide 5: Revised text - 3
Attribute | Type | Range | Description | Default
macSlotframeAdvertise | Boolean | TRUE, FALSE | If TRUE, this Slotframe should be advertised in Enhanced Beacon frames using the “TSCH Slotframe and Link IE.” If FALSE, this Slotframe should be added locally only. | -
Add entry in table 8-95 – TSCH MAC PIB attributes for macSlotframeTable:

## Slide 6: Revised text - 4
Add parameter called ‘Advertise’ to the primitive
MLME-SET-LINK.request (
Operation,
LinkHandle,
SlotframeHandle,
Timeslot,
ChannelOffset,
TxLink,
RxLink,
SharedLink,
TimekeepingLink,
PriorityLink,
LinkType,
NodeAddrMode,
NodeAddr,
Advertise
)

## Slide 7: Revised text - 5
Name | Type | Valid range | Description
Advertise | Boolean | TRUE, FALSE | If TRUE, this Link should be advertised in Enhanced Beacon frames using the “TSCH Slotframe and Link IE.” If FALSE, this Link should be added locally only.
Add entry in Table 8-47 – MLME-SET-LINK.request parameters:

## Slide 8: Revised text - 6
Attribute | Type | Range | Description | Default
macLinkAdvertise | Boolean | TRUE, FALSE | If TRUE, this Link should be advertised in Enhanced Beacon frames using the “TSCH Slotframe and Link IE.” If FALSE, this Link should be added locally only. | -
Add entry in table 8-96 – TSCH MAC PIB attributes for macLinkTable: