## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed resolution for CID#222]
Date Submitted: [12 March, 2019]
Source: [Hidetoshi Yokota, Shoichi Kitazawa] Company [Landis&Gyr, Muroran IT]
Address: [Tokyo Japan, Hokkaido Japan]
Voice: [], E-Mail: [hidetoshi.yokota@landisgyr.com, kitazawa@ieee.org]
Re: []
Abstract: [This contribution proposes additional descriptions and SRM specific MAC PIB attributes as a resolution for CID#222]
Purpose: [Discussion and Approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments on SRM specific MAC PIB (Table 8-106 on p.399)
CID | Clause | Comment | Proposed change
222 | 8.4.2.9 | Why is there macChannelPage, macChannelNumber, macRxAddrMode and macRxDeviceAddress in this PIB table. What is this table used for? I assumed this was global table used to measure global metrics, but it seems it is not. | Clarify the role of this table.

## Slide 3: Proposed resolution (1)
Add the following sentence at the end of l.4 of p.399:
8.4.2.9 SRM specific MAC PIB attributes
Table 8-106 contains the PIB values for SRM. The stored attributes are a snapshot of the last or ongoing measurement, which can be referred to by the upper layer. The usages of these attributes are described in Section 6.17.

## Slide 4: Proposed resolution (2)
Attribute | Type | Range | Description
macStartTime | Integer | 0x00–0xff | The remaining time to start the next measurement that can be referred to by the upper layer. If this value is zero, the requested measurement has been started or finished.
macDuration | Integer | 0x0000-0xffff | The remaining duration of the next or on going measurement that can be referred to by the upper layer. If this value is zero, the requested measurement has been finished.
Table 8-106 --- SRM specific MAC PIB attributes
Add the following items after macRxDeviceAddress in Table 8-106 (the entire table is not shown)