## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Rogue Resolutions from kivinen
Date Submitted: 12 March, 2019
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: LB Resolutions from kivinen to rogue comments
Abstract:
Here is resolutions to comments assigned to Kivinen.
Purpose: Provide information which kind of changes are needed to the standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
4md LB Resolutions from Kivinen to rogue comments
Tero Kivinen

## Slide 3
CID 1040
Comment: Section 6.7.3 describes the purpose of the macAutoRequest* PIB attributes, and indicates that they only apply to transmitting “internally-generated” Data Request command frames. In section 9.2.1 it looks like they apply to all internally-generated frames. Also, there is no way to specify the security parameters to use for Enhanced Beacons; jupiterMesh requires Enhanced beacons to secured at level 2.
Proposed resolution: ... Otherwise, for internally-generated frames, the security depends on the type of frame.
    If the frame is a Data Request command , the inputs are as folows:
    — SecurityLevel shall be set to secAutoRequestSecurityLevel
    — KeyIdMode shall be set to secAutoRequestKeyIdMode
    — KeySource shall be set to secAutoRequestKeySource
    — KeyIndex shall be set to secAutoRequestKeyIndex
    If the frame is an Enhanced Beacon, the inputs are as folows:
    — SecurityLevel shall be set to secEnhancedBeaconSecurityLevel
    — KeyIdMode shall be set to secEnhancedBeaconKeyIdMode
    — KeySource shall be set to secEnhancedBeaconKeySource
    — KeyIndex shall be set to secEnhancedBeaconKeyIndex
    For other frames (e.g. Acknowlegements), the inputs are as folows:
    — SecurityLevel shall be set to 0

## Slide 4
CID 1040 Background
In section 9.2.1 we have text saying:
  If the frame was generated in response to an MLME or MCPS primitive, then the value of SecurityLevel, KeyIdMode, KeySource and KeyIndex are set to the corresponding values of the primitive parameters
The MLME-START.request has Beacon* and CoordRealign* and Beacon* for security levels.
So based on the existing text we already have separate security level, key id mode, key source and key index for beacons and coordinator realignment, so no new feature is needed.

## Slide 5
CID 1040 Resolution
Add text in 9.2.1 saying: MLME-START.request primitive gives SecurityLevel, KeyIdMode, KeySource and KeyIndex for Beacon frames and Coordinator Realignment commands.

## Slide 6
CID 1045
Comment: Add 4 PIB attributes to table 9-8 to specify security to use for Enhanced Beacons.
Proposed resolution:
    secEnhancedBeaconSecurityLevel, Integer, As defined in Table 9-6, The security level used when transmitting Enhanced Beacons., 0x00
    secEnhancedBeaconKeyIdMode, Integer, As defined in Table 9-10, The key identifier mode used when transmitting Enhanced Beacons. This attribute is invalid if the secEnhancedBeaconSecurityLevel attribute is set to 0x00., 0x00
    secEnhancedBeaconKeySource, As specified by the secEnhancedBeaconKeyIdMode parameter, —, The originator of the key used when transmitting Enhanced Beacons. This attribute is invalid if the secEnhancedBeaconKeyIdMode element is invalid or set to 0x00 or 0x01., —
    secEnhancedBeaconKeyIndex, Integer, 0x01–0xff, The index of the key used when transmitting Enhanced Beacons. This attribute is invalid if the secEnhancedBeaconKeyIdMode attribute is invalid or set to 0x00., —

## Slide 7
CID 1045 Resolution
Those PIB values should be added to table 8-92, as that contains other values from the MLME-START.request primitive.
Add following entries to table 8-92 (see next page):

## Slide 8
CID 1045 Resolution
macCoordRealignSecurityLevel | Integer | 0x00-0x07 | The security level to be used for Coordinator Realignment commands, as described in Table 9-6.
macCoordRealignKeyIdMode | Integer | 0x00-0x03 | The mode used to identify the key to be used, as described in 9.4.1.2. This parameter is ignored if the macCoordRealignSecurityLevel parameter is set to 0x00.
macCoordRealignKeySource | Set of octets | As specified by the macCoordRealignKeyIdMode parameter | The originator of the key to be used, as described in 9.4.3.1. This parameter is ignored if the macCoordRealignKeyIdMode parameter is ignored or is set to 0x00 or 0x01.
macCoordRealignKeyIndex | Integer | 0x01-0xff | The index of the key to be used, as described in 9.4.3.2. This parameter is ignored if the macCoordRealignKeyIdMode parameter is ignored or is set to 0x00.
macBeaconSecurityLevel | Integer | 0x00-0x07 | The security level to be used for beacon frames, as described in Table 9-6.
macBeaconKeyIdMode | Integer | 0x00-0x03 | The mode used to identify the key to be used, as described in 9.4.1.2. This parameter is ignored if the macBeaconSecurityLevel parameter is set to 0x00.
macBeaconKeySource | Set of octets | As specified by the macBeaconKeyIdMode parameter | The originator of the key to be used, as described in 9.4.3.1. This parameter is ignored if the macBeaconKeyIdMode parameter is ignored or is set to 0x00 or 0x01.
macBeaconKeyIndex | Integer | 0x01-0xff | The index of the key to be used, as described in 9.4.3.2. This parameter is ignored if the macBeaconKeyIdMode parameter is ignored or is set to 0x00.

## Slide 9
CID 1041
Comment: Thread 1.2 Requires that the status of Frame Pending is reported up in every MCPS-DATA.Confirm on an informative basis so that a SED is more aware of when there is data available for it and when it would be worthwhile to perform another MLME-POLL.Request. This also requires that the coordinator calculates the value of the Frame Pending bit on the reception of every data frame, not just Mac Command Data Request
Proposed resolution: Add a Frame Pending parameter to the MCPS-DATA.Confirm. Allow the coordinator to set the Frame Pending field of the Ack to a data frame to 1 if it can determine that there is data pending for the destination.

## Slide 10
CID 1041 Background
The section 7.3.3 says:
  If the Ack frame is being sent in response to a received Data Request command the Frame Pending field shall be set as indicated in 6.7.3.
  If the Ack frame is being sent in response to either a Data frame or another type of MAC command, the device shall set the Frame Pending field to zero.
This would mean that no other Ack frame can have Frame Pending bit set except the Data Request MAC Command.
On the other hand 6.12.1 has example in Figure 6-62 which sets Frame Pending bit on the Ack of the Data frame.

## Slide 11
CID 1041 Resolution
Add text in section 7.3.3:
  If the Ack frame is being sent in response to a received Data frame as explained in 6.12.1 the Frame Pending field is set as indicated there.
Add FramePending to MCPS-DATA.confirm with type of Boolean, and description of:
  The Frame Pending field value from the incoming Ack frame.

## Slide 12
CID 1048
Comment: In IEEE:802.15.4-2006, the unique device flag in a device descriptor could be set to always use a certain DeviceDescriptor to unsecure an incoming frame. Thread used this to create a 'filtering' key that any Thread device could use to send a frame using Key Id Mode 2 security, and any non-thread devices would filter it out due to not having the required security information. As the device table structure has changed significantly since then, this is no longer natively possible.
Proposed resolution: Add the 'Unique' Flag back to the secKeyIdLookupDescriptor and use the secKeyDeviceAddress to locate the required secDeviceDescriptor in the following stage if the unique flag is set

## Slide 13
CID 1048 Background
All keys using KeyIdMode 2 in 802.15.4-2015 are group keys and are not tied to any specific device. The secKeyIdLookupDescriptor table 9-9 uses only the secKeySource and secKeyIndex for KeyIdMode 2 and 3 as specified in the 9.2.2 KeyDescriptor lookup procedure. The step c) does the KeyIdMode 2 and 3 processing and does NOT use the addressing fields of the original frame, it only uses the secKeySource from the secKeyIdLookupDescriptor table and KeySource from the auxiliary security header.
Note that secDeviceDescriptor is not used at all while locating the secKeyIdLookupDescriptor or secKeyDescriptor. Keys are completely separated from the devices. Only the KeyIdMode 0 uses source address from frame and matches them against secKeyDevice* fields in secKeyIdLookupDescriptor.
See 15-15-0106-07-0mag-security-section-pictures for better picture of how security tables work.

## Slide 14
CID 1048 Resolution
Resolution: Rejected
The proposed change is not needed as all KeyIdMode 2 and 3 keys are already group keys in 802.15.4.